## Slide 1: Calibration and Validation Activities at NOAA/NESDIS
Michael P. Weinreb
CEOS WG on Cal/Val
Feb. 12-14, 2003

## Slide 2: Review of Cal & Val Activities at NOAA/NESDIS
Assure Functionality of Current/Near-Future Operational Systems
  Develop & maintain on-orbit calibration approach, algorithms, & databases
  Oversee pre-launch sensor calibration
  Perform post-launch checkout, monitoring, and trouble-shooting
Apply Experience to Design of Future systems
  Define future measurement requirements & support development of future systems (NPP, NPOESS, GOES-R)
Assure Required Accuracy, Stability, Inter-comparability
  Perform vicarious calibrations and sensor inter-calibrations
  Incorporate national calibration standards
  Validate products

## Slide 3: What’s New in the Past 9 Months?
NOAA-17 Launch and On-Orbit Verification
Planning for Unified System for Monitoring On-Orbit Sensor Performance
V & V Plan for METOP/NOAA-N,N’
Workshop on Satellite Instrument Calibration for Measuring Global climate change
Cal/Val Plans for NPP and NPOESS
Notes: NOAA-N in 2004
METOP1 in late 2005

## Slide 4: N-17 Post-Launch Checkout by NOAA/NESDIS
NASA On-Orbit Verification (OV)
    during 1st 45 days after launch
    primarily tests spec compliance
Resumption of participation by NOAA/NESDIS,
Our objective: Test compliance with users’ scientific requirements
  Test planning, data analysis, reporting/documentation combined with NASA OV’s
  Limited to payload radiometry & geolocation (AVHRR, AMSU, HIRS, and SBUV/2)
  Two categories of test supplements
    Enhancement of NASA OV tests
    New tests
Notes: NOAA-17 in 10 AM (descending) orbit.
Launch was on 6/24/02
Had some problems with NOAA-15, -16: HIRS pixel offset, AVHRR mis-location, AVHRR PRT coeffs wrong, AMSU roll error…

## Slide 5: Examples of Enhancements and New Tests
Characterize anomalies and devise operational workarounds
  AMSU-A 30-count jump
  HIRS pointing error and “initial pixel biases”
Search for AMSU-A and HIRS scan asymmetries and offsets
Determine absolute navigation accuracies of AMSU-A and –B and AMSU-A/AMSU-B co-registration.
Search for AVHRR image striping
Characterize time dependence of responsivities
Intercompare observations from NOAA-17, -16, and –15

## Slide 6
AMB016
Relative pointing accuracy of AMSU-B to AMSU-A
Bennartz
Kleespies/ORA
Notes: Use Backus-Gilbert to convolute (or interpolate) AMSU-B (1.1o, or 16 km) 89 GHz channel to AMSU-A (48 km) 89 GHz channel (ch 15). Compute rms differences in TB as function of BG interpolation coeffs. BG interp coeffs give shift of AMSU-B. (More correctly, make linear comb of AMSU-B fov’s to approximate AMSU-B fov; then compute rms diff over scene. Y axis is AMSU-B line shift. X-axis is AMSU-B pixel shift. )
Geolocation accuracy tests indicate the problem is with AMSU-B.
Geolocation accuracy gotten from convoluting land-sea map to resolution of AMSU. Vary locations about initial navigation state, computing correlation with each. Highest correlation wins.

## Slide 7: AVHRR Channel 2 Response Decay
“Truth”
NOAA-17
NOAA-14
Data are “albedos” of Libyan desert from pre-launch cal.
J. Sullivan, ORA
Notes: 0.58-0.68 um
0.725-1.00 um
1.58-1.64 um
NOAA-14 points are for same # days after launch as NOAA-17. N-14 launch was 12/30/94
Veg index = (2 –1)/(2+1)
June 24 (launch) is day 175

## Slide 8: Intercomparisons at Orbit Intersections
C. Cao
ORA
Notes: NOAA-17 is 10 AM descending
NOAA-16 is 2 PM ascending
Location is East Siberian Sea
Orbital intersection technique uses coincidences between satellites with different local observing time, which occur in polar regions
Data from SAA. If we were doing AVHRR, would want HRPT (full resolution)
About 10/month in north. Here used north, rather than south, because it was summer—got warm and cold scenes, water, …

## Slide 9
HIRS-16/HIRS-17 Brightness Temperature Differences
(T16 - T17) (sample size: 11x11x3)
C. Cao, ORA
C. Cao, ORA
Notes: Not adjusted for SRF differences
11 x11 at center of superswath (near nadir). Three different scenes.

## Slide 10
Unified NESDIS System for Monitoring Instrument Radiometric Performance

## Slide 11: Motivation
Need for updated monitoring capability in Initial Joint Polar System (NOAA/METOP) ground system
National Research Council recommendation: NESDIS should create web site with info on S/C condition and changes of interest for construction of climate data records
Generally acknowledged need for comprehensive, user-friendly system for monitoring radiometric performance
Notes: In various offices, NESDIS has pieces of monitoring system, but no integrated, one-stop system.

## Slide 12
High-level information for managers
A history of metadata, e.g., to help climate scientists interpret features in time series of satellite-based geophysical data
Time series of engineering and radiometric performance data
Permanent archive, retrieval, & documentation
Example: GOES-8
sounder slopes
A Single, Web-Based Searchable System
Notes: An early quality-control component of system for NOAA/NESDIS Scientific Data Stewardship
Initially to be designed for POES, IJPS, GOES I-Q
Later extend to NPP?, NPOESS, GOES-R, DMSP
Initially use current data
Later add in retrospective data

## Slide 13: Plan
Kickoff meeting held 1/6/03
Survey of current capabilities & generation of system requirements document (FY03)
Formulation of alternative architectures (FY04)
4. Design and construction of system (FY04-FY05)

## Slide 14: NPOESS Cal/Val
NPOESS concept--“Shared System Performance Responsibility” (contractor and government teams)
Cal/Val planning is joint activity between SSPR contractor & gov’t
IPO soliciting internal government studies for cal/val
Sensor calibration to be based on NIST standards
SSPR contractor has prime role in pre-launch cal, verification, & characterization, with gov’t oversight
Gov’t has ultimate responsibility for executing post-launch validation, with contractor participation
  Gov’t maintains key correlative data
  ------------------------------------------------------------------------
NPOESS = National Polar-orbiting Operational Environmental Satellite System (NOAA/DOD/NASA), managed by Integrated Program office (IPO)
Notes: Northrop-Grumman/Raytheon = SSPR contractor/sub-contractor
Gov’t responsible for availability of validation data
CrIS = Cross-track Infrared sounder
VIIRS= visible/infrared imager/radiometer suite
ATMS= advanced technology microwave sounder
CMIS= conical microwave imager/sounder
GPS = global positioning system occultation sensor
OMPS = ozone mapping and profiling suite
APS = aerosol polarimeter sensor
ERBS= Earth radiation budget sensor
And more: Scatterometer, Total solar irradiance sensor (TSIS), Radar altimeter, …

## Slide 15: NPP Cal/Val
NPP = NPOESS Preparatory Project (IPO/NASA)
NPP carries VIIRS, CrIS, ATMS, and OMPS
Purpose
  Risk-reduction for NPOESS
  EOS-NPOESS bridge for data for Global Change Research
A joint cal/val plan was developed by IPO and NASA
  IPO: cal/val for operational products (RDRs, SDRs, EDRs)
  NASA: cal for science applications, trending of sensor performance, validation of level-1 data and CDRs
  SSPR Contractor: development of cal/val activities adopting NPP cal/val guidelines
Notes: Understanding & compliance of draft cal/val plan was a criterion for contract award
Ball Aerospace = NPP contractor, only for space segment
Ground system & processing involves NPOESS SSPR
NPP launch ’06; 5-yr life
EOS Terra quits: late ’05
EOS Aqua quits: ’08
NPOESS C1 launch ‘09
VIIRS = Visible/Infrared Imager/Radiometer Suite
CrIS = Cross-TrackInfrared Sounder
ATMS = Advanced Technology Microwave Sounder

## Slide 16: EXTRAS

## Slide 17: NOAA-17 AMSU-A Ch. 3 Anomaly
Corrective algorithm being implemented in ops
Scene Tb errors  0.8K
T. Mo, ORA
Notes: 30-count jump, lasts 30 min
Assuming effect is also in Earth counts, effect is calibrated out everywhere except for the seven lines surrounding the discontinuities because of the 7-line averaging of cal coeffs.
Although this anomaly is not related to the PLLO, for information, PLLO stands for phase locked loop oscillator.

## Slide 18: AVHRR Visible/Near IR
Preliminary vicarious calibration from Libyan desert
Albedo (%)
J. Sullivan/ORA
Notes: Meas uses pre-launch coeffs.
Since ch 2 decreased more than ch 1, the veg index sometimes goes negative, which is interpreted as water. Sometimes this water shows up in the Sahara desert!

## Slide 19: HIRS Initial Sample Bias
3 counts higher for channel 1, ~1 count for most other longwave channels
Regardless of space, bb, or earth view
C. Cao/ORA
Sample number (56 samples)
Parked bb view, 877 scanline average, channel 1, 7/15/2002
Sample number (56 samples)
Count (average)
Notes: Effect is serious only in channels 1-3, and mostly in 1.
We only use the last 48 samples of BB and space, so that isn’t a problem.
But it affects Earth data too!! So channel-1 data are wrong on first 3 or so pixels of scan.

## Slide 20
HIRS slew to space for 11 cal sequences D02197, Jul 16,2002
HIRS15 sees space at element 4, HIRS 16 and HIRS 17 see space at element 3 .
HIRS Pointing Error
T. Kleespies/ORA

## Slide 21
Satellite Collocation

## Slide 22: New System Will
Be a one-stop, user-friendly, searchable, web-based system for compiling, monitoring, and archiving polar and geostationary instrument performance data
Not re-invent the wheel: It will be based on, and/or incorporate, and/or link to existing systems in NESDIS and elsewhere (e.g., MIT/LL, ITT, …)
Link to related external sites, e.g., NCEP and ECMWF radiance quality assessment pages
Notes: Prototype could be SRAS (Secure Remote Access System) in SOCC
Should be web-based searchable system.
Should include TOARS
Need to coordinate with NPOESS