## Slide 1: NASA/NIST Report Remote Sensing Efforts During the Past Nine Months
CEOS WGCV 20
12 – 14 February 2003
Hobart, Tasmania, Australia

## Slide 2: Outline
Calibration/Validation Activities
  Lunar Radiometry
  Sun Photometers
  Ocean Color & SIMBIOS
  Aura (HIRDLS)
Intercomparisons
  Aperture Area for Total Solar Irradiance
  NASA’s Commercial Remote Sensing Program
Workshops
  Satellite Instrument Calibration Workshop
  Climate Change Research Initiative
Planned Events
  Terra Deep Space/Lunar Maneuver
  Terra Cross-calibration Workshop
  TXR deployment to Oxford for HIRDLS
  Solid state source

## Slide 3: Calibration/Validation Activities
Lunar Radiometry (ROLO, USGS/Flagstaff)
  lunar observations with orbiting satellites are a cal/val activity
  accuracy of ground observations critical
  ROLO lunar irradiance model successfully used in on-orbit inter-instrument comparisons
NASA EOS/NIST goals
  verify absolute radiometric calibration of ROLO
  compare stellar photometry (Vega) with NIST radiance scale based on HACR
  collimator built for telescope characterization
ROLO’s two telescopes: VNIR and SWIR
On-orbit comparison of SeaWiFS, MTI, ALI, and Hyperion calibrations using ROLO lunar irradiance model
Notes: -The lunar radiometry project known as ROLO (Robotic Lunar Observatory) has acquired over 85,000 images of the Moon during the past 8 years from an dedicated observatory in Flagstaff AZ. The lunar images are acquired over all phases during the bright half of the month (+90 to –90 degrees phase). If the radiance or reflectance of the Moon can be measured over a range of phases and librations, the Moon can be used as a radiometrically stable on-orbit calibration target for remote sensing instruments. The top photo shows the VNIR and SWIR telescope systems in ROLO.
-The ROLO project has produced a lunar irradiance model which can be used to compare the measurements of on-orbit satellite instruments. This is illustrated in the plot. The plot shows the % difference of lunar measurements made by the SeaWiFS, the Multispectral Thermal Imager (MTI, a DOD instrument), the Advanced Land Imager (ALI), and the Hyperion instruments. ALI and Hyperion are on NASA’s EO-1 spacecraft.
-NASA and NIST are engaged in a program to verify the absolute radiometric calibration of ROLO. Currently, the lunar radiance and irradiance models are tied to stellar photometry using the star Vega. In April/May 2003, a collimated, calibrated source which mimics the size and intensity of the Moon will be used in the absolute calibration and characterization of the ROLO telescope systems.

## Slide 4: Calibration/Validation Support
Sun Photometer Characterization
  Two instruments from the SIMBIOS Project were characterized at NIST
  Plans in formulation for CIMEL/AERONET reference instrument characterizations (early 2003)
Spectral Responsivity: Supplied data compared to actual instrument response
Notes: -SIMBAD information here available from either Carol or Steve.
-Two reference CIMEL sunphotometer instruments from NASA’s AERONET project will be characterized using the SIRCUS facility in 2003. Initial testing of these instruments will begin in mid-February.

## Slide 5: Ocean Color
Marine Optical Buoy (MOBY)
  absolute, in situ validation for ocean color satellites (SeaWiFS, MODIS, OCTS, etc.)
NIST support to correct for spectral out of band (stray light in spectrographs)
  Experimental characterization completed
Impact (SeaWiFS): 6% decrease in median global chlorophyll
Red Spectrograph
Blue Spectrograph
Lu() derived using the two spectrographs in MOBY or the MOS
Profiler disagree in their region of overlap;
MOBY data uncorrected and corrected for stray light
Notes: -Ocean color information here available from either Carol or Steve.

## Slide 6: SIMBIOS Program http://simbios.gsfc.nasa.gov
The Sensor Intercomparison and Merger for Biological and Interdisciplinary Ocean Studies (SIMBIOS) Program goal is to assist the international ocean color community in developing a multi-year time series of calibrated radiances that transcend the spatial and temporal boundaries of individual missions.
Objectives
Ensure development of internally consistent research products and time series from multiple satellite ocean color data sources
Develop methodologies for cross-calibration of satellite ocean color sensors
Develop methodologies for merging data from multiple ocean color missions
Promote cooperation between ocean color projects
Serve as a prototype for other Earth observation programs
Notes: <number>
<footer>
<header>
<date/time>

## Slide 7: Instrument Reviews
HIRDLS
  High Resolution Dynamic Limb Scanner on EOS Aura scheduled for launch in January 2004.
    infrared, 6 m to 18 m
  NIST and EOS Calibration representation on calibration and instrument pre-ship reviews at Oxford (7/9-10 & 11/21)
SORCE
  SOlar Radiation and Climate Experiment
  EOS Calibration representation on all pre-ship instrument, environmental, and observatory reviews (2/2,10/8-9 & 10/22)
  SORCE successfully launched on 1/25.
MISR
  Multi-angle Imaging SpectroRadiometer on EOS Terra
  EOS Calibration representation on calibration workshop (10/21)
Notes: -Personnel from NASA and NIST have recently participated in a number of instrument reviews and workshops.
-The High Resolution Dynamics Limb Sounder (HIRDLS) instrument was successfully calibrated in November & December 2002, shipped to Northrop Grummond in December 2002 and integrated onto the Aura spacecraft. The HIRDLS instrument and the other Aura instruments (the Ozone Monitoring Instrument (OMI), the Microwave Limb Sounder (MLS), the Tropospheric Emission Spectrometer (TES) engaged in intensive calibration and characterization programs in late 2002. In particular, Oxford University did a wonderful job of calibrating HIRDLS under demanding time constraints.
-The Solar Radiation and Climate Experiment (SORCE) launched on 1/25/03. SORCE contains the Total Irradiance Monitor (TIM) and Spectral Irradiance Momitor (SIM) instruments in addition to the SOLSTICE and XPS instruments. The team of University of Colorado’s Labroratory for Atmospheric and Space Physics (LASP) and Orbital Sciences Corporation worked extremely hard to make this mission a success.
-The MISR instrument on EOS Terra has examined its calibration, particularly with respect to dark ocean scenes. MISR is interested in radiometry over ocean scenes and detection of aerosols over oceans.

## Slide 8: Aperture Area Comparison for Exo-atmospheric Total Solar Irradiance (TSI)
Goal: quantify the spread in aperture area measurements made by/for previous, existing, and planned TSI missions.
Aperture area is the largest contributor to TSI measurement uncertainty.
Led by Earth Observing System (EOS) Calibration Scientist and NIST
Apertures measured to date at NIST:
  Royal Meteorological Institute, Belgium
  World Radiation Center, PMOD, Switzerland
Expect apertures from JPL/ACRIM III & possibly NASA/LaRC ERBS
Note: First comparison of ACRIM & SORCE/TIM TSI measurements will occur in approx. May 2003.
Notes: We’ve included the main groups with historical heritage for solar irradiance. They’ve done balloon, shuttle, spacecraft. On the RMI (Belgium) list is SOLCON, SOVA1, PICARD, and SOVIM. On the WRC/PMOD list is PMO, SOVA-R, and VIRGO. ACRIM is a JPL instrument and there are currently two on-orbit. The ERBS apertures, if they are located, were last measured approximately 18 years ago.
The note on this slide points out that the first on-orbit comparison of ACRIM and TIM will be in May of this year. The agreement is hoped to be much better than 0.2%.

## Slide 9: Site Visit to NASA Stennis
NASA’s Commercial Remote Sensing Program (CRSP)
  geo-location, imaging studies, radiometry
NASA EOS/NIST visit in November 2002
  Areas examined:
    uncertainty budgets
    integrating sphere sources
    validation instrument characterizations
EOS/CRSP radiometric measurement comparison in Spring 2003
Natural and man-made targets at Stennis
Notes: The Commercial Remote Sensing Program is located at NASA Stennis Space Flight Center. The mission of this program is to validate the image and radiometric calibration of Earth scenes obtained from commercial remote sensing instruments. The EOS program, represented by NIST and NASA, in November 2002 visited Stennis with the goal of “closing the loop” on calibration in the EOS and CRSP.
The top photo is a pond at Stennis whose primary use is to cool the test stands after rocket test firings. The CRSP deploys radiometers on float in this pond to validate the thermal measurements of overflying instruments. The bottom photo is a large concrete pad which has been painted with alternating, converging white and black stripes. It is use to validate the resolution of commercial remote sensing instruments.

## Slide 10: Workshops
Workshop for Satellite Instrument Calibration for Global Climate Change
  held November 12-14, 2002 in College Park, MD
  organizing agencies: NIST, NOAA, NPOESS-IPO, NASA
  workshop objectives:
    Develop satellite cal and intercal requirements for measuring global climate change
    Recommend directions for future improvements in satellite instrument cal and intercal
US Climate Change Science Program: Planning Workshop for Scientists and Stakeholders
  - held December 3-5, 2002 in Washington D.C.
  - review of U.S. Global Change Research Program (USGCRP) and Climate Change Research Initiative (CCRI) strategic plans with emphasis on the development of short-term (2-5 year) products to support climate change policy and resource management decision-making.
Notes: Satellite instrument workshop-I think you know about this.
CCRI – NIST (CSTL and PL) attended the US Climate Change Science Program Planning Workshop for Scientists and Stakeholders from 3-5 December 2002. The purpose of the meeting was to review the draft of the Strategic Plan for the Climate Change Science Program. NIST participants reviewed the plan and forwarded our comments through our representative, Hratch Semerjian, director, CSTL.

## Slide 11: Planned Events
Terra Deep Space/Lunar Maneuver
  Pure pitch of Terra spacecraft to enable instruments to view deep space and/or Moon
  Approved by NASA HQ
  Request made for deep space maneuver on 3/24 & 4/4 and lunar maneuver on 4/14.
AM Instrument Cross-calibration Workshop
  April/May 2003 timeframe
  Examine AM instrument (Terra, EO-1, SAC-C, ETM+) comparison and cross-calibration issues
TXR deployment to Oxford University
  Independent measurement of blackbody sources used to calibrate HIRDLS
  First deployment of TXR for EOS in thermal vacuum chamber for EOS sensor
Solid State (LED-based) Source Development
  for instrument calibrations and stability monitors
  for direct measurement of spectral stray light correction factors
Notes: Planned events include a pitch of the EOS Terra platform in March and two in April to enable on-orbit calibration of visible, near infrared, shortwave infrared, and thermal instruments.
The AM cross-cal workshop coordination is just beginning.
The TXR deployment to Oxford is being coordinated.
The Solid State Source development involves the use of different color LEDs in a sphere setting. Specific LEDs could be illuminated at set levels to mimic the spectral distribution on on-orbit scenes, thereby addressing the universal problem of using a red source (typical integrating sphere) in the calibration of Earth scenes (which are often bluer).

## Slide 12: Summary
Workshops
  aid for future planning
Intercomparisons
  aperture area: modern methods for a decades-old problem in solar physics
  establish linkage between commercial and scientific remote sensing
Cal/Val Activities
  continue to improve and/or assess accuracy of radiometric scales
  focus on calibration, characterization of validation instruments and develop measurement protocols
New Technologies & Methods in Cal/Val
  extend EOS calibration and characterization to NPP/NPOESS era instruments
Notes: I think this slide is self-explanatory.