## Slide 1
CEOS WGCV 20
Presentation of Norwegian CalVal activities
NILU, NIVA and NERSC
Presented by: Aasmund.Fahre.Vik, afv@nilu.no,

## Slide 2
  Kerstin Stebel et al. - 05.02.2003
Cal/Val measurements in 2002
Oslo (59.9 oN, 10.7 oE)
GUV: 0601 - 1019 O3 column
Brewer: 0821 - 1023 O3 column
Ørland (63.4 oN, 9.2 oE)
O3 sondes: 0606 - 1127 (23 profiles) O3 profile
Andøya (69.3 oN, 16.0 oE) Ozone DIAL: 0908 - 1228 (46 profiles) O3 profile
Symocs-Vis: 0719 - 1115 O3, NO2 column
Symocs-UV: detector failure OClO, BrO column
Brewer 0602 - 1017 O3 column
GUV 0601 - 0827 O3 column
Ny Ålesund (78.9 oN, 11.9 oE) GUV 0601 - 0830 O3 column SAOZ 0909 - 2010 O3, NO2 column
.
Comparison of co-located O3 profiles from the ALOMAR lidar
with MIPAS data (6 pairs) shows good agreement between above 100 hPa, particularly below 20 hPa (0+10 %). Mean differences of ca. 15 % are seen between 1 and 10 hPa. The comparison of GOMOS twilight measurements (7 pairs)
with ozone profiles from the lidar show large fluctuation in GOMOS ozone profiles and a ca. 20% negative bias
at around 20 km.
Norwegian Validation of ENVISAT Atmospheric Chemistry Products (NOVENA)
Objective: To contribute to the validation of level-2 products of three ENVISAT instruments (GOMOS, MIPAS, SCIAMACHY) by means of the Norwegian Atmospheric Monitoring network.

## Slide 3
YVAN ORSOLINI
Norwegian Institute for Air Research
NILU
Mapping of ENVISAT MIPAS Ozone
in the Stratosphere
November 2002
Southern Hemisphere Final Warming
Isentropic Ozone (ppmv): 3-day time-averaged, binned in longitude-latitude (figure at 650K or 25 km)
Orsolini Y., D. Allen , C. Randall , G.L. Manney, G. Stiller, ”Final breakdown of the southern hemisphere stratospheric polar vortex in the spring 2002, as diagnosed in MIPAS ozone”, J. of Atmos. Sci., Special Issue on Antarctic winter and sudden warming in 2002

## Slide 4: Validation of MERIS data products in Skagerrak and Kattegat Sea - VAMP Norwegian Institute for Water Research, Oslo Contact Kai Sørensen, NIVA kai.sorensen@niva.no ESA contract no 14849/00/NL/Sfe(IC)
Validation activities in 2002
  Skagerrak with Norwegian coastal current and Atlantic North Sea
  Kattegat with Baltic water,
  Danish West Coast with Jutland Current and German Bight water
Validation methods used
  In situ optical measurements
  Water analysis
  Ships of opportunity
MERIS data to be validated
  Water Leaving Reflectance
  Algae Pigment Index
  Total Suspended Material
  Yellow Substance

## Slide 5: Validation of MERIS
Optical in situ measurements
  Scattering measurements with bb6 and absorption data with AC9
  Water leaving reflectance with an Biospherical radiance meter
Inter-comparisons of Chlorophyll
  11 MAVT validation teams represented
  20 laboratories participated
  HPLC chlorophyll-a methods
  Spectrophotometric chlorophyll methods
Water analysis performed
  Algal pigment and pigment absorption
  CDOM and bleached particle absorption
  Total suspended material

## Slide 6: ESA ENVISAT AO 813: MERIS Validation in the Norwegian Coastal Current by The Nansen Center / University of Bergen
Lasse H. Pettersson, Dominique Durand, Kai Sørensen*, Birgitte R. Furevik, Johnny A. Johannessen, et al.
Nansen Environmental and Remote Sensing Center, Bergen, Norway
*NIVA, Oslo, Norway

## Slide 7: Norwegian Coastal Current: Validation Activites
Three validations cruises with R/V H. Mosby
Sample Validation - MERIS L-2 Products (MAVT protocol)
  Chlorophyll-a (HPLC and absorption)
  Total Suspended Matter (GF/F)
  Yellow Substance
Planning and Complementary Information
  Hydrography - CTD and SeaSoar
  Ocean Currents - ADCP
  Model integration (3-D bio-physics)
  NRT SeaWiFS
Cloud cover “predictions”!
  NRT AVHRR & SeaWiFS
Clouds

## Slide 8: Preliminary MERIS ”Validation” - 13. July
Area/ Parameter | MERIS 13. July | Samples + 1-3 days
Coastal Algal1 | 0.95 | 0.93
Coastal Algal2 | 2.5-3.5 | 0.91
Coastal TSM | 0.4 | 0.43
Off-shore Algal1 | 1.5 | 1.31

## Slide 9
SeaWiFS: 26 March 2002
ERS/SAR: 27 March 2002
Sensor
Synergies
SeaWiFS
Chlorophyll
ERS-2 SAR
Roughness

## Slide 10: Summary (NERSC)
23 days of sampling at 73 station locations at 3 depths
Some validation match-up in SeaWiFS data
Poor match of high quality data for MERIS - in time and space (clouds/weather/sensor problems)
Results: Acceptable MERIS Coastal Algal1 and TSM products
Significant (3*) overestimate of Coastal Algal2 product
Still ”match-ups” in lacking MERIS data - require ESA ACTION!
Extended products validation efforts through:
  MERIS, SeaWiFS, MODIS and others (!) cross comparisons - most data available and provide others
  Envisat synergies MERIS FR, AATSR and ASAR
Operational NRT MERIS data delivery from March, 2003 - spring bloom