## Slide 1
Country report 2003
Masanobu Shimada
NASDA/EORC/Feb, 12-14/CSIRO Hobart, Tasmania, Australia
ADEOS-2
ALOS(Pi-SAR)
PR/TRMM

## Slide 2
ADEOS-2
Launched on 10:30:00, Dec. 14 2002, at Tanegashima Space center
800 Km, 14 + 1/4 daily revolutions,
AMSR
GLI(36 channels, include. 250m vegetation channels)
ILAS-2
Seawinds
POLDER2
All the sensors are well conditioned.
Data will be recorded by Tape recorder, Optical disk recorder,and down linked to walloppes, Alaska, Hatoyama, through DRTS(when available)
First images were acquired on January 18, 25, 2003.

## Slide 3
AMSR First-light
In the Sea of Okhotsk, colors varying from light blue to white correspond to sea ice distribution.
Over the Pacific Ocean and Japan Sea, the areas of light blue correspond to high-concentration liquid water clouds.
AMSR capturing the Japanese Islands
R: 37GHz H-Pol.
G: 89GHz H-pol.
B: 89GHz V-pol.
Captured by AMSR
9:45 (JST)
January 18, 2003
Notes: This is the first-light image obtained by the Advanced Microwave Scanning Radiometer (AMSR) onboard Midori-II. This is a false-color composite image using brightness temperatures of 36.5-GHz horizontal polarization, 89.0-GHz horizontal polarization, and 89.0-GHz vertical polarization channels. The data is acquired around 11 a.m. on January 18, 2003 JST. Over the Pacific Ocean and Japan Sea, the areas of light blue correspond to liquid water clouds. In the Sea of Okhotsk, colors varying from light blue to white correspond to sea ice distribution.
みどりII搭載高性能マイクロ波放射計による初画像。36.5GHz水平偏波、89.0GHz水平偏波、89.0GHz垂直偏波を用いた擬似カラー合成画像である。観測時間は2003年1月18日午前11時頃(日本時間)。本州以南の海域における薄い青色部分は水を多く含んだ雲に、オホーツク海に見られる薄い青色～白色の部分は流氷に、それぞれ対応する。

## Slide 4
Sea ice concentration and motion vector
Increase of sea-ice covered areas is indicated by colors varying from cobalt blue to white.
The arrows shows sea ice motion derived by comparing the left data and that from the same day about 10 hours before.
RGB composite of brightness temperatures
In the Sea of Okhotsk, colors varying from light blue to white correspond to sea ice.
Sea ice distribution in the Sea of Okhotsk observed by AMSR
R: 37GHz H-pol.
G: 89GHz H-pol.
B: 89GHz V-pol.
Captured by AMSR
11:30 (UTC)
January 18, 2003
AMSR First-light
Notes: 高性能マイクロ波放射計(AMSR)によるオホーツク海の流氷(海氷)画像。左図は2003年1月18日の夜間(20時半頃)に取得されたデータによる擬似カラー合成画像。36.5GHz水平偏波、89.0GHz垂直・水平偏波を用いている。オホーツク海に見られる薄い青色～白色の部分は流氷に、薄い青色は新しくできた氷にほぼ対応している。また、太平洋における薄い青色部分は水を多く含んだ雲に対応する。マイクロ波観測は昼夜に関係なく、かつ雲の影響を受けにくいという利点を持っており、流氷をくっきりと捉えることができている。
右図は、同データから求めた海氷密接度であり、濃い青色が海氷のない海水面で、白くなるほど海氷に覆われていることを示す。図中の矢印は同日午前11時頃(約10時間前)に観測されたAMSRデータと比較して求めた海氷の動きを表している。海氷がオホーツク海北部から南下している様子と、知床半島に接岸していることがわかる。例年に比べると、今年は海氷の南下が早く、網走では1月11日に流氷初日を迎えた。
Sea ice distribution in the Sea of Okhotsk captured by AMSR. Left is the false-color composite image using the data acquired at night time (around 20:30) on January 18, 2003 JST. Brightness temperatures of 36.5-GHz (horizontal polarization) and 89.0-GHz (both vertical and horizontal polarization) channels were used. In the Sea of Okhotsk, colors varying from light blue to white correspond to sea ice. Distribution of newly-formed sea ice is approximately indicated by light blue. Areas of light blue over the Pacific Ocean correspond to high-concentration liquid water clouds. It is the advantages of microwave observation techniques to enable measurements during night and day. Thus, through non-precipitating clouds, the sea ice extension can be well distinguished using the night-time image.
The right image shows the sea ice concentration estimated from the same data. Cobalt blue indicates open sea surface with no sea ice coverage. Increase of sea-ice covered areas is indicated by colors varying from cobalt blue to white. The arrows superimposed on the map shows sea ice motion derived by comparing AMSR data acquired at 8:30 p.m. and that from the same day about 10 hours before. It can be seen that sea ice is advancing southward from northern part of the Sea of Okhotsk and reaching to the Shiretoko Peninsula. This year, the sea ice is advancing southward faster than in other years. At the Abashiri weather station in Hokkaido, Japan, approaching sea ice was observed on January 11th at the first time.

## Slide 5
Aqua/AMSR-E
AMSR-E on EOS Aqua
Left: Monthly mean global SST in November 2002 retrieved from the AMSR-E
Right: Close-up view (TRMM PR, AMSR-E SST, AMSR-E SST: Anomaly from Reynolds Climatology)
2002/03 El Niño Event Observed from AMSR-E
SST is 2 to 3ºC higher than that of a normal year over the central equatorial Pacific and about 1.5ºC higher over the eastern equatorial Pacific.
Notes: These are the images acquired by NASDA developed AMSR-E aboard NASA’s Aqua satellite, capturing the first El Niño event in the 21st century. AMSR-E is successfully continuing the global measurement since June 2002. Left image shows the monthly mean global SST in November 2002 retrieved from the AMSR-E data. The SST retrieval algorithm was developed by Dr. Shibata of the Meteorological Research Institute. Right figures present the close-up view of the white rectangle in the left figure. The top panel indicates monthly accumulated rainfall of the same month observed by the Precipitation Radar on board the TRMM satellite. Middle panel illustrates the monthly mean SST retrieved from AMSR-E data. These two images clearly illustrate that the warmer SST regions correspond well to the heavy rainfall regions. Lower panel indicates the differences of monthly mean sea surface temperature from normal years. SST is 2 to 3ºC higher than that of a normal year over the central equatorial Pacific and about 1.5ºC higher over the eastern equatorial Pacific.
NASAのAqua衛星に搭載したAMSR-Eによる、21世紀最初のエルニーニョ現象。AMSR-Eは昨年の6月から順調に全球観測を継続している。左図は、AMSR-Eデータから推定した2002年11月の全球月平均海面水温である。海面水温推定アルゴリズムは気象研究所柴田氏の開発による。右図は、左図の白枠領域の拡大である。上段は、TRMM搭載降雨レーダにより得られた同じ月の月積算降水量である。中段はAMSR-E月平均海面水温である。これらを比較すると、海面水温の高い領域と降水量の高い領域が良く一致していることが分かる。下段は海面水温の平年値からの差を示しており、通常の年に比べて中部赤道太平洋で海面水温が2～3度高くなっており、また東部赤道太平洋上でも1.5度程度、海面水温が上昇していることがわかる。

## Slide 6
Aqua/AMSR-E
AMSR-E on EOS Aqua
Daily mean sea ice concentrations around the Antarctic regions during the period of July to December in 2002.
In the Antarctic, sea ice cover is extending toward the winter in the months of June to August and is decreasing after September.
Sea ice concentration around Antarctica observed by AMSR-E
Observed by AMSR-E
July - December, 2002
Notes: This is another example showing the continuous observation by AMSR-E. This animation shows daily mean sea ice concentrations for the Antarctic region in the period from July to December, 2002. The sea ice cover in the Antarctic is extending toward the winter in the months of June to August and is decreasing after September. AMSR-E’s high spatial resolution enables us continuous monitoring of sea ice extent in detailed.
南極周辺の海氷密接度の季節変化。AMSR-Eが連続して観測を行っているひとつである。アニメーションは南極域における日平均の海氷密接度を示しており、期間は2002年の7月1日から12月31日まで(Aqua衛星の状態によりデータが欠けている日付がある)。南極域の海氷面積は6月～8月の冬季(南半球)に向けて増加し、9月以降は減少する。AMSR-Eの高い分解能により、海氷域の継続的なモニタリングが詳細に実施できる。

## Slide 7
R: Ch 13 (678nm)
G: Ch 8 (545nm)
B: Ch 5 (460nm)
1 km
Captured by GLI
9:45 (JST)
January 25, 2003
Pressure 966hPa
A great winter cyclone.
GLI First-light

## Slide 8
R: Ch 28 (1640nm )
G: Ch 23 ( 825nm )
B: Ch 22 ( 660nm )
Kyushu, Japan
Taiwan
Captured by GLI
11:30 (JST)
January 25, 2003
ICE CLOUD (Blue)
WATER CLOUD (White)
WATER CLOUD
250m
View of Kyushu Island, southern Japan, and the East China Sea.
GLI First-light
Notes: [View of Kyushu Island, southern Japan, and the East China Sea]
The color composite image was derived from the GLI spectral channels 28 (1640 nm), 23 (825 nm), and 22(660nm). The spatial ground resolution is 250m. Thick cloud systems stretching from the Asian continent to the East China Sea are visible in the image, with low altitude warm clouds appearing white and higher altitude ice clouds in blue. Kyushu Island and northern part of Taiwan can be identified at the chink of the clouds systems.
The GLI instrument has 36 spectral channels ranging from ultraviolet to infrared, designed for high accuracy observations of the atmosphere, ocean,land, and the cryospehre.
「GLIが観測した九州と東シナ海」
宇宙開発事業団(NASDA)が開発した環境観測技術衛星「みどりII」搭載のグローバルイメージャ(GLI)による画像。図-1は2003年1月25日の昼間(11時30分頃)に取得されたデータによる合成画像。250メートル解像度の観測波長チャンネル28(波長1640ナノメートル)、23(825ナノメートル)、22(660ナノメートル)を使用している。大陸から東シナ海にかけて雲が広がっている。白い部分は低層の暖かい雲を、青い部分は高層の氷雲を示している。雲の間から、九州および台湾北部が見える。
グローバルイメージャは紫外から赤外域にかけて36の観測波長チャンネルを持ち、大気・海洋・陸域・雪氷圏の様子や変化を高精度かつ全地球規模で観測することができる。

## Slide 9
ALOS project
Launch timing: June-August of 2004
Launcher H2A
PALSAR, PRISM, AVNIR-2, high resolution sensors.
All the sensors were integrated at Tsukuba space center and the other on-ground measurement, interface testing started.
Ground system is under integration
ALOS NODE project (among NASDA, ESA/CNES, NOAA, GA) is in progress.
Observation scenario is being built up for consistent observation of the three sensor for enough CAL/VAL and application.
CAL/VAL plan an procedure is being integrated.
Amazon rain forest is selected, and artificial PARC is being developed.
Geometric and radiometric accuracy will be assured in 8 months before data distribution (9 months after the launch)
PI workshop will be held at Awaji-island, Jan 19-23, 2004

## Slide 10
ALOS Orbit and satellite parameters
Type Sun-Synchronous Sub-recurrent
Local Time at DN 10:30 AM ± 15min.
Altitude 691.65km
Inclination 98.16 degrees
Revolutions per day 14+27/46
Period 98.7 minutes
Longitude Repeatability +/-2.5km (above equator)
Orbit maintenance Once every week
Max. operation period 70 minutes per orbit
Data collection DRTS+direct transmission
Yaw steering Selective ON/OFF
Attitude error each axis 0.4e-4°(determination),
0.1°(maintenance)

## Slide 11
PALSAR Operation Modes
Limitation: Incidence angel < 30 degrees

## Slide 14
Polarimetric Active Radar Calibrator (PARC)
Earth Observation Center
North

## Slide 15
ALOS project
Launch timing: June-August of 2004
Launcher H2A
PALSAR, PRISM, AVNIR-2, high resolution sensors.
All the sensors were integrated at Tsukuba space center and the other on-ground measurement, interface testing started.
Ground system is under integration
ALOS NODE project (among NASDA, ESA/CNES, NOAA, GA) is in progress.
Observation scenario is building up for consistent observation of the three sensor for enough CAL/VAL and application.
CAL/VAL plan an procedure is being integrated.
Amazon rain forest is selected, and artificial PARC is being developed.
Geometric and radiometric accuracy will be assured in 8 months before data distribution (9 months after the launch)