## Slide 1
NPL activities related to CEOS WGCV
Nigel Fox
Optical Radiation Measurement Group
Feb 2003

## Slide 2: NPL activities:
General awareness and promotion of “traceability” and “best practise” – EO community, WMO, Users.
Calibration support for Geostationary Earth Radiation Budget (GERB) series On board MSG
Development of improved calibration transfer standards
Cal/Val for Atmospheric chemistry
Promoting TRUTHS as a concept
Seeking to develop a network to improve “QA of EO measurement”
Land as a starting point

## Slide 3
Geostationary Earth Radiation Budget (GERB) calibration support
NPL developed and supplied radiance sources for both visible and IR calibration of GERB at Imperial College London
Uncertainties required, ~1% (300 nm to 2.5 um) is lower than any terrestrial requirement
NPL also provided support equipment to determine end-to-end spectral response at IC and calibrated all optical sub-systems – mirrors, detector array before integration

## Slide 4: Technology Innovations for Radiometer Instruments (TIFRI) Reference black bodies for in-flight and pre-flight calibration
ESA Technology development project: To design,
build and test a black body with criteria to suit space
applications.
Design Specification EOL (7yrs) :
200 – 400 K
5 mK accuracy
1 mK resolution
HIRDLS used as example for FoV and size
Thin film Pt 100 selected
Novel AC bridge electronics
Reflective wall black body
- Low mass
BB < 0.3 kg (0.7 )
Ft Electron ~1.5 kg (3.0)
- High emissivity ~0.999 (0.997)
Active heating and cooling using Peltier
TIFRI utilises reflective walls to increase emissivity but with low mass and power

## Slide 5
Transfer Standard Absolute Radiance Source (TSARS)
High spatial uniformity and use of filter radiometer stabilisation allow accuracies approaching 0.1%
100 mm Exit port
50 mm Exit port
±0.2%
±0.05%
A new smaller TSARS (<0.5 m3) for potential field applications is currently under evaluation at NPL.
To be used as demonstration with GOME 2 in conjunction with TNO

## Slide 6: Understanding need / role for “standards”
Requirement: greater uptake and use of EO data as a routine tool by USERS
Many issues
    Cost
    Ease of use
    Lack of knowledge/confidence of users
    Reliance on status-quo
    Range of applications
    …..
    Fit for purpose
    Reliability - Quality Assurance
    Value for money

## Slide 7: Questionnaire
Small questionnaire to solicit opinion and collect information on the state-of-the-art (and future need) for QA (validation/verification) at all stages of “data product” production – split by discipline (land, ocean, atmosphere) and focussed on application need
    Data collection
    Data correction
    Data processing
As perceived by: end users, “added value providers” , data collectors
Seek to collect information/references on cal/val plans and methods
Identify critical areas for improvement, their interdependence, and if possible quantify requirement to meet application need
Identify “best practise” within and between disciplines
Raise profile of QA issues
http://www.npl.co.uk/optical_radiation/gmessurvey
      >1000 hits within 1 week !

## Slide 9: Validated data products on a project by project basis – ISO 17025?
Pre-flight
  User specification
  Instrument build compliance
  Calibration?
Post-launch
  In-flight checks
  Ground “Truth” comparison
  Inter-sensor cross calibration
Processed data released
  “validated”
  Uncertainty?

## Slide 10: ValDEOS – Integration of the European Infrastructure to validate Earth Observation Data (EOI for Network of excellence to FP 6)
Requirement
- Needed to underpin user confidence in EO data – Operational
services of GMES require reliable Quality Assured Data
- Applications and high level data products rely on combination of data from
many sources – in-situ and multi-satellites
accuracy and thus traceability must be known and consistent
- European research effort often targeted on specific missions
- Community recognises the need (76 participants indicated interest in initial
consultation)
- QA needs to include full data product process – data collection, data correction, data processing

## Slide 11: Initial thoughts on activities
Build on successes of Ocean community for Land
  Common calibration procedures/protocols
  Comparisons
  Corrections and processing algorithms
Coordinate R&D on algorithms encouraging commonality of some outputs for compatibility
  - Atmospheric corrections
  - BRDF
  - Scaling of local to global
Encourage and organise comparisons – measurements and algorithms
Establish coordinated spectral libraries
Coordinate equipment loans, field campaigns, long-term sites etc
Improve traceability and consistency of evaluation/presentation of uncertainties
Establish a Web home for exchange of information, database of references, “best practise” guides, Training packages
Establish network with meetings, working groups to define protocols, build a training programme to educate “users” in the basics.

## Slide 12: TRUTHS overview
Satellite based mission to make SI traceable measurements of solar radiation incident on and reflected from the Earth and to transfer its calibration accuracy to other satellite based EO instruments.

## Slide 13: Mission objective: to provide for the first time, directly traceable measurements of solar radiation incident on, and reflected from, the Earth with unprecedented accuracy in SI units”.
Establish a set of reference sites and targets (Land, Water, Sun and Moon) to act as calibration standards for next generation EO sensors.
Removes bias and uncertainty caused by ground calibration/storage/launch by performing spectral calibration of instrumentation in-flight directly against primary standard i.e. establishing true “traceability”.
Measure Earth hyper-spectral radiance (400 – 2500 nm) with polarisation information at high accuracy (0.1%) at 20 m ground resolution.
Simultaneously compare, ground, aircraft and space based measurements of spectral radiance/reflectance to improve accuracy and reliability of atmospheric radiative transfer code.
Determine Total Solar Irradiance (TSI) and Solar Spectral Irradiance (SSI) and their variance with uncertainties of < 0.01 and 0.1% respectively
To provide the tools to generate unequivocal data to allow policy makers to make decisions and take actions on climate change with confidence.

## Slide 14
Primary standard lamp
Working standard lamp
Cal Lab Primary lamp
Cal Lab working std Lamp
User Cal Lamp
User Instrument
Spectroradiometer
Spectroradiometer
Spectroradiometer
Spectroradiometer
Fundamental constants (SI)
Primary standard cryogenic radiometer
Laser
Cal interval ~100nm
Laser
Cal interval ~0.1 nm
Photodiode
(spectral responsivity
Filter Radiometer
Radiance Temperature
Ultra High Temperature Black Body (3500 K)
Radiance continuum
(Planck)
Spectroradiometer
(multi-band filter radiometer
Spectral Radiance/Irradiance
calibrations
LAND
OCEAN
ATMOSPHERE
Satellite Pre-flight
Calibration
Traceability ??
Satellite In-flight
Calibration
Data products
Atmosphere/
Model
Vicarious
Lamp
Solar illuminated Diffuser

## Slide 15: TRUTHS Traceability
Calibration drift, spectral and gain, removed by performing calibrations in space directly against a primary standard using terrestrial methodologies adapted for space.

## Slide 16: Transfer of calibration to global EO missions
Establishment of network Earth based Reference test sites e.g. GIANTS
    E.g Railroad Valley, Libyan Desert, Antarctica etc
    Sites to be characterised by field studies
    Instrumented with remotely controllable/readable monitors
    Calibration coefficients updated regularly by TRUTHS satellite
    Data accessible over WWW to allow reprocessing to suit individual satellite footprints and spectral characteristics
Establishment of reference data for Sun and Moon.
Archived data reprocessable to improve historical reference.
    Many in-flight sensors have the resolution, dynamic range, stability and viewed same desert targets thus allow update of calibration
In-orbit Comparison of solar viewing instruments e.g SORCE.
    Link to VIRGO of SOHO.
Notes: Establishment of reference data for Sun and Moon
In-orbit Comparison of solar viewing instruments e.g SORCE.
    Link to VIRGO of SOHO
Establishment of network Earth based Reference test sites.
    E.g Railroad Valley, Libyan Desert, Antarctica etc
    Sites to be characterised by field studies
    Instrumented with remotely controllable/readable monitors
    Calibration coefficients updated regularly by TRUTHS satellite
    Data accessible over WWW to allow reprocessing to suit individual satellite footprints and spectral characteristics
Archived data reprocessable to improve historical reference
    Many in-flight sensors have the resolution, dynamic range and stability to allow update of calibration.

## Slide 17: Summary
TRUTHS “in-flight calibration laboratory” removes uncertainty due to storage,
launch and degradation and its mission provides this benefit, together with SI
traceability, to all other EO optical sensors.
Set of SI traceable reference targets: Sun, Moon, network of ground sites
Utilises terrestrially implemented techniques and technology
- In-flight calibration concept applicable to other missions
Order of magnitude improvement in measurement accuracy
Baseline for detection of climate change
Quality Assure data used by ‘decision makers’ and improve synergy between sensors
    Tools to audit Kyoto & underpin GMES initiative
Identify the polluters
Improved algorithms to allow quantitative measurement of bio-physical products
Provide data to improve understanding of natural solar induced variation on climate and compare with anthropogenic effects.
The step change reduction in uncertainty and spin-off benefits is analogous to that obtained
in NMIs when cryogenic radiometers were introduced in 1980s
Contact: Nigel.Fox@NPL.CO.UK

## Slide 18: TRUTHS : - Status
Not selected in opportunities call – reviewers conclusion:-
  Accept mission as a technical solution capable of achieving high accuracy radiances
  Science case not made clear in proposal
      Who needs more accurate data?
      Is radiometric accuracy limitation?
Way forward:
  Increase awareness
  Develop case studies to demonstrate benefit of high accuracy
      Ability to transfer calibration
  Make clear concept can be adopted within other missions
      In-flight calibration
      Reference targets as transfer for others
  Keep open opportunities
  Review / simplify capabilities