## Slide 1
SAR Subgroup’s report to WGCV-21
Masanobu Shimada
JAXA, EORC
Activity in 2003
11th workshop in Montreal, Canada hosted by CSA
Action items Status
Activity in 2004
    12th workshop in Ulm, Germany hosted by ESA/ESTEC

## Slide 2
SAR subgroup
Mission to foster high-quality synthetic aperture radar imagery from airborne and spaceborne systems through precision calibration in radiometry, phase, and geometry, and validation of high level products
Objectives
Act as a forum for international technical interchange on the evolving methodologies, techniques, and equipment of SAR calibration and validation.
To determine standard definitions and calibration-validation requirements for synthetics aperture radar imaging systems.
To support changes in CEOS formats and user products as appropriate.
To facilitate international cooperative programs in the calibration and validation of SAR systems.
To educate the SAR community
Action plans
Annual meeting
Set up standard cal/val sites -> inter-sensor comparison
Calibration accuracy requirement for Polarimetry >2003

## Slide 3
Global warming
Deforestation in Amazon
Biomass estimation
JERS-1 SAR Rondonia, NASDA
Pol-In-SAR, S. Cloude
0

## Slide 4
Topics will include:
*Next Generation SAR Systems
*New SAR Missions
*Innovative SAR Concepts
*Antennas, T/R Modules, Phased Arrays, On-board Processing
*Polarimetry and Interferometry
*Signal Processing Techniques
*SAR User Requirements
*SAR Polarimetric Calibration
*Validation
*SAR Applications
Advanced SAR Workshop 2003 jointly with CEOS Working Group on Calibration and Validation (WGCV) – SAR Workshop 2003.
Time and Location June 25, 26 and 27, 2003
at the Canadian Space Agency's Conference Centre in Saint-Hubert, Quebec.
Co-Chairs
General Chairmen: Masanobu Shimada (NASDA) , Guy Séguin (CSA)
Organizing Committee P.W. Vachon, R. Touzi, R. Hawkins (CCRS) , R. Girard, M. Farhat, S. Srivastava (CSA)
Scientific Committee
Bamler, Richard DLR Germany Boerner, Wolfgang UIC-Chicago USA
Cumming, Ian UBC Canada Gray, Laurence CCRS Canada
James, Kenny MDA Canada Luscombe, Tony MDA Canada
Martins-Camelo, Luis EMS Canada Souyris, Jean-Claude CNES France
Massonnet, Didier CNES France Riegger, Sebastian Astrium Germany
Wood, Peter EMS Canada
Calendar of Events
First Call for Abstracts January 2003
Second Call February 2003
Deadline for Abstract Submission April 1, 2003
Notification of Acceptance April 15, 2003
Presentation Material for Proceedings June 18, 2003
Workshop June 25-27, 2003
Paper for Proceedings August 31, 2003

## Slide 5
Publication
SAR CAL/VAL 10th workshop in London made available by CD-ROM

## Slide 6
2003 activity
Joint workshop between Atelier ASAR workshop 2003 and 11th CEOS SAR CAL/VAL workshop 2003 has been held at and hosted by Canadian Space Agency, St-Hubert, Montreal, CA between June 25 and 27 2003.
There were almost 120 participants and 99 presentations.
There were fourteen fascinating sessions, i.e., 1) keynote talks, 2) SAR missions, 3) Pol-In-SAR processing and applications, 4) Pol-Int-Calibration, 5) SAR calibration, 6) SAR technologies, 7) SAR applications, 8) Multiple Aperture/Split aperture/MTI, 9) Amazon Calibration, 10) SAR interferometry, 11) SAR processing and simulation, 12) Scattering models, Scatterers, and ground SAR, 13) Marine Surveillance, and 14) SAR concepts and techniques.
As a final, we had some recommendations on using the Amazon rain forest for the standard reference target for C and L band SAR, which will be provided to the CEOS CAL/VAL plenary. We had a great deal of the results on the calibration and validation for the SAR system. Next meeting will be considered to be at ESTEC in May 2004.

## Slide 7
Action items:
SAR subgroup to request WGISS to provide task team for Pol-In-SAR data formatting. ->In Toulouse workshop(1999), it was recommended that SLC is the only data for preserving phase for interferometry, compressed data is necessary for polarimetry. -> In Montreal(2003), We have discussed this issue. Two candidates are listed, SLC and the other (preserving phase). We will reopen the discussion in 2004.
The WGCV SAR subgroup should set up calibration and validation reference sites (to include both natural and man made targets) :In Montreal, we have confirmed the Amazon’s stability for some test sites, 1 in Radarsat, 1 in JERS-1, and whole Amazon in ERS). We will list the possible sites in 2004 meeting.
Space Agencies should continue to improve the quality of single and full polarization SAR data by technical exchange of information on the development of SAR calibration and imaging algorithms and techniques. >This action is being conducted through the several international science workshops and CEOS SAR CAL/VAL workshop. Ongoing.

## Slide 8
The stability of the Amazon rainforest should be systematically studied as a function of incidence angle, frequency and polarization using existing data sets including SEASAT, ERS, JERS, RADARSAT and TRMM and emerging data sets from ENVISAT, TerraSAR and RADARSAT-2. Funding to complete the study should be solicited at the CEOS Plenary.-> > In Montreal, most of the SAR data were analyzed and reached to a conclusion that the Amazon can be the very stable target both for C and L band SARs. (finished)
Next meeting of the SAR subgroup should focus on the problem of full polarimetric SAR calibration, both establishing requirements and techniques.
> Engineering requirement has been almost (not fully) established. The scientific requirement and techniques will be discussed in future.
Space agencies should ensure that calibration processes for SAR are traceable to the primary standards.-> ongoing.

## Slide 9
Amazon Calibration: Summary(1/3)
Chair: E Attema, ESA/ESTEC
This session consisted of five full papers as follows:
1. M. Shimada, "Long-term stability of L-band Normalized RCS of Amazon rain forest using the JERS-1 SAR", describes a long-term stability of L-band SAR data observed for Amazon and its applicability as a calibration reference target. We evaluated the 139 JERS-1 SAR images acquired for the south west Amazon over six years and a half (1992-1998), including wet and dry seasons, and obtained that each wet and dry season data is very stable with mean values of -7.08 dB and -6.81 dB and standard deviations of 0.20 dB and 0.18 dB, with a seasonal difference of 0.27 dB. It can be concluded that the Amazon data is well-stabilized reference target for the calibration. Questions are raised if the faraday rotations affected on this analysis. It seems that the data shows no faraday effect appeared however a test site should be selected from the equatorial area to reduce this effect.
2. A. P. Luscombe, "Radiometric Stability of RADARSAT-1 Images of the Amazon Calibration Site". As part of the baseline calibration of RADARSAT-1, a restricted region of the Amazon rainforest is regularly imaged and a large archive of data are available since launch in 1995. By concentrating on variations observed in the mean rainforest backscattered power over the scene, it was demonstrated that low level (0.3 dB) seasonal and dawn/dusk variations exist in RADARSAT data. This trend has been partially obscured previously by calibration changes in the instrument. The data set demonstrates that the mean level from a scene of this region of the Amazon is consistent to less than 0.2 dB (s.d.) for any of the RADARSAT-1 beams when compensation is applied for the systematic variations. This includes both backscatter changes and changes to the radar system and beam pattern.

## Slide 10
Amazon Calibration: Summary (2/3)
3. A. P. Luscombe, "Use of Amazon Imagery for Polarimetric Calibration". This paper outlined the principles for a scheme to perform full polarimetric calibration of the RADARSAT-2 SAR using assumptions about the backscatter properties of Amazon rainforest. Justification of the procedures and assumptions were made by analysis of a series of SIR-C data takes. This analysis demonstrated that all parameters required for polarimetric calibration can be estimated effectively from the ensemble statistics (covariance matrices) of the four-channel (HH, VV, HV, VH) data. The resulting estimates were obtained as functions of elevation angle across the beam, and are extremely consistent for independent data sets within one pass, and also very close to data determined by JPL using calibration targets.
4. M. Satake and H. Hanado " (presented by RK Hawkins) Effect of water drops on backscattering coefficients of rain forest observed by Ku-band space-borne radar". Observations beginning in November 1997 from the Ku-band scatterometer on TRMM have allowed a study of backscattering properties of the rainforest including the Amazon. These observations for incidence angles below 17 degrees have shown that diurnal variations exist in the backscatter on the order of 0.5 dB with some seasonal dependence as well. A maximum was observed in the early morning when accompanying temperature information suggests that dew droplets on the leaves would be formed. Modeling at Ku-band for this effect substantiated this explanation, but did not seem to support similar effects at longer wavelengths.

## Slide 11
Amazon Calibration: Summary (3/3)
5. R. Crapolicchio and P. Lecomte (presented by B. Rosich) "On the stability of Amazon rainforest backscattering during the ERS-2 Scatterometer mission lifetime". ERS-2 Scatterometer data acquired over the Amazon rain forest for more than 7 years provides a valuable time series of mean gamma measurements. The mean gamma values have been compensated for changes introduced in the processor calibration or on the instrument. The results clearly show an annual γ variation with a peak-to-peak value around 0.15 dB. A more detailed analysis indicates also a diurnal variation, with an average difference of 0.1 dB between ascending (about 03:00 a.m.) and descending (about 14:00 p.m.) acquisitions.
The discussion following the presentations was lively and focused on need for manmade targets when the stability of the Amazon seemed to be high and variations quantified and even predictable. Data from storm cells, weather fronts, and river basins can affect results but procedures to deal with these variations appear to be feasible with sufficient spatial and temporal averaging. Nevertheless many new programs will continue to use the Amazon for in-orbit antenna pattern verification only and the chair stressed the need for manmade standards to supplement and validate results from this important natural target.

## Slide 12
Wet Season images (Jan. - June)
illumination
Satellite
432-313
433-315

## Slide 13
Dry Season images (July - Dec.)
illumination
Satellite
432-313
433-315

## Slide 14
Samples of NRCS (Gamma-Naught) and incidence angles
Incidence angle
NRCS

## Slide 15
Temporal dependency of averaged sigma-naught (139 points)
Total Data
Dry/Wet Season
Month after Nov. 1992
Month after Nov. 1992

## Slide 16
Proposed calibration area for PAL SAR
UL -7.068,-72.100
UR -7.182,-70.265
LL -10.668,-72.892
LR -10.786,-71.051
JERS-1 SAR HH polarization

## Slide 17
Calibration requirements for the polarimetric SAR
System stability (short and long term):?
Cross-Talk < -35 dB
Channel amplitude imbalance: 0.2 dB (soil moisture)
Channel-phase: 2- 5
Channel registration <0.1 pixel ?
Requirements should be expressed in term of NESZ as a function of the frequency
X: -23 dB?
C: -25 dB?
L: -30 dB?
P: -35 dB?
L-band Faraday rotation correction requirement: 2.5 degree (it is accepted that C-band Faraday rotation of 2.5 is not significant)

## Slide 18
Recommendation
Noting that the Amazon rainforest has been well studied and is currently the best natural target for SAR calibration. Statistical evaluation of the Amazon rainforest SAR data sets acquired for more than five years shows that C and L band SAR data (ERS-2 Scatterometer data for AMI, Radarsat SAR, JERS-1 SAR) are ultimately stable with the absolute backscattering coefficients (sigma-naught or gamma-naught), which vary with frequency, polarization, and incidence angle(for sigma-naught and not for gamma-naught), and standard deviation of less than 0.3 dB, which includes diurnal and seasonal variation (CEOS SAR CAL/VAL 11th workshop report to be published Dec 2003).
CEOS CAL/VAL recommends that the Amazon rainforest area be used as one of the calibration transfer standards.
Amazon rainforest must be regularly measured to maintain its traceability to the internationally agreed standards.

## Slide 19
1. Geometry
2.Radiometry
3.Calibration Methodology
4.Polarimetry and Interferometry
–Faraday rotation
–Across-track
–Differential
–Along-track/MTI
5.Land
–Forestry
–Crop monitoring
–Land use
6.Ocean
–Waves
–Wind speed/direction
7.Atmosphere
–Water vapour
–Precipitation
8.Instrument Calibration Concepts
2004, May 27 and 28, Ulm, Germany
contact:Christopher Buck/ESTEC
Schedule
15 January 2004:Deadline for submission of abstracts
29 February 2004:All authors notified
15 March 2004:Issue of preliminary programme
27 May 2004Deadline for submission of final papers
27-28 May 2004:CEOS SAR Workshop 2004
30 June 2004:Distribution of proceedings to all participants