## Slide 1
Country report from Japan
Masanobu Shimada
EORC/JAXA
(Earth Observation Research and application Center)
Oct. 15-17 2003
CEOS CAL/VAL Plenary in China

## Slide 2
ALOS performance, view on orbit
ﾌｪｰｽﾞﾄﾞｱﾚｲ方式
Lﾊﾞﾝﾄﾞ合成開口ﾚｰﾀﾞ
（PALSAR）
ﾊﾟﾝｸﾛﾏﾁｯｸ
立体視ｾﾝｻ
（PRISM）
高性能可視近赤外
放射計２型
（AVNIR-2）
太陽電池パドル
（PDL）
データ中継衛星通信部
（DRC）
恒星センサ
（STT）
GPSアンテナ
衛星進行
方向
地球方向
Orbit sun-synchronous
Local Time at DN 10:30 ± 15min.
Altitude 691.65km
Inclination 98.16 degrees
Revolutions per day 14+27/46
Period 98.7 minutes
Longitude Repeatability +/-2.5km Equator
Max. operation period 70 minutes
Data collection 1 DRTS+DT
Yaw steering OFF
Attitude error each axis 2.0e-4°(det),
0.1°(maintain)
Weight 4000 Kg

## Slide 3
Project Schedule
Before launch CAL. | Initial mission check | Initial CAL. | CAL.
3mos
5mon
Launch
L+９
Data release
Data release(limited for PI
, PDF for general）
Ver.0
Ver.1
Ver.2
Ver.n
EOC software version
Ver.0
Ver.1
Ver.n
EORC software version
1 year after
Launch is later than Sept. 10, 2004
CAL/VAL review
march 20 2003
CAL/VAL review
DEC 2003
PI meeting (Jan. 2004)

## Slide 4
Basic Operation
scenario
Dual HH/HV 34.3
Dual HH/HV 43.4
Single HH 34.3
SCANSAR 5 scan
Dual HH/HV 21
POL-INSAR 21
CAL phase
Pol - InSAR
a year
Dual 34
Dual 43
Ascending
Dual 21
Single 34
SCANSAR

## Slide 5
 | ARC | PARC
Frequency band | 1256～1284MHz | 1256～1284MHz
Off nadir angle | 9.9～50.8° | 9.9～50.8°
RCS | 15～60dBm2 | 15～60dBm2
RCS stability | <±0.1dB | <±0.1dB
ALOS tracking | Yes(program tracking) | Yes(program tracking)
Max. Rec. power | -44.5dBm | -44.5dBm
Max. trans. Power | 22.5dBm | 22.5dBm
temperature range | -10～＋50℃ | -10～＋50℃
Humidity range | 35～100%RH | 35～100%RH
Polarimetric Active Radar Calibrator
Single POL.
polarimetry
Polarimetry and single polarization supported.
Remotely controlled for off nadir angle.
High RCS stability using thermally insulated units and ALOS tracking performance.
Wide resistance for temperature and humidity
PARC mode prepares the H and V phase difference

## Slide 6
Calibration sites
Institute Type Numbers Locations
NASDA PARC 4 Tsukuba
CR 2+2 Tomakomai
ERSDAC PARC 3 TBD
CR 2 TBD
CNES/ESA CR 10 Germany,Swiss
ARC 1
AU-ADN CR 2 TBD
ASF/NOAA CR 5 Alaska
Others ARC/CR 3+10
NASDA Forest １ Amazon
Sites will be established collaborating with the institutes.

## Slide 7: Along path GCP’s #1 for PRISM
East Japan
Tsukuba
Tomakomai
691km
Iwate
Utsunomiya
To evaluate the same-time performance of the three radiometers, three test sites were established within a same orbit :
Tomakomai : 70x10km/5km > 42points
Iwate : 70x25km/5km > 69 points
and GSI/GEONET stations (4+4 points).
We will setup the third site in Utsunomiya City.
Iwate
Tomakomai
25km
70km
70km
10km

## Slide 8: PRISM “Triplet Matching” Algorithm
Evaluation of matching accuracy using 120 selected points
Max. Min. RMS (pixel)
Nadir – Forward : 1.291 -1.321 0.390
Nadir – Backward : 1.081 -1.521 0.409
“Core” to generate DEM
- PRISM simulated images from the Three Line Scanner (TLS) onboard a helicopter.
One dimensional search along the semi-epipolar line
Triplet matching by aerial-based correlation
Automatic window size optimization
TLS-nadir image
Generated DEM
Evaluation point distribution
* Reference: J. Takaku et al., IGARSS 2003.

## Slide 9: PRISM “Image Quality Evaluation” – S/N, MTF, JPEG
Stagger correction using AVNIR/Pan.
a) Input (aerial photo, 0.32m) b) MTF=0.2 (2.5m) c) JPEG compression (1/4.5)
▼
Example of simulated images to evaluate image quality.
(Spatial resolution, MTF, S/N, and JPEG compression.)
> Algorithms evaluation and tool
development
Radiometric Cal., image quality evaluation:
Current satellite image and aerial photo
Geometric Cal.:
Current high-resolution satellite image,
aerial photo + GCP
Modification for PRISM.

## Slide 10
Pi-SAR
Frequency 1.275e9 Hz Band width 50 MHz
Sampling freq. 61.275MHz
Height 6~12Km
Image swath <=15Km
AD(I/Q) 8 bits
 (R) slant 3 m
 (A) 4look 3.2 m
0 1.1 dB
NE0 -30 dB
Inci. Angle 10~60
Polarimetry Full
 10s
Pt 3.5KW
Beam width(A) 8.4 degrees
Sigma-SAR processor
R:HH,G:HV,B:VV
Tottori Dune
Ｎ

## Slide 11
2002
Nov. 7
Tomakomai
2002
June 13
Hatoyama

## Slide 12
Forest monitoring using L band SAR
made already
planned

## Slide 13
Mosaic of Southeast Asia using the JERS-1 SAR images
2000 images (39 paths) were used.
Data were mainly acquired in the winter season (January and February) of 1997.
CD-ROMs are available Oct. 2003!