## Slide 1
Report of Australian Activities to
the CEOS WGCV#21
Ian Barton
CSIRO Marine Research
Presentation to CEOS WGCV#21
Hosted by CSSAR/CAS
Friendship Hotel, Beijing, PRC

## Slide 2
Structure of Report
1. Topex/JASON: Altimeter SSH Validation
2. ENVISAT: AATSR LST Validation
AATSR/GLI/MODIS: SST Validation
ENVISAT: MERIS ocean colour validation
SeaHARRE

## Slide 3
2. 2. Validation of Land Surface
Temperature (LST)
• Three land sites on the Australian continent are maintained by
Dr Fred Prata of CSIRO Atmospheric Research
• Each site makes continuous measurements of many parameters
including LST
• Measurements are made at several locations within a 1 km2
area and are transmitted to a central location.
• Data have been used to confirm the accuracy of the LST
derived from AATSR measurements

## Slide 4
Hay
Alice
Springs
Thangoo
LST Validation sites

## Slide 5
ATSR-2 image of the Uardry field site

## Slide 6
Albedo measurements at Uardry, NSW

## Slide 7
Amburla Field Site, Alice Springs NorthernTerritory

## Slide 8: 3. RV Southern Surveyor – Voyage SS0403
Cairns to Darwin, 9 May – 10 June
DATA SETS –
DAR011 most days 0800-1200 & 2000-2400
EST
Thermosalinograph – complete record
Navigation - full record from GPS
Met data – Licor, wind & ship velocity, Ta, Q

## Slide 11: Satellite data sets
Total Ship match-ups
NOAA-12 AVHRR 49 36
NOAA-16 AVHRR 47 42
TERRA MODIS 47 25
AQUA MODIS 47 28
AMSR-E 30 8
ADEOS-2 GLI 40 24
ERS-2 ATSR-2 7 4
ENVISAT AATSR 18 4

## Slide 12
Gulf of Carpentaria
GLI 25 May 2003

## Slide 13
28

## Slide 14
28
AATSR 28 May Night

## Slide 16: Satellite-derived SST validation against ship data
Bulk SST from the ship thermosalinograph is available for the entire cruise
DAR measurements have been corrected for surface emissivity and averaged into 1-minute intervals
AVHRR x 2, MODIS, MYDIS, AMSRE, and GLI have all been compared with Bulk SST
AATSR and ATSR-2 have been compared with radiometric SST from the DAR011 radiometer
A bias and standard deviation is given for each instrument.

## Slide 17: Important factors
GLI - Using the latest SST algorithms provided by Kawamura
- De-striping factors are all unity
- Bow-tie effects have been removed in L1B data
MODIS & MYDIS -
- Bow–tie effects removed when re-mapped
- Algorithms not the latest version
AATSR -
- Uses the official ESA algorithms
- Offsets of 1 pixel, 1 line often required in collocation

## Slide 18
TERRA MODIS
Bias 0.53 Std Dev 0.63
AQUA MYDIS
Bias 0.76 Std Dev 0.65
NOAA-12 AVHRR
Bias -0.42 Std Dev 0.77
NOAA-16 AVHRR
Bias 0.07 Std Dev 0.51

## Slide 19
AQUA AMSR-E
Bias 0.05 Std Dev 0.67
ADEOS-2 GLI
Bias 0.10 Std Dev 0.25

## Slide 20
ERS-2 ATSR-2 Mean diff = -0.09
ENVISAT AATSR Mean diff = -0.12

## Slide 21: Satellite image data inter-comparisons
All infrared satellite data have been re-mapped onto a 0.01 x 0.01 degree latitude-longitude grid
AMSR-E data at 0.25 degree resolution have been duplicated to provide a value at each 0.01 degree grid point
Image areas of 2.5 x 2.5 degrees in latitude and longitude have been compared
Histograms of SST differences from pairs of instruments have been plotted
In some images an offset has been subtracted from the image data for image comparisons

## Slide 22
28 May 2003
Night - EST
AVHRR – 0300
AATSR – 2200
MODIS – 2230
AMSRE – 0200
15.5–17.0 OS
138.5–141.0 OE

## Slide 23
AVHRR – AATSR = 0.2 OC
AVHRR – MODIS = -1.5 OC
AVHRR – AMSRE = -1.2 OC

## Slide 24
25 May 2003
Night - EST
AVHRR – 0330
AATSR – 2200
MYDIS – 0200
GLI – 2230
15.5–17.0 OS
139.5–142.0 OE

## Slide 25
AVHRR – AATSR = 0.2 OC
AVHRR – MYDIS = -1.5 OC
AVHRR – GLI = -0.3 OC

## Slide 26
7 June 2003
Day - EST
AVHRR – 1500
MODIS – 1030
GLI – 1030
AMSRE – 1400
15.5–17.0 OS
138.5–141.0 OE

## Slide 27
AVHRR – MODIS = -0.8 OC
AVHRR – GLI = 0.0 OC
AVHRR – AMSRE = 0.5 OC

## Slide 28: Summary
Navigation of all instruments is very good
AVHRR, AATSR, and GLI show excellent agreement both with each other and with ship data
MODIS instruments look to be too warm by a degree or so
AMSR-E has shown a day/night difference –needs further checking
GLI shows striping effects due to detector array as well as some slowly varying electronic effect
AVHRR – NOAA-12 is inferior to NOAA-16

## Slide 29
Perth to Rottnest Island ferry
• Radiometer based on a TASCO radiometer
• Calibration using a portable black body target
• Ferry operates 4 to 6 times daily
• Bulk SST measured with water intake PRT
• Position logged with GPS
• Sky radiance from shore-mounted radiometer

## Slide 34
Perth ferry data analysis
Eight months of data - October 2002 to May 2003
1134 ferry transects mainly from Hillarys Marina to
Rottnest Island – but some whale-watching trips.
Bulk SST from the Intake PRT. No radiometer data
Transects split into five longitude zones between
Hillarys and Rottnest, and the PRT data were averaged
in each of these zones for each transect. Usually 4 or 5
one-minute readings in each zone. First and last zone
discarded so there are usually three data points for each
transect.

## Slide 35
All day

## Slide 36
DT < 2 hr

## Slide 37
dT < 1 hr

## Slide 38: Ferry data analysis – other satellites
A full Perth ferry data set has been sent to -
University of Miami for MODIS SST validation
(both Terra and Aqua)
JAXA for GLI SST validation

## Slide 39: 4. Ocean colour calibration/validation
Australian MERIS validation project (AO595)
MERIS Cal/Val will be reported to the MAVT-2003 meeting in Frascati, Italy next week

## Slide 40: Measurement locations
The optical and biogeochemical properties of Australian waters were measured during 5 field campaigns in 2002-2003.
Perth (West Australia)
Hobart (Tasmania)
Brisbane (Queensland)
Great Barrier Reef (Queensland) – 2 sites

## Slide 41: Optical measurements
Water-leaving reflectances –
in situ profiling spectroradiometers (TRIOS Ramses or HOBILABS Hydrorad-2).
Inherent optical properties (spectral absorption, scattering and backscattering coefficients) –
- in situ WETLabs ac9 and HOBILabs Hydroscat-6.

## Slide 42: MERIS match-ups
Where MERIS match-up data are available
MERIS L2 optical water quality and geophysical products are compared to the in situ measurements of –
- water leaving reflectances,
- chlorophyll a,
- TSM and
- CDOM absorption.

## Slide 43: 5. SeaHARRE
Australian scientists are participating in the Second SeaWiFS HPLC Analysis Round-Robin Experiment (SeaHARRE-II). Data samples were delivered to CSIRO in Hobart and were processed during February 2003. The results will be compared with those from seven other international laboratories analyzing the data samples. A meeting to discuss final results will be held in France at the end of 2003.