## Slide 1: USGS Report to the 23rd CEOS/WGCV Plenary
David Meyer, SAIC
US Geological Survey National Center for Earth Resource Observations and Science
March 7-10, 2005
CONAE CETT – Cordoba, Argentina

## Slide 2: Items
Landsats 5, 7
  landsat.usgs.gov
EO-1 relevance to Landsat Data Continuity
  eo1.usgs.gov
  ldcm.usgs.gov
Land Process Distributed Active Archive Center
  lpdaac.usgs.gov
Commerical providers and Cal/Val
  remotesensing.usgs.gov/commercial_activities.html (site under construction)

## Slide 3: Landsat 5 Spacecraft Status and Configuration
HIGH GAIN ANTENNA
GPS ANTENNA
PROPULSION MODULE
ACS MODULE
POWER MODULE
(2) OMNI ANTENNA
THEMATIC MAPPER
MULTI- SPECTRAL SCANNER
S-BAND ANTENNA
X-BAND ANTENNA
SUN SENSORS
SOLAR ARRAY PANELS
WIDEBAND COMMUNICATIONS MODULE
05/2004 Battery #1 relay anomaly
3/84 Primary Thruster D failure
8/85 Transmitter A failure
10/94 Power Supply 1 failure
8/95 Band 4 failure
8/87 Prime X-band failure (OCP)
11/92 Earth Sensor 1 failure
2/02 Earth Sensor 2 failure
Not Operational
7/03 FHST #1 Degradation Failure
8/28 Redundant X-band Anomaly (OCP)
4/04 Fine Sun Sensor in control loop

## Slide 4: Landsat 5 Summary
Fixed Head Star Tracker #1 Anomaly
  Start Tracker 1 was taken out of the OBC loop on 08/04/2003
Battery 1 temperature started to increase in mid 2003
New Battery management strategy was introduced in April 2004
Fine Sun Sensor was added to the control loop to improve the fine pointing mode
Traveling Wave Tube Amplifier anomaly
Battery #1 relay malfunctioned
  Declared non operational on 05/21/2004
  Landsat 5 power is sufficient with additional margin at all times
Implementation to capture more than 18 to 22 hours of telemetry play back on a daily basis to LMOC continued.
Fine Sun Sensor (FSS) and tracker # 2 are configured to be used for the control loop
Problem with primary motor/clutch for solar array; switched to redundant with no effect on continued mission
Current Battery Charge Investigation
  The investigation was initiated due to low C/D ratio to Battery 2 and 3
  All indication suggests that the Battery 2 & 3 are healthy
  Noise in the charge current was discovered during investigation
Planned Ku-band TWTA Recovery Effort
Planned Star tracker / Master Catalog Update
Estimated end of mission: December 2009 based on remaining fuel and assuming 9:30AM MLT crossing minimum criteria

## Slide 5: Landsat 5 Definitive Ephemeris
New capability to improve the data calibration
  Definitive ephemeris generated from available satellite telemetry range data
  Initial indications are that definitive ephemeris improves overall geolocation accuracy and reduces outliers
The definitive ephemeris data from 2001 to present is available on FTP server (http://landsat.usgs.gov/ephemeris/index.php)

## Slide 6: Landsat 7 Summary
.
SLC Failure
  (gap-filled products:http://landsat.usgs.gov/gapfilled_off2off_release.php)
Reaction control system line #4 thermostat failure. No mission impact due to system architecture
Gyro #3 shut down due to anomalous gyro telemetry
ETM+ usage increased from 250 scenes/day to 300 scenes/day
Begin collection of Three Axis Magnetometer (TAM) data using new flight software module. Data being used to validate use of TAMs to generate spacecraft attitude change rates. This will be used in support of “virtual” gyro procedures being developed to control the spacecraft with the single gyro.
Estimated end of mission: January 2011 based on remaining fuel and assuming 9:30AM MLT crossing minimum criteria

## Slide 7: EO-1 ALI Image Assessment System (ALIAS)
Major assumptions in the development of ALIAS
  LDCM Operational Land Imager (OLI) will be similar to ALI “push broom” design
  NASA and USGS will remain as partners in LDCM Cal/Val
Builds on successes of Landsat 7 IAS and EO-1 Science Validation Team (SVT)
Goals of the ALIAS prototype
  Mitigate the risk associated with losing key knowledge, experience, and personnel before the LDCM mission fully commences
  Generate an Image Assessment System prototype based on the algorithms and software used for EO-1 ALI and Landsat 7 ETM+ analyses
Partners
  USGS/EROS
  NASA/GSFC
  MIT/Lincoln Laboratories
  South Dakota State University

## Slide 8: ALIAS: EO-1 & LDCM Synergies
EO-1 ALI Benefits
  Radiometric & Geometric algorithms & CPF used in EO-1 Product Generation
    ALI L1Gs product released in December 2004
    ALI L1Gt product planned for Spring 2005
  EO-1 user community benefits greatly, and ALIAS team benefits from external validation & user feedback of corrected products
LDCM Benefits
  ALI data and ALIAS prototype allow the LDCM Project to minimize risks of new technology and ground processing algorithms
  Stimulates early research and development of needed calibration and correction algorithms
  Trending database design and evaluation (database to grow to ~5TB)
  Collaborative (GSFC & EROS) workflow simulation & validation
  Prepares instrument team for acceptance testing and On-orbit Initialization and Verification (OIV)

## Slide 9: LDCM Update
August 2004 memorandum from Director, Office of Science and Technology Policy, Executive Office of the President states that DoD, Department of the Interior, Department of Commerce, and NASA agree to:
  Transition Landsat measurements to an operational environment on NPOESS
  Plan to incorporate a Landsat sensor on first NPOESS (“C-1”) projected for 12/09 launch
  Further assess options to mitigate risks to data continuity prior to C-1 launch, including a “bridge” mission

## Slide 10: LP DAAC Status: ASTER
ASTER corrections being implemented
  Geometric errors (georeferencing)
    Earth nutation (TBD)
    Earth rotation (0-200m day, 0-700m night)
    Height above sea level (0-500m)
  SWIR cross-talk
    Stray light from band 4 to bands 5&9
  Corrections 1&2 to implemented in Level-1B, corrections 3&4 implemented in Level-2

## Slide 11: MODIS Direct Broadcast
Implemented IMAPP (University of Wisconsin) software for Level-1B processing
Use standard product (MOD03-geolocation) and MRTSwath tool for swath to grid
Implemented MODAPS code for surface reflectance and vegetation indices
Verified surface reflectance from direct broadcast by comparison to standard product (MOD09GHK/MYD09GHK-daily 500m surface reflectance)

## Slide 12: Comparison of MODIS Surface Reflectance EROS Direct Broadcast vs. Standard MODIS Daily 500m for Aqua and Terra

## Slide 13
Comparison of NDVI from NOAA AVHRRand MODIS for developing long term records of terrestrial vegetation dynamics

## Slide 14: Differences in sensor calibration and atmospheric correction must be resolved to enable derivation of consistent metrics related to vegetation phenology
No aerosol corrections have been applied to NOAA AVHRR.
Post-launch calibration of NOAA-17 AVHRR were not yet available.
MODIS QA information should be used to filter for aerosol, clouds, and snow cover.

## Slide 15: Commercial Providers and Cal/Val
USGS serves users having divergent requirements
  Science users
    Land processes/Earth science studies
    Wide range of spatial scales
    Tends to use “transparent” government systems
    Peer review
  Resource management users
    Often have regulatory missions
    Tendency toward finer spatial scales
    Tends to use “intellectual properties” of commercial providers
    USGS historically plays “certification” role (US)
Increasingly, these requirements are merging
  How to maintain transparency required by science when using data provided by commercial providers?

## Slide 16: Commerical Providers and Cal/Val (con’t)
Examples exist for space-borne systems
  SeaWifs, SPOT, Radarsat, Ikonos, Quickbird, Orbimage, DMC
What frameworks exist to incorporate commercial products into a peer-reviewed environment?
  Existing frameworks:
    US: Joint Agency Commercial Imagery Evaluation (JACIE)
    International: WGCV/ISPRS Joint Working Group
  NRC/Space Studies Board Assessments
    Transforming Remote Sensing Data into Information and Applications (NAP 2001)
    Toward New Partnerships In Remote Sensing: Government, the Private Sector, and Earth Science Research (NAP 2002)
    Using Remote Sensing in State and Local Government: Information for Management and Decision Making (NAP 2003)

## Slide 17: Commercial Providers and Cal/Val (con’t)
NRC recommendations
  licensing: negotiate open scientific distribution/reuse
  lessons learned: review of SeaWifs, NASA “data buy”
  access: academics should be able to compete for data
  continuity: seamlessness across new generations of satellites
  archive: negotiate permission for commercial data
  cal/val: partnership agreements to provide relevant info
  standards: metadata, formats, portability
  communication: public sector facilitates during planning phase
  accounting: partnership costs transparent, open to negotiation

## Slide 18: Commercial Providers and Cal/Val (con’t)
How should WGCV address this?
  Review of existing partnerships
    Mission/platform based (e.g., SPOT, Radarsat)
    “data buys” (e.g., NASA)
  Participation by industry
    very different models in different countries for private/public partnership
    who represents “industry”?
  WGCV/ISPRS Joint working group
    Gulfport Workshop & Proceedings
    ongoing activities?