## Slide 1: WGCV-52 SRIX4Veg: Surface Reflectance Inter-comparison eXercise for Vegetation
Valentina Boccia, ESA
Cindy Ong, CSIRO
Agenda Item #2.7
WGCV-52, ESA/ESRIN, Italy
6th June 2023

## Slide 2: FRM4Veg
Slide 2
FRM4Veg = Fiducial Reference Measurements for Vegetation
FRM4Veg is an ESA-funded activity aimed at defining and applying the FRM concept to the vegetation biophysical variables acquired by European satellites, i.e. surface reflectance (SR), fraction of absorbed PAR (fAPAR), and canopy chlorophyll content (CCC).
FRMs have the following properties:
  Documented SI traceability (or conform to international community standards)
  Independent from the satellite geophysical retrieval process
  Accompanied by an uncertainty budget for all instruments and derived measurements
  Adhere to community-agreed, published and openly-available measurement protocols
  Accessible to other researchers allowing independent verification of processing systems

## Slide 3: SRIX4Veg
Slide 3
In the context of the FRM4Veg activity, we developed the SRIX4Veg concept.
SRIX4Veg = Surface Reflectance Inter-comparison eXercise for Vegetation using UAVs
RATIONALE for using UAVs:
Significant interest in UAV-based hyperspectral instruments.
UAVs usage is expected to grow as instruments get lighter, cheaper and easier to use.
UAVs have several advantages when used for validating vegetation biophysical variables:
  Cover a greater area
  Remove site disturbance
  Measure inaccessible sites (water, trees, etc.)
  Complement permanent infrastructure
  Measure complicated sites (mixed pixels, etc.)
Protocols yet to be developed and lots of people are developing different things (some more systematically than others)
BUT

## Slide 4: SRIX4Veg
Slide 4
In the context of the FRM4Veg activity, we developed the SRIX4Veg concept.
SRIX4Veg = Surface Reflectance Inter-comparison eXercise for Vegetation using UAVs
GOAL:
Assessing the variability associated with different teams conducting the same SR validation work with drones and moving towards a community-agreed Protocol to reduce this variability, following the FRM principles.

## Slide 5: SRIX4Veg
Slide 5
Endorsed by:
In collaboration with:
In partnership with:
Project partners:
Funded by:

## Slide 6: SRIX4Veg
Slide 6
1st SRIX4Veg Workshop
28th March 2022
@virtual
SRIX4Veg Field Campaign
with ALL teams
18th – 22nd July 2022
@Las Tiesas (Barrax, Spain)
2nd SRIX4Veg Workshop
23rd – 24th November 2023
@ESA-ESRIN
3 MAIN STEPS:
WE ARE HERE

## Slide 7: SRIX4Veg
Slide 7
1st SRIX4Veg Workshop
28th March 2022
@virtual
SRIX4Veg Field Campaign
with ALL teams
18th – 22nd July 2022
@Las Tiesas (Barrax, Spain)
2nd SRIX4Veg Workshop
23rd – 24th November 2023
@ESA-ESRIN
3 MAIN STEPS:
WE ARE HERE

## Slide 8: SRIX4Veg
Slide 8
1st SRIX4Veg Workshop
28th March 2022
@virtual
1ST STEP:
PREPARATORY WORK before the Workshop:
Definition of a data collection plan based on a draft protocol based on a typical Sentinel-2 overpass.
Setting up of a dedicated webpage for registration to SRIX4Veg and related info & news.
One-to-one meetings with each participating team.
Preparation of all the logistics in view of the SRIX4Veg field campaign (e.g. equipment shipping and storage, potential issues, UAV regulations in Spain, UAV EU licence, UAV insurance, travel and accomodation, helath and safety, etc.).
https://frm4veg.org/srix4veg/

## Slide 9: SRIX4Veg
Slide 9
1st SRIX4Veg Workshop
28th March 2022
@virtual
1ST STEP:
GOALS of the 1st WORKSHOP:
Presentation of the several teams participating in SRIX4Veg.
SRIX4Veg Strategy and Logistics in view of the filed campaign.
Preparatory activities for the field campaign.
Attendance and reporting from the several agencies and institutions supporting SRIX4Veg.

## Slide 10: SRIX4Veg
Slide 10
1st SRIX4Veg Workshop
28th March 2022
@virtual
SRIX4Veg Field Campaign
with ALL teams
18th – 22nd July 2022
@Las Tiesas (Barrax, Spain)
2nd SRIX4Veg Workshop
23rd – 24th November 2023
@ESA-ESRIN
3 MAIN STEPS:
WE ARE HERE
Preparatory work before the Field Campaign:
Collection of the validation strategy plans prepared by each team participating in SRIX4Veg

## Slide 11: SRIX4Veg
Slide 11
2ND Step: SRIX4Veg Field Campaign
FRM criteria | 
1 | Vegetation Type
2 | Representativeness
3 | Extent
4 | Homogeneity
5 | Topography
6 | Weather
7 | Accessibility
8 | Site Maturity
Las Tiesas Experimental Farm, Barrax, Castilla-La Mancha, Spain
(39.054313°, -2.101054°)
NRC
RIT
NERC
NPL
WUR
GFZ
GEO-K
PARTICIPATING
TEAMS

## Slide 12: SRIX4Veg
Slide 12
EXPERIMENT 1: Each team was given a data collection plan based on an initial, draft protocol based on a typical Sentinel-2 overpass.
EXPERIMENT 2: Each team collected data according to their own plans but given the same information
about a satellite overpass.
Area: 60 m x 60 m (consistent with 3 x 3 pixels at 20 m resolution)
Flight lines orientated to the Sentinel-2 orbit inclination: 98.62°
Overlap (80%) increased to get as many pixels at each angle
Speed
Height
Sampling
Optimised to ensure the UAV
can cover the area within the battery limits

## Slide 13: SRIX4Veg
Slide 13
SI
ASD measurements:
Spectralon > Light > Middle > Dark > Spectralon
5 spectrums per location @ 4 locations
Spectralon Panel
Three step grey scale Tarpaulin
11%, 30%, 56%
GNSS
Smart Target
Base station
ASD
Microtops II
Sunphotometer
ON GROUND INSTRUMENTS

## Slide 14: SRIX4Veg
Slide 14
ON GROUND INSTRUMENTS

## Slide 15: SRIX4Veg
Slide 15
LOGISTICS and CHALLENGES
Organisation
&
logistics
Heat
Software issues….
52 flights in total!

## Slide 16: SRIX4Veg
Slide 16
A big part of the experiments was ensuring that the participants just had to bring their UAVs and not set up all the supplementary instrumentation
This meant providing them with IMU/GPS corrections through a fixed GPS sensors (left demonstrated for an NPL flight)
And a DEM of the measurement area (middle and right)
(bottom right image) you can see the tents and the vehicles
(top right image) you can see a close up of the rows in the corn

## Slide 17: SRIX4Veg
Slide 17
Processing steps:
  Individual scans within each set of 10 spectra are flagged and removed from if they are more than 2 standard deviations away from the mean DN value.
  For each sequence of measurements (panel -> tarp -> panel) reflectance values are calculated for the middle timestep between the panel measurements.
  For each flight, interpolated reflectances are calculated w.r.t the middle of the flight time.
Because of changes to illumination conditions, different instrument operators (of the ASD), and the occasional mistake in the data collection we needed to do some quality control (QC).
This meant flagging individual spectra or sequences of spectras and removing them; for the latter case we also used temporal interpolation to fill in gaps.
The gif here shows what the reflectance looks like without QC, you’ll notice that:
  The reflectance jumps around when it should increase as it gets closer to midday
  The uncertainties can be very large (>50%)

## Slide 18: SRIX4Veg
Slide 18
To be removed
This gives an example of the removal of individual spectra which are outside 2 standard deviation of the median.
The flagged spectra could be caused by the instrument operator moving the FOV so it’s not looking at the target anymore (it was uncomfortable so might be as simple as a fidget!).
This will also make the uncertainty big if left.

## Slide 19: SRIX4Veg
Slide 19
We interpolated to the middle of the flight so the reflectance data were representative of as much of the flight as possible
The left plot shows the change in the brightness of the white reference panel measured before and after each flight
  Which explains why we interpolated the reflectance to the middle of the flight
The right two plots show the before and after filtering of the individual spectra (note the reduced uncertainty in the second plot)

## Slide 20: SRIX4Veg
Slide 20
This is the gif from a few slides ago but after full QC:
  The spectra rises up to noon and then decreases (small variations are now because of natural illumination changes)
  Uncertainties are all reasonable
  This data was sent to participants

## Slide 21: SRIX4Veg
Slide 21
1st SRIX4Veg Workshop
28th March 2022
@virtual
SRIX4Veg Field Campaign
with ALL teams
18th – 22nd July 2022
@Las Tiesas (Barrax, Spain)
2nd SRIX4Veg Workshop
23rd – 24th November 2023
@ESA-ESRIN
3 MAIN STEPS:
WE ARE HERE
Mark your Calendars !

## Slide 22: SRIX4Veg
Slide 22
1st SRIX4Veg Workshop
28th March 2022
@virtual
SRIX4Veg Field Campaign
with ALL teams
18th – 22nd July 2022
@Las Tiesas (Barrax, Spain)
2nd SRIX4Veg Workshop
23rd – 24th November 2023
@ESA-ESRIN
3RD STEP:
WE ARE HERE
Mark your Calendars !
GOALS of the 2nd SRIX4Veg Workshop:
Discuss together about the outcomes of the SRIX4Veg field campaign;
Receiving feedback on the draft Protocols and Procedures for SR validation using UAVs.

## Slide 23: SRIX4Veg
Slide 23
Proposed Future Steps:
Updated version of the Protocols and Procedures for SR validation using UAVs to be shared with CEOS WGCV LPV and IVOS for review and contribution in Q1 2024.
CEOS WGCV LPV and IVOS review process (2-3 months?).
Inclusion of feedback and updated version of Protocols & Procedures to be submitted to CEOS WGCV for potential endorsement in Q3 2024.
In Parallel:
- Cooperation with SRIX4Veg-II in Australia by sharing the latest version of the Protocols & Procedures document available at that time, so to be used by SRIX4Veg-II participants. Detailed plan to be discussed.
- Cooperation with SRIX4Veg-II in order to prepare updated Protocols & Procedures, based on the outcomes of both SRIX4Veg-I and -II.

## Slide 24: SRIX4Veg-II
Australia has an active community deploying UAS for Earth Observation including the development of complementary methods, protocols & apps, e.g. TERN Drone Protocols for Data Collection, RGB and Multispectral Imagery Processing, Lidar Processing;
There is a recognised need to develop a community approach/guideline for the collection of data from UAS for the validation of satellite-derived surface reflectance products across vegetated areas;
Good synergies to extend effort and be involved in co-development with international partners;

## Slide 25: SRIX4Veg-II
Slide 25
Underlying aims:
To harness the Australian community;
Development of a EO community project (as an EOA calval WG initiative);
To showcase Australian EO capabilities & infrastructure (sites, facilities, labs)

## Slide 26: SRIX4Veg-II
Slide 26
Site
TERN/LPV supersite Calperum (https://www.tern.org.au/tern-observatory/tern-ecosystem-processes/calperum-mallee-supersite/, https://www.tern.org.au/site-of-the-month-calperum-mallee-supersite/) across 9000 km2 ~270 km E of Adelaide, close to Renmark;
13 years measuring fundamental carbon, water, energy and nutrient pools and fluxes;
                One eddy-covariance flux tower
                Soil water content, temperature and electrical conductivity probes
                Phenocams
                Groundwater bores with nested piezometers
                18 x 1 ha Surveillance monitoring plots
                Airborne LiDAR and hyperspectral imagery calibrated using SLATS star transects, leaf sampling, tree structure and LAI measurements
Mallee semi-arid ecosystem, fringing the River Murray floodplains on Calperum Station, South Australia;
Comprises undulating mallee woodlands and riverine vegetation alongside the river;
Image credit: TERN
Pinnacles
Calperum

## Slide 27: SRIX4Veg-II
Slide 27
    Plan
Timing
  postponed to weeks of 4th or 11th March 2024;
  Methodology
  Based on SRIX4Veg-I, updated to reflect outcomes & adjusted for Calperum;
Logistics
  Insurance, licencing, regulations, shipping, etc.
  Field equipment & ancillary equipment, e.g. reference panels, gazebos, tables, etc.
  Accommodation, food, etc;
  Strong in-kind support from TERN, administration/promotional support from EOA;
  Developing proposition for support beyond best efforts;
Teams
  Currently 7 local teams, 1-2 international team, noting that this is close to the limit, 52 flights for 7 teams for SRIX4Veg-I