## Slide 1: WGCV-52 Agency Report Aerospace Information Research Institute (AIR), Chinese Academy of Sciences (CAS)
Lingling Ma, AIR
Agenda Item 3.9#
WGCV-52, ESA/ESRIN, Italy
5th - 9th June 2023

## Slide 2: 1. Brief introduction of AIR
The Aerospace Information Research Institute (AIR), Chinese Academy of Sciences (CAS), was established by incorporating three former CAS institutes:
The Academy of Opto-Electronics (AOE), Chinese Academy of Sciences;
Institute of Remote Sensing and Digital Earth (RADI), Chinese Academy of Sciences;
Institute of Electronics, Chinese Academy of Sciences (IECAS).
Over 3,984 employees by March 2023
        Five CAS academicians
        Over 300 full professors and professorate senior engineers
        Over 600 associate researchers and senior engineers
        AIR houses 21 national-level / CAS-level key laboratories, centers, and unincorporated units.
12 campuses across China
        AIR owns complete chains of RS payload developing, data receiving, processing and application.

## Slide 3: 2.Status of Baotou Cal&Val Site and recent activities
乌梁素海
试验场区
Located in Inner Mongolia, China. 50km away from the Baotou city.
Integrate multi-type typical natural scenes and permanent artificial for HR sensor calibration and evaluation.
It is designated as “National calibration and validation site for high resolution remote sensors” by NRSCC,MOST. It is also one of the demonstration sites of the RadCalNet, listed in the databases as permanent MTF target and SAR target.
Overall status
http://sarcv.ceos.org/targets/
Grassland
Ulansuhai lake
Bare soil
desert
sunflower
lucern
potato
maize
Artificial GCPs
Gravel targets

## Slide 4: 2.Status of Baotou Cal&Val Site and recent activities
Automatic calibration for optical satellites
Desert
Permanent targets
SV-01 MUX
(2018/5/2 12:03:54)
Complete instrument systems for surface spectral feature and atmospheric parameter automatic measurement
GF-1 Pan 2018/4/23
GF-2 Pan 2018/5/27
SV-1 Pan 2018/5/2
SV-1 Pan 2018/5/2
ZY-3 Pan 2018/5/27
ZY-02C Pan 2017/4/13
GF-6
RadCalNet BTCN
RadCalNet BSCN
In the past years, Baotou site has provided automated radiometric calibration and performance assessment supports for a lot of Chinese HR optical satellites.

## Slide 5: 2.Status of Baotou Cal&Val Site and recent activities
Automatic calibration for optical satellites
Empirically fitted model of temperature corrections for automatic surface spectrum measurement
Atmospheric diffusion model for Baotou artificial target
Uncertainty of TOA reflectance
(IEEE TGRS，2021)
Uncertainty tree diagram to describe the BOA reflectance
(Remote Sensing, 2020)
Great efforts have been made to decrease the uncertainty of the simulation of TOA reflectance.

## Slide 6
  75 small-scale permanent GCPs for geometric calibration of airborne sensors: within the range of 5km×6km, including 43 permanent targets (2m*2m) and 32 simple bases.
  16 large-scale permanent GCPs for geometric accuracy validation of HR satellite sensors: 4 targets were 13m×8m in size and 12 targets were 3m×3m in size.
permanent targets(13m×8m)
permanent targets(3m×3m)
GCPs at the site
satellites image（SuperView-1，GSD 0.5m）
Geometric Control Points for HR optical sensors
Google Earth image
(from Digital Global, 0.5m)
permanent targets(2m×2m)
simple bases
2.Status of Baotou Cal&Val Site and recent activities

## Slide 7: 2.Status of Baotou Cal&Val Site and recent activities
Cal&Val for SAR satellites
70m
60m
  A bar-pattern target based on roughness-difference was developed, offering a visual representation of image resolution.
The “image resolution” is better than 3m.
Corner reflector
SAR image
Nominal resolution:
Ground range instrument geometric resolution:1.21m
Azimuth instrument geometric resolution: 0.90m
The resolution assessment results of the seven CRs are consist with each other except CR#7. The image of CR#7 is not a ideal point response image.
CR #7
CR #1
Azimuth
KOMPSAT-5 SAR image on October 22, 2014(HH Polarization)
  For quickly deploying corner reflectors and avoiding repeated measurement of position information, 15 corner reflector bases were constructed and distributed across the site.

## Slide 8: 2.Status of Baotou Cal&Val Site and recent activities
Capability of atmospheric parameters observation
  Microwave Radiometers (MP-3000A): the temperature and humidity profiles.
Aerosol Extinction Coefficients from LiDAR
Temperature profile from MP-3000A
  Two sets of Automated Meteorological Observing System
  Sun Sky Multispectral Photometer (CE318): jointed in AERONET
  Mini Micro Pulse LiDAR

## Slide 9: 2.Status of Baotou Cal&Val Site and recent activities
Updating of Baotou site Infrastructure for flight campaign
Airstrip
Hangar
Satellite image over the Airstrip at Baotou site
2 km long airstrip and a test hangar in the field, which can easily support UAV flight tests.

## Slide 10: 2.Status of Baotou Cal&Val Site and recent activities
Flight campaign
An airborne flight campaign with 7.8km flight altitude.
Sentinel-2/MSI (2021-10-23)
Prototype of LIBRA’s EMIS (Earth-Moon Imaging Spectrometer, 0.38 – 2.35μm with spectral resolution of 10nm)
Aircraft: Pilatus PC-12
The hyperspectral data was compared with Sentinel-2/MSI and in situ measurement. Airborne data shows much better agreement rather than that of in situ data.

## Slide 11: 3. The validation site network for national civil space infrastructure
The National Civil Space Infrastructure project was proposed and began to construct in 2017.
It aims to provide common and basic services and support facilities for satellite remote sensing applications, and effectively serves different applications.
Guarantee of basic information products and service quality
Authenticity inspection and optimization guarantee of information products
Guarantee of generic key technologies of satellite application
Provide resource sharing services for new technology research and development
Comprehensive experimental field
provide a comprehensive site and capability for integrated field campaign
Validation sites
Time-series high frequency multitype parameter automated measurement.
Benchmark and comprehensive laboratories
Towards the building of capacity of SI traceability
The validation site network
48 optical & microwave sites
6 electromagnetic test sites
6 comprehensive fields
Integrated field campaign instrument
Instrument calibration lab.
Microwave simulation lab.
Optical simulation lab.

## Slide 12: 3. The validation site network for national civil space infrastructure
The validation network composed of 48 sites has been built nationwide, so as to validate six categories of products.
12
Test site network
Geometry products
Radiation products
Vegetation products
Water products
Atmosphere products
Land products
Achieved: DEM, DOM
Achieved: TOA radiance, Land Surface reflectance, Land Surface temperature, Brightness Temperature, Backscattering coef. …
Achieved: Land cover, Soil moisture, Snow cover, Soil salinity, Surface albedo, Interferometric deformation
Scheduled: Evapotranspiration, emissivity, snow cover …
Achieved: Vegetation index, Leaf area index, Vegetation phenology, vegetation height,…
Scheduled: SIF…
Achieved: AOD, Water vapor content,
Scheduled: Greenhouse gas, Pollution gas …
Achieved: Water surface reflectance, Water surface temperature, Water chlorophyll content, SSC…

## Slide 13: 4.1 Optical radiometric calibration based on PICS in Northwest China
TOA reflectance model suitable for several stable targets in Golmud area was constructed using Aqua/MODIS and ECMWF reanalysis data.
MODIS TOA reflectance time series
Atmospheric parameters time series
Parameterized TOA reflectance model
Constraint conditions for TOA reflectance model
SZA≤35°；AOD@550nm ≤0.4；WVC≤2.0g/cm2
DaZaoHuo East in Golmud
XiaoChaiDan Lake West in Golmud
Scattering angle was introduced to characterize the multiple scattering contributions between the surface and atmosphere;
DOY was introduced to characterize seasonal changes

## Slide 14: 4.1 Optical radiometric calibration based on PICS in Northwest China
Sentinel-2A/2B @ DaZaoHuo East
Landsat-8 @ DaZaoHuo East
Sentinel-2A/2B @ XiaoChaiDan Lake West
Landsat-8 @ XiaoChaiDan Lake West
 | B1 | B2 | B3 | B4
VZA | 0.07 | 0.07 | 0.04 | 0.01
VAA | 0.11 | 0.03 | 0.01 | 0.03
SZA | 0.11 | 0.01 | 0.01 | 0.03
SAA | 0.23 | 0.04 | 0.01 | 0.06
MODIS | 2.00 | 2.00 | 2.00 | 2.00
Model fitting | 2.26 | 2.22 | 2.05 | 1.93
Spectral Match factor | 2.01 | 2.29 | 2.15 | 2.01
Spectral expanding | 1.00 | 1.00 | 1.00 | 1.00
Total uncertainty | 3.77 | 3.90 | 3.72 | 3.57
The uncertainty / % associated with modelled TOA reflectance (Take GF6/WFV as an example)
The relative difference between the simulated TOA reflectance values and satellite observations is basically distributed within ± 5%.

## Slide 15: 4.1 Optical radiometric calibration based on PICS in Northwest China
A total of 91 cross calibrations (with an average of at least 2 per month) were performed on GF6/WFV data from 2019 to 2021 without relying on ground measurements.
GF6/WFV time series calibration coefficient:（a）B1（b）B2（c）B3（d）B4
Orbit altitude | 505 km
Swath | PMS: 60 km; WFV:800km
GSD | PMS: 8 m
 | WFV: 8 16m
Maximum sidelooking angle | 35°
Spectral Response Function of GF-6/WFV
Technical parameters of the WFV onboard GF-6

## Slide 16: 4.2 Infrared sensor radiometric calibration with reanalysis time-series data
Temperature difference /K
Latitude
Mean bias
Abs. bias
STD
RMSE
No. sample
Sample size
In order to conduct recalibration of historical infrared data, the reanalysis time-series data (ERA 5) over the ocean area are used as the consistency calibration sources.
Though reanalysis data may have large uncertainty for individual record, the total calibration uncertainty can be reduced with massive samples.
Ocean area: with good homogeneity in infrared image
Sea skin temperature (SSTskin), atmospheric profiles of temperature and humidity derived from ERA5 are mainly used.
The standard deviation is 0.5K - 0.6K
The mean bias is around 0.2K
ERA5 SSTskin V.S. Argo buoy observation
the time-series trend is consistent

## Slide 17: 4.2 Infrared sensor radiometric calibration with reanalysis time-series data
BT(MODIS) /K
BT(HJ-1B) /K
Original RMSE: 0.69K
Recalibrated RMSE: 0.30K
Recalibrated results
Original observations
Tsinghai Lake
BT(HJ-1B) /K
BT(MODIS) /K
Original RMSE: 2.84K
Recalibrated RMSE: 0.86K
Recalibrated results
Original observations
Dunhuang Site
10 years’ historical HJ-1B (China’s environmental satellite) infrared data were recalibrated.
The recalibrated coefficients has been validated with MODIS observations in Tsinghai Lake and Dunhuang site.
Spectral response function
Wave length / μm
HJ-1B IRS thermal band

## Slide 18: 4.3 Cross-calibration of HR optical satellite over RadCalNet sites
The project “Cross-calibration of high-resolution optical satellite with SI-traceable instruments over RadCalNet sites” was supported by ESA-MOST cooperative Dragon 5.
The objective is to build the benchmark transfer chain from well-calibrated satellites (future SI-traceable sensor) to RadCalNet TOA reflectance, so as to decrease the uncertainty of TOA reflectance product.
SI
RadCalNet TOA reflectance
Calibrated instruments
SI-traceable reference instruments
The benchmark transfer chain
Focus on the satellite data processing, calibration
Metering experts
Cal&Val experts
Sensor R&D experts
RS data processing and application experts
AIR-CAS
Chinese PI: Prof. Chuanrong Li
ESRIN-ESA
European PI: Prof. Philippe Goryl
NPL and NIM
AIOFM-CAS, CIOMP-CAS and SITP-CAS
CMA, CRESDA
Team composition

## Slide 19: 4.3 Cross-calibration of HR optical satellite over RadCalNet sites
Case study
Empirical Model over BSCN, RVUS and GONA were built using Landsat-8/OLI as reference sensor, and validated by comparing with Sentinel-2A/B observations.
LCFR is not yet analyzed as the site’s TOA reflectance for Red and NIR bands have shown variance in the summer, possibly due to vegetation growth in the area.
Modelling
B2
ρTOA = f(X1,X2,X3L)
S2：The correction factor between RadCalNet TOA reflectance product and modelled TOA reflectance was used to correct other TOA reflectance at the same day;
For BSCN, the relative difference between TOA reflectance product and the observed TOA reflectance is reduced from 6% to less than 3%. The same relative difference for RVUS and GONA site has decreased as well.
S1：The TOA reflectance model was firstly modelled, and the errors of TOA reflectance model were less than 4%;
S3: The corrected TOA reflectance was compared with Sentinel-2A/B observed TOA reflectance.
BSCN
RVUS
GONA

## Slide 20: Summary
Status of Baotou Cal&Val Site and recent activities
The validation site network for national civil space infrastructure
New technology explorations:
  Optical radiometric calibration based on PICS in Northwest China
  Infrared sensor radiometric calibration with reanalysis time-series data
  Cross-calibration of HR optical satellite over RadCalNet sites

## Slide 21
Thanks!