## Slide 1: Indian SAR Missions & CB Support
Raj Kumar
Space Applications Centre, ISRO
WGCapD-8
Dehradun, India
March 6-8, 2019
Committee on Earth Observation Satellites
rksharma@sac.isro.gov.in

## Slide 2
  Development and operation of state-of-the-art Microwave Sensors
    Active
    Passive
    Spaceborne, Airborne and Ground applications.
  SARs,
  Wind Scatterometer,
  Radiometers,
  Altimeters,
  GPRs,
  Sounders
Indian Microwave Remote Sensors Activities
Bhaskara-1 1978
Bhaskara-2
1981
ASAR
1989-1993
OCEANSAT-1 MSMR
1996-1999
OCEANSAT-2 SCATTEROMETER
2009-2014
MEGHA-TROPIQUES
2011
Notes: Bhaskara 1 & 2 had SAMIR (microwave radiometer) working at 19.35 , 22 & 31.4 GHz for study of ocean surface study & study of water vapour, liquid water content in the atmosphere.MSMR 6.6 GHz- sea surface temp, 10.65- wind speed, 18-precipitation, 21- liquid water content in atm.

## Slide 3
Scatterometers
Airborne SARs
Microwave Sensor Payloads
Space SARs
C-band SAR (RISAT-1)
2012
CY-2 L/S SAR
2018
C-band SAR
(RISAT-1A & 1B)
2019-20
S-band SAR
(NI-SAR)
2019-20
DMSAR (2007-2012)
L/S Airborne
SAR (2017-18)
OS-2 SCATT (2009)
SCATSAT-1 (2016)
OS-3 & 3A SCATTS
(2018-19)
SCATSAT-2 (2020)
Radiometers
MEGHA-TROPIQUES
2011
ISRO’s Array of Microwave Sensors
ATMSAT 1 (2021)
ATMSAT 2 (2022)

## Slide 4
Earth Observation Space-borne SARs
C-band SAR (RISAT-1) 2012
RISAT-1
HRS Mode
C-band SAR (RISAT-1A) 2019
RISAT-1
RISAT-1A

## Slide 5: RISAT-1A Increments
InSAR detecting a volcano in Kenya.[Sparks et al., 2012; observations from Envisat ERS-1 & ERS-2].
Polarization chart for SAR(courtesy Renay et al).

## Slide 6
Chandrayaan-2 Dual FrequencySAR

## Slide 7
Earth Observation Air-borne SARs
ASAR
1989-1993
DM Airborne SAR
2007-2011
X-Band Minisar
L & S-Band SAR

## Slide 8
Geometry
L&S Band Airborne SAR System

## Slide 9
SAR APPLICATIONS
Agriculture
Soil Moisture
Forestry
Terrain
Geology
Landuse/
Landcover
Oceanography
Polar Studies
Snow & Glaciers
Floods
Operational
Quasi- Operational
Technique Development
Capacity Building
Early
rice
Very Late rice
Late rice
C-band SAR Image
Gujarat
Kinnoi Fault
RISAT-SAR

## Slide 10
Parameters | L-band SAR |  | S-band SAR
Orbit | 747 Km with 98.5 Inclination |  | 
Frequency (wavelength) | 1.25GHz (24cm) |  | 3.20 (9.3cm)
Repeat cycle | 12 days |  | 
Time of Nodal Crossing | 6AM / 6PM |  | 
Polarization | Single (SP), Dual (DP), Circular (CP), Quad (QP) and Quasi-quad pol (QQP) |  | 
Incidence angle range | 33 – 47 deg |  | 
Available Range Bandwidths | 5 MHz, 20 MHz, 40 MHz, 80 MHz | 10 MHz, 25 MHz, 37.5 MHz, 75 MHz | 
Resolution (Azimuth  Slant range) | 6.9m  7.5m (for 20MHz bw) 6.9m  1.9m (for 80MHz bw) | 6.4m  6m (at 25MHz bw) 6.4m  2m (for 75MHz bw) | 
Max. Swath width | > 240 Km |  | 
Data and Product Access | Free & Open |  | 
S-SAR Antenna Beams 1 to 24
Reflector
Feed
1
24
425kms
230kms
699kms
Nadir Axis
S/C
Beam #24
Beam #24 Projected at Near-End of Feed
Beam #1 Projected at Far-End of Feed
Beam #1
370
S-SAR Range Imaging Geometry
370
425kms
230kms
699kms
Tx Beamwidth 9.30
Rx Beam #1
747kms
Rx Beam #24
NISAR Satellite
NISAR

## Slide 11: S-SAR
Science require frequent coverage over global targets
NISAR would acquire sufficient swath with high resolution
New SweepSAR technology being implemented by both JPL and ISRO
S-SAR Operation:
Thermal constraints ( 0 to +40degC / 45degC thermal design limit)
Data Volume (>3Gbps Max.)
Desired Science requirement
  4 Orbits / 14 Orbits – 15Minutes over SAARC and Antarctica regions.
  10 Orbits / 14 Orbits - 2 Minutes globally / orbit
Thermal analysis of S-SAR
  14 Orbits / 14 Orbits – 10 Minutes over SAARC and Global regions
Comfortable Thermal Margins to meet desired science requirements
Payload to JPL by end 2019
Launch by December 2021
3-Beam Overlap DBF
420kms
700kms
P
12
11
Beam 11 Data
Beam 12 Data
θ11
θ12
Notes: Emphasis:
New technology to allow fast repeat, wide swath, full resolution.
Someone might ask about receiver blanking leading to gaps in the swath. It is true if we have fixed PRF we’ll have 2 or 3 10 km gaps in the swath. We can either suffer it, with ascending descending coverage filling in almost all gaps, or we can dither the PRF to fill them in. We are studying the impacts in detail now.

## Slide 12
Geological Applications: 6.1 Structural & Lithological mapping; 6.2 Lineament mapping; 6.3 Paleo-Channel study; 6.4 Geomorphology; 6.5 Land degradation mapping; 6.6 Geo-archaeology; 6.7 Mineral explorations
Ecosystem Structure: 1.1 Agriculture biomass & Crop monitoring; 1.2 Forest biomass; 1.3 Forest disturbance; 1.4 Mangroves / Wetlands; 1.5 Alpine vegetation; 1.6 Vegetation phenology; 1.7 Soil moisture; 1.8 Ecosystem stress assessment
Land Deformation: 2.1 Inter-seismic / Co-seismic deformations; 2.2 Landslides; 2.3 Land subsidence; 2.4 Volcanic deformations
Cryosphere: 3.1 Polar Ice Shelf / Ice sheet; 3.2 Sea Ice Dynamics; 3.3 Mountain snow/ glacier 3.4 Glacier dynamics/ hazard (Himalayan Region); 3.5 Climate response to glaciers; 3.6 Sea–Ice advisory on safer marine navigation in Antarctica region
Coasts & Ocean: 4.1 Coastal erosion / shoreline change; 4.2 Coastal subsidence and vulnerability to sea-level rise; 4.3 Coastal bathymetry; 4.4 Ocean surface wind; 4.5 Ocean wave spectra; 4.6 Ship detection; 4.7 Coastal watch services; 4.8 tropical cyclone
Disaster Response: 5.1 Floods; 5.2 Forest fire damage assessment; 5.3 Coastal oil spill; 5.4 Earthquakes / Others
NISAR: Proposed Applications

## Slide 13
ISRO Observation Plan
Disaster Management
Himalayan Snow & Glacier
Deformation Monitoring
Polar Science (ISRO+ Joint targets)
S (CP) 25 MHz; L (QP) 40+5 MHz
Agriculture, Forest & Wetland
Background Land (Systematic Coverage)
S (DP/CP) 37.5/25 MHz;
L (DP) 20+5 MHz
Coasts / Coastal Ocean
S (CP) 25 MHz; L (VV+VH) 20+5 MHz
Indian Ocean
S (DP-VV+HV) 10 MHz
L(SP) 5 MHz
Ice Charactn (Ant; Svalbard; Bohai)
S (CP) 25 MHz; L (VV+VH) 20+5 MHz
High Resolution Urban / Landslide
S (SP) 75 MHz; L (DP) 40+5 MHz
Deformation Studies
S (DP) 37.5 MHz; L (DP) 20+5 MHz
Polar Region (Antarctica + Greenland)
S (CP) 25 MHz; L(SP) 80 MHz
Ind ocean-Indonesian volcanic arc
Polar Science (ISRO targets)
Period of Obs.
Jan – Dec; All 30 cycles
Jan – Nov; 16/30 cycles
Jan – Dec; Every Alternate cycles
BoB: Jun – Dec; All cycles
Arabian Sea: Apr- Sep; All cycles
Oct-Apr (Antarctica); Dec-May (Svalbard & Bohai)
Jan – Dec; Every Alternate cycles
Ant: Every/ alternate cycle; Greenland: every cycle
svalbard
Bohai bay
Indian Research Stns
Background Land
Agriculture & Forest
Coastal Applications
Ocean Applications
Important Obs. Modes

## Slide 14
India + neighbors boundary
Agriculture/ Forest/ wetland
Jute crop
Alpine forest
Seismic Deformation
Land Subsidence
Landslide
Urban subsidence
Volcanic deformation/ studies
Coastal region (sea 300km)
Coastal habitat
Coastal deformation
Coastal mud bank
Coastal region (land, 100 km)
Ocean – Arabian Sea
Ocean – Bay of Bengal
Disaster – floods
Disaster – forest fire
Disaster – oil slick
Cryosphere - Himalayas
ISRO Targets over India and Surroundings
These exclude polar targets
Arabian Sea
Bay of Bengal
Coastal Ocean
Coastal Ocean
Forest Fire
Himalayas
Himalayas
Seismic Deformation
Flood
Land
Subsidence
Oil
Slick
Agril.
Forest
Wetland
Snow
Glacier
Mud bank
Coastal
Habitat
Volcano
Urban
Landslide

## Slide 15: NASA Polar Cryosphere Targets
Sea Ice Q1 (L- single-pol : 5 MHz) - same as NASA requirement
Sea Ice Q2 (L- single-pol: 5 MHz) - same as NASA requirement
Sea Ice Q3 (L- single-pol : 5 MHz) - same as NASA requirement
Sea Ice Q4 (L- single-pol : 5 MHz) - same as NASA requirement
Ice Characterization: S (CP) 25MHz & L(VV+VH) 20+5MHz; Sep-Apr, every 3days
Land Ice Antarctica: S (CP) 25MHz; Jul-Sep, 2 sets of mosaics
L (SP) 80 MHz, Half swath (same as NASA requirement)
Land Ice Greenland: S (CP) 25MHz; Dec-Mar, 2 sets of mosaics
L (SP) 80 MHz, Half swath (same as NASA requirement)
Priority Ice: L (SP) 80 MHz-half swath – same as NASA reqmt
Svalbard Ice Characterization: S (CP) 25MHz & L(VV+VH) 20+5MHz; Dec-Mar, every 12 days
Bohai Bay Ice Characterization: S (CP) 25MHz & L(VV+VH) 20+5MHz; Dec-Mar, every 12 days
Svalbard
Bohai Bay
Indian Stations in Antarctica
(Targets of ISRO’s Interest: Land Ice & Sea-Ice Q1-Q4)

## Slide 16
Orissa
CALIBRATION SITES (Point target Sites)
Amrapura,
Little Rann of Kutch
Image Courtesy: Google Earth
Indian Sites
International Point Target Sites
Rosamond CR array, California, USA
Australian CR array, Queensland
IMGEOS, Shadnagar
Desalpar, Rann of Kutch
Ahmedabad
SAC-Bopal
&
SAC-Ground
Distributed Target Sites
Amazon rainforest
Congo rainforest
Notes: It is planned to permanently deploy different types and sizes of corner reflectors at additional sites (educational institutes, RRSCs) in each state of India to cover all the beams of S-band.
In the first phase, permanent deployment of CRs in six Indian states (Gujarat, West Bengal, Rajasthan, Chhatisgarh, Karnataka and Madhya Pradesh) has been initiated.
For L-band beams, campaign modes will be carried out in various Indian sites in joint-mode with S
It is planned to develop point target site at Antarctica (near Indian stations Bharti and Maitri -band for the external calibration.

## Slide 17
Detachable Panels
Assembled 2m Perforated CR
Response of perforated CR in L-band
airborne image of 14th February 2018
Calibration
Customised & Built perforated 2m CR, based on the design by JPL
Compact light weight detachable CR design is in progress
90cm CR planned to be deployed in Antarctica, Designed & developed in SAC
In-house development of ARC in progress
Deployed Perforated CR
SAC-Bopal New Campus
SAC-Bopal
CAL-VAL Site
Perpendicularity Check
Amrapur
Patan
SIMULATED NISAR Coverage and response of Amrapur
Amrapur
Ground Photo
Amrapur

## Slide 18
1 - 2
3 - 4
5 - 8
9 - 10
11 - 15
No. of Projects
(Total: 77)
Region-wise distribution of Project Proposers
Airborne SAR R.A. Project Proposal Statistics:
77 Proposals; 45 Institutions
Science Plan and Research Announcement for L&S Airborne SAR

## Slide 19: L&S Airborne SAR Flight Campaign-2017/2018
Phase1 | June 2017
Area | Gujarat Sites (8 sites)
Base | Ahmedabad
Phase2 | February 2018
Area | Andra/Telengana (5 sites)
Base | Hyderabad
Themes
Agriculture
Soil Moisture Study
Urban Applications
Hydrology/Flood Mapping
Wetland Mapping
Coastal Applications
Oceanography
Mangroves
Geological Applications
Forest
Total sites: 66
Ph-II
Ph-I
Phase-I: June 2017, 8 sites
Phase-II: March 2018, 05 sites

## Slide 20
Possible targets for the ISRO L+S band airborne SAR flights
(Nominal site locations)
Alaska Glaciers
Texas/Louisiana Offshore oil slick sites
Beaufort Sea
Sea Ice site
Massachusetts
Harvard Forest area
Louisiana/Mississippi/Alabama
Ecology sites
Tennessee/N. Carolina
Ecology sites
Crop, forest and wetland applications
forest AGB and disturbance mapping
forest AGB & veg characterization

## Slide 21
  NASA and ISRO plan observations in the USA by ISRO L&S band SAR in FY 2019 on a NASA aircraft
  Some acquisitions will be designed to assess SAR calibration for UAVSAR and ISRO L+S.
  Many of the joint sites are likely to coincide with the sites identified in this UAVSAR campaign
  Some of the ISRO SAR flights could either duplicate or substitute for UAVSAR acquisitions
Exploring Options for Accommodating L+S ASAR on NASA Aircraft
Proposal for L&S airborne SAR Campaign over USA & Canadian targets
Construct new aircraft radome
• Modify aircraft to accommodate radome
• Modify aircraft to accommodate antenna
• Route antenna cables to cabin
• Place radar electronics in cabin
Mount antenna to UAVSAR pod
• Construct new pod radome
• Route antenna cables to cabin
• Place radar electronics in cabin

## Slide 22
Outreach Programs
Satellite Meteorological and OceAnographic Research and Training (SMART)
Training & Research in Earth-Eco Systems (TREES)
Outreach activities provide:
Familiarization with Indian EO data
Short-term advanced training courses
Long duration 3-9 months - Research
Data analytics and advanced visualization
State-of-the-art computing facilities
Research guidance
Subsidized accommodation & food
ISRO’s initiative to promote use of Indian EO data & products for research in Satellite Meteorology & Oceanography and Earth eco-system studies among students, researchers & academia
Research Programme
Training Programme
Challenges
Research Initiation Programme
Advance Research Programme
Data Exploration Programme
Fields of
Research
Processes
Retrieval
Assimilation
NWP
Vegetation Dynamics
Hydrology
Digital Image Processing and m/c learning
SMART / TREES
University
Institutes
R & D Organ.
Faculty
Teachers
IMD
NCMRWF
INCOIS
IAF
NAVY
State RS Centers
Student & Researchers
Training
Popularise ISRO Missions, Data & Products
Operational Agencies
Trainers

## Slide 23: TREES & SMART: Research and Training opportunities at EPSA
Participants Trained : 723
Research Projects Completed : 148
Trainings : 34
Human Discomfort
Index
Global analysed wind fields from
ScatSat-1 and its application
Convective Overshooting using Satellite Data
Effect of ships on scatterometer measurements
Generation of 3D building model & shadow analysis
Crop Suitability Analysis for UP
ORTHOSEG
AltiKa derived Global ship count
Mar,13 to June,18 at1° x 1°

## Slide 24
SMART Research Programme – Summary (2016-Present)
Assam University (1)
Anna University (18)
University of Madras (7)
Nirma University (4)
Indus University (4)
Annamalai University (1)
Alagappa University (1)
Charusat University (1)
Pune University (2)
Central Uni. of Haryana (1)
Central Uni. of Jharkhand (5)
Gujarat University (1)
Mangalore University (2)
Indian Maritime University (2)
Banaras Hindu University (1)
Sardar Patel University (2)
Cochin University (5)
Madurai Kamaraj University (1)
IIT-BHU (1)
IIT-Bhubaneswar (4)
IIT-Bombay (1)
IIT-Kharagpur (5)
IIST-Trivandrum (1)
IISER, Bhopal (1)
SV-NIT (3)
U V Patel College, Mehsana (2)
St. Albert’s College, Cochin (5)
Atharva College, Mumbai (1)
PDPU, Gandhinagar (1)
LDRP College, Gandhinagar (1)
MPSTME, Mumbai (1)
Dharmsinh Desai University (1)
Andhra University, Vizag (1)
PSG College, Coimbatore (1)
NIT, Warangal (1)
IITM-K, Trivandrum (1)
Amity University, Noida (2)
Universities/ Colleges
Total Students Trained – 93
[One month to 9 months]

## Slide 25
SMART Outreach Activity at Universities / IITs
Totally 530 students sensitized since 2016
Sl No | Dates | University / Colleges | No students attended
1 | 24-25 July 2017 | Cochin University of Science & Technology (CUSAT), Cochin | 100
2 | 26-27 July 2017 | Anna University, Chennai and University of Madras, Chennai | 200
3 | 19-20 March2018 | Savitribai Phule Pune University, Pune | 50
4 | 05-06 September 2018 | Department of Meteorology and Oceanography, Andhra University, Vishakhapatnam | 100
5 | 07-08 September 2018 | School of Earth, Ocean and Climate Sciences, IIT-Bhubaneswar | 80

## Slide 26
Training Title | Start Date | End Date | Participants | Institutes
Polarimetric SAR data Processing and Analysis | 20-Dec-16 | 21-Dec-16 | 21 | 12
SAR and Hyper-Spectral Data Analysis for Forest Applications | 30-Oct-17 | 03-Nov-17 | 24 | 13
SAR Data Processing and Analysis for Land Applications with Special Emphasis on L & S Bands | 06-Aug-18 | 10-Aug-18 | 32 | 27
SAR Data Processing and Analysis for Land Applications with Special Emphasis on L & S Bands | 24-Sep-18 | 28-Sep-18 | 25 | 19
Visualization of Earth Data and Archival System (VEDAS)
Training & Research in Earth-Eco Systems (TREES)
Total 102 Participants from 4 Trainings

## Slide 27
No. of Participants
Year 1998 - 17
Year 2000 - 21
Year 2002 - 19
Year 2004 - 15
Year 2006 - 18
Year 2008 - 16
Year 2010 - 14
Year 2012 - 14
Year 2014 - 17
Year 2016 - 13
----------------
Total - 164
Country Name
Azerbaijan
Bangladesh China DPR Korea India Indonesia Iran Kazakhstan Kyrgyz Republic Malaysia Maldives
Myanmar Mongolia Nepal
Papua New Guinea Philippines Republic of Korea Sri Lanka
Tajikistan Thailand Uzbekistan Vietnam
from 22 Countries
Centre for Space Science and Technology Education in Asia and Pacific- CSSTEAP- (Affiliated to UN)
SATELLITE METEOROLOGY AND GLOBAL CLIMATE
CSSTEAP-SATMET- Activities

## Slide 28
MIDAS (MIcrowave Data Analysis Software)
SAR Polarimetry (PolSAR)
SAR interferometry (InSAR)
Polarimetric SAR interferometry (PolInSAR)
Written in C/C++
Capable GUI in JAVA
SAR radiometric analysis tools like SAR image quality parameter estimation and impulse
Other modules like σo, γo generation, etc
Support for full & Hybrid-pol decompositions
Support for RISAT-1 hybrid pol analysis and various spaceborne and L&S airborne sensor
Polarimetric speckle filter integrated (POLSAR refined Lee)
Modular and easily extensible
Applications such as Glacier, Ship detection, Oil Spill, Supervised Classifier, Polarimetry based Crops discrimination