## Slide 1: Sustained Climate Data Record Generation at EUMETSAT
Slide: <number>
Jörg Schulz
Notes: <number>

## Slide 2: Content
Satellite launches
Finalised Data Records
Current Activities
Planned Data Records
Engineering homogenisation within the EUMETSAT distributed ground segment
Slide: <number>

## Slide 3: Upcoming Satellite Launches
Slide: <number>

## Slide 4: Finalised Data Records
Reprocessing of SEVIRI Level 1.5 image data for Meteosat 8 and 9 – Done, data available from the EUMETSAT data centre.
Reprocessing of GOME-2 level 1a and 1b radiances for Metop-A (2007 – 2011) - Done - Data Release Readiness Review on 22 May 2012 – Need to provide initial 10 orders with volume of ~200 TB;
Completion of Geostationary Surface Albedo (GSA) for Meteosat First Generation – Done – Validation started with external contractor – Data Release Readiness Review in July 2012
Supported GSA retrieval implementation in NOAA/NCDC.
Slide: <number>
Notes: <number>

## Slide 5
GOME-2 Long-term throughput changes
Solar Mean Reference (SMR) spectrum
Reprocessed signals R2 PPF 5.2 until August 2011
relative to February 2007
Slow onset of degradation observed after 2nd throughput test in channel 1 and 2.
Instrument is stable now in channel 3 and 4.
240 nm
790 nm
Feb. 2007
Aug. 2011
0.3
1.0
Notes: Reprocessing campaign R2 for level 1 data January 2007 to August 2011
  Main objective: Evaluation of a 3D (spectral, temporal, scan angle) degradation for both earthshine and solar mean reference
  Updated throughput monitoring
  Derivation of offline degradation characterization matrix (“Level 1B to C processor”) to be provided offline for the reprocessed data set.
<number>

## Slide 6: Current Activities
Slide: <number>
  Generation of consistent AMV and CSR products for Meteosat 2 – 9 (covering 1982 – 2010) – Delivery MSG part December 2012 – MTP part December 2013 after inter-calibration;
Inter-calibration of Meteosat First and Second Generation IR and WV channel using IASI and HIRS data as first GSICS climate related activity – Delivery End 2012-first half 2013;
Generation of Metop AVHRR Atmospheric Motion Vector – Delivery December 2012.
Notes: AVHRR polar winds is a relatively new operational product since August 2010.
Will reprocess to the beginning of 2007 to increase coverage.
Will implement two algorithms (1) EUMETSAT operational and (2) prototype that is similar to the NOAA/CIMMS algorithm. Will allow to generate comparison statistics for 5 years over Arctic and Antarctic areas.
We plan to make the operational algorithm also applicable to AVHRR data in GAC format. We think about a reprocessing of all GAC data back to 1982 or 1979 in 2013.
We are preparing an implementation directly at ECMWF using input data provided from CM-SAF. This is planned to be an processing outsource test from EUMETSAT (go where the data is).
<number>

## Slide 7: Scale of the Challenge
Slide: <number>
Fig: Satellites used for the ISCCP climate data record. (Courtesy of Ken Knapp, NOAA-NCDC)
Notes: Make ISCCP image smaller, and add title
<number>

## Slide 8: Scale of the Challenge
Slide: <number>
MET2
MET3
MET4
MET5
4
3
Original
Instrument changes
Calibration changes

## Slide 9: Example: Two Wind Vector Processors Arctic 13 April 2008, 11:34 UTC
EUM/STG-OPSWG/31/12/VWG/19 Slide <number>
EUM OPERATIONAL
CIMMS (EUM Prototype)

## Slide 10: Planned Data Records
Generation of consistent radio-occultation data (bending angles) back to 2001 from GRAS, CHAMP, GRACE and COSMIC sensors – Delivery of GRAS and COSMIC December 2012 – CHAMP and GRACE in 2013;
Total ozone and profiles from combined GOME-2 and IASI observations – Delivery December 2013;
Generation of Metop ASCAT level 1b – Delivery December 2013 – has clear links to ESA CCI soil moisture project.
Reprocessing of IASI level 1c with CNES – Delivery tentatively second half 2013.
Slide: <number>

## Slide 11: EUMETSAT WG on Data Set Generation through Reprocessing
The WG held its 4th meeting on 1-2 February 2012 at EUM HQ with participants from 5 SAFs, ECMWF and the CAF;
Consolidation of the EUM Data Set Generation Plan after the approval of the SAF proposals for 2012-2017;
In addition the WG agreed the need for harmonisation of data set formats, the versioning system for data records, associated file naming and the publication of data sets using a digital object identifier system – EUM Secretariat works out a proposal towards the end of 2012;
The WG decided that the DOI system shall be used for the publication of all data records. EUM Secretariat will function as the publication Agent, i.e., issuing the doi numbers.