## Slide 1: IROWG Climate Activities Co-Chairs: Axel von Engeln (EUMETSAT), Dave Ector (UCAR) Rapporteur: Tony Mannucci (NASA/JPL)

## Slide 2: Overview
Background Radio Occultation / IROWG
Climate Activities
Conclusions

## Slide 3: Background Radio Occultation (1)
Radio Occultation instruments observe GNSS (GPS, ...) satellites:
  rising, setting (atmosphere)
  zenith (orbit)
with GPS up to 650 occs / day & instr
currently up to 3000 occs / day (mainly COSMIC-1, Metop-A & -B, early record about 180 occs / day)
0.2km – 1km vertical resolution
products:
  level 1b: bending angle
  level 2: refractivity, temperature, pressure, water vapour, geopotential
  level 3: gridded products of level products above
Radio occultation principle: Observation of e.g. GPS satellite signals through the atmosphere; changing refractivity leads to bending of rays. Refractivity depends on pressure, temperature, water vapour. Depending on observation, either setting or rising events are observed.

## Slide 4: Background Radio Occultation (2)
Radio occultation (RO) has several features which make it an ideal NWP and climate monitoring data set:
  essentially a measurement of time;
  requires no calibration / potential benchmark capability;
  ideal to generate long term data sets, no issues with combining different satellites, e.g. < 0.05K bias for CHAMP to COSMIC, processing should though be by one setup;
  all weather capability;
  high vertical resolution in the upper troposphere, lower stratosphere, high sensitivity between ~5km to ~40km;
  “random sampling” in space and time (although tied to LEO orbit);
  provides “anchor” point in NWP analysis, re-analysis.

## Slide 5: Background Radio Occultation (3)
RO has a significant impact in NWP: Forecast error reduction, plot for different instrument type (source C. Cardinali, ECMWF)

## Slide 6: Background Radio Occultation (4)
Note: Figure from SCOPE-CM RO-CLIM proposal, now outdated for dates > 2013!
See also:
Status of the Global Observing System for Radio Occultation (Update 2013), IROWG/DOC/2013/02,available at:
http://irowg.org/workshops/irowg-3/
Initial ROTrends, RO-CLIM Focus
Extended RO-CLIM Focus
Record >12 years, from late 2001

## Slide 7: Background CGMS/IROWG History
IROWG initiated at CGMS-37 (Oct. ‘09)
First meeting (extension of OPAC Workshop 2010):
  IROWG #1 (Sep. 2010, joint OPAC, GRAS SAF, IROWG)
  provided summary report to CGMS-38
Second workshop:
  IROWG #2 (Mar./Apr. 2012)
  provided summary report, 2 WP (on CGMS-39 actions) to CGMS-40
Third workshop:
  IROWG #3 (Sep. 2013, OPAC, IROWG)
  provided summary report, several IROWG reports, CGMS-42 WP to be provided
Further info at http://www.irowg.org

## Slide 8: Climate Activities: RO Offers
FCDR:
  bending angle
  refractivity, …
ECV:
  temperature (RO not mentioned in http://ecv-inventory.com ?)
  pressure
  geopotential
  air density
  water vapor? (generally requires a-priori info)
  bending angle?
  refractivity?
Detection Times:
  Leroy et al. [2006], climate model testing, 7 to 13 years
  Ringer and Healy [2008], bending angle climate trend assessment, 10 to 16 years
  confirmed with RO observations (Steiner et al., 2011)
Notes: An Essential Climate Variable (ECV) is a geophysical variable that is associated with climate variation and change as well as the impact of climate change onto Earth. GCOS has defined a set of ECVs for three spheres, atmospheric, terrestrial and oceanic (GCOS-82, 2003).
The term Fundamental Climate Data Record (FCDR) denotes a well-characterized, long-term data record, usually involving a series of instruments, with potentially changing measurement approaches, but with overlaps and calibrations sufficient to allow the generation of products that are accurate and stable in both space and time to support climate applications (NRC, 2004). FCDRs are typically calibrated radiances, backscatter of active instruments, or radio occultation bending angles. FCDRs also include the ancillary data used to calibrate them. The term FCDR has been adopted by GCOS and can be considered as an international consensus definition.

## Slide 9: Climate Activities: Error Assessment
assessments on profile accuracy:
  RO vs. RO (allows also instrument to instrument)
  RO vs. radio sondes
  RO vs. (A)MSU (, IR)
  RO vs. NWP
assessments on climatology accuracy:
  statistical error (small)
  sampling error (decreases with increasing observations)
  systematic errors (dominating, increases with production level)
    ROTrends, SCOPE-CM RO-CLIM activities: compare climatologies, profiles from different centers and assess structural uncertainty
    various studies on comparison, orbit processing impact, improvements in initialization, etc

## Slide 10: Climate Activities: Projects (1)
ROTrends: RO community already started comparison of different processing centres in 2006. Main aim is to validate RO as a climate benchmark, initially by identifying processing impact (structural uncertainty). Note: best effort & unfunded.
  Initial ROTrends participants: JPL, GFZ, UCAR, WEGC
  1st Round: CHAMP Monthly Mean Climatology of refractivity (found ±0.03%/5 yrs trend uncertainty)
  2nd Round: Profile by profile comparisons, extension to include bending angles, dry temperature & pressure, … - ROM SAF, EUMETSAT also joined - (found trend uncertainty <0.03%/7yrs for bending angle, refractivity, pressure; <3m/7yrs geop. height of pressure levels, <0.06K/7yrs temperature. SU lowest within 50S to 50N at 8 km to 25 km)
  See also: http://irowg.org/projects/rotrends/
  Note: Activity now part of SCOPE-CM RO-CLIM project.

## Slide 11: Climate Activities: Projects (2)
SCOPE-CM RO-CLIM: encompasses ROTrends, brought under SCOPE-CM, with extended membership (NWP, Re-analysis, Climate models)
http://irowg.org/projects/ro-clim-under-scope-cm/
Reprocessing activities at the different centres for e.g. climate, re-analysis
GRUAN-GSICS-GNSSRO: Workshop on Upper-Air Observing System Integration and Application, WMO HQ in Geneva 6-8 May 2014

## Slide 12: Climate Activities: Possibilities
Direct trending from RO:
  bending angle for temperature trends
  refractivity for temperature trends
  temperature trends
  geopotential height trends
  bending angles for tropopause height
  temperature for tropopause height
Monitoring / Calibration:
  microwave and infrared instruments
  radio sondes
  others
Other phenomena observed by RO:
  Atmospheric gravity waves, Kelvin waves, Mountain waves, Quasi-Biennial Oscillation, El-Niño Southern Oscillation, Madden-Julian Oscillation, Diurnal tides, Sudden stratospheric warmings, Convective systems
Note: neutral atmosphere focus, no ionosphere included!

## Slide 13: Conclusion
RO has shown a large impact in NWP systems - thus should also have a great potential for climate monitoring, with the possibility for SI traceability. Currently about 3000 occs/day are available. The additional future GNSS signals will further increase the potential number of available observations.
Issues:
no long term RO continuity plan, to work towards an availability of at least 10,000 occs / day (IROWG recommendation)
risks of observational gap at mid- and high-latitudes, full diurnal coverage not assured (COSMIC-2 Polar - funding not assured)
RO record still short, not fully used yet for climate, climate models
availability of climate RO data sets (SCOPE-CM RO-CLIM project tries to address this but requires more reprocessing activities)

## Slide 14: References/Further Info
Some (incomplete) list of good websites for data quality, products:
  http://www.romsaf.org/monitoring/
  http://www.cosmic.ucar.edu/satStatus/
  http://www.romsaf.org/climate_monitoring/
  https//www.globclim.org/
Some selected overview presentations/publications:
  http://irowg.org/further-information/overviews/
IROWG website:
  http://www.irowg.org/
Acknowledgements:
  A. Steiner’s talk at 2nd International Conference on GPS Radio Occultation - ICGPSRO, May 14-16, 2013, Taipei, Taiwan
  U. Foelsche, A. Steiner (WEGC, Graz), R. Anthes (UCAR)