## Slide 1: Development of LiDAR Technology for Disaster Mitigation
Presented by Chuanrong Li
September, 2015 Frascati, Italy
Key Laboratory of Quantitative Remote Sensing Information Technology, Academy of Opto-Electronics (AOE), Chinese Academy of Sciences (CAS)
CEOS Working Group on Disaster Meeting #4

## Slide 2
LiDAR Technology--Distance Measurement
Imaging theory of airborne LiDAR
Scanning modes of LiDAR
LiDAR is the production of the combination between traditional Radar technology and modern laser technology. LiDAR was born in 1961, the next year after the invention of laser technology. Starting with simple distance measurement technology, a series of LiDAR have been developed for different application areas.
When laser pulse from laser device hits the target, a part of optical wave would reflect to LiDAR receiver. According to the theory of Laser distance measurement, the distance from target to LiDAR is calculated as
According to laser device position from GPS and laser emission direction from INS, each coordinate (X,Y,Z) of ground luminous spot can be precisely calculated.

## Slide 3
Concealed cars
Characteristics of LiDAR
Laser of ability to penetrate to forest
24-hour：actively emit laser signal and detect target information without the influences of shadow and solar altitude angle.
Direct Measuring: rapidly and directly achieve three-dimensional(3D) space information of wide-area ground target
Penetrable：partially penetrate plant cover ; thus can be used for forestry detection in forest and mountain region, provide search service for targets under plant cover.
Active Remote Sensing

## Slide 4
LiDAR Point Cloud
LiDAR Point Cloud colorized by Elevation
Intensity Image
DSM
DEM
Development of LiDAR Technology(Ⅰ) -Imaging

## Slide 5
Full waveform LiDAR record
Extracted features
Original Point Cloud data
Development of LiDAR Technology(II) -Full Waveform
Extract Multiple features including:
Distance
Intensity
Width of Echo Waveform
Backscattering cross section
Components number of a waveform
…
More Information
More Precise for feature recognition
Distance
Intensity
Width
Backscattering
cross section

## Slide 6
Application: Fine classification based on point cloud data
Development of LiDAR Technology(II) -Full Waveform
Remote Sensing Image
Point Cloud Data (colored by classification results)

## Slide 7
Three-Dimension City Modeling
Measurement of power lines
Coastline Detection
Selection Optimization of oil and gas pipelines
Forestry deposit quantity evaluation
Driveway Prospecting
Currently Primary Application of LiDAR

## Slide 8
Application for Disaster Mitigation
Advantages of LiDAR Application
24-hour observation and high-speed information extraction
Emergency response for disaster zone
Providing in-situ information for on site rescuing decision
Precisely 3D measurement for the structure and shape of the observed object
The detection of full procedure of geological disaster
Damage assessment of infrastructure
Detection and evaluation of post-disaster reconstruction

## Slide 9
Seismic Hazard
The 2010 Haiti earthquake was a catastrophic magnitude 7.0Mw earthquake, which caused major damage in capital Port-au-Prince and most region of Haiti and about 220,000 casualties. The scientists from University of Rochester utilized “Piper PA-31 Navajo”airplane equipped with LiDAR to collect 3D Port-au-Prince images.
Application for Disaster Mitigation
Haiti Earthquake“National Palace”
(a)Post-seismic high-Resolution(HR) aerial image(b) Post-seismic LiDAR image(c)Transformation between pre-seismic and post-seismic(bright area)

## Slide 10: Disaster Mitigation Application
Secondary Disaster Barrier Lake
Figure of Local Topography of TangJiaShan barrier lake(Including landslide and spill way)
The 2008 Great WenChuan Earthquake, measured at 8.0Ms on Monday, May 12 in Sichuan province and killed about over 69,000 people, caused massive landslides in TangJiaShan. Two adjacent landslides with megalith and clay filled in river channel to form giant barrier lake. The scientists from Wuhan University collected LiDAR point-cloud data in TangJiaShan barrier lake and achieved high-definition digital elevation image to qualitatively and quantitatively analyze water level, water retention capacity, spill way, and neighbor landslides of TangJiaShan barrier lake.
(a)Optical image (b)LiDAR Data

## Slide 11
Hurricane Hazard
（b） Before hurricane Elevation
（c）After hurricane Image
Huuricane“Ike” was a powerful tropical cyclone that swept through portions of coastal area of Texas in US and resulted in ten billions of US dollars in property damage and about a hundred casualties in September 2008. The researchers utilized the USGS Experimental Advanced Airborne Research LiDAR (EAARL) system to achieve LiDAR data by twin-engine “Cessna 310”airplane.
Application for Disaster Mitigation
（a） Before hurricane Image
（d） After hurricane Elevation

## Slide 12
Application for Disaster Mitigation
Landslide/ Mud-rock Flow Hazard
After Great SiChuan Earthquake, measured at 8.0Ms, the digital elevation model were achieved by LiDAR. The relative elevation accuracy could be reached by 30cm. The landslide zone can be easily recognized, and there are too many landslides in a few hundred meters in hardest-hit area.
(a) 3D Topographic Map nearby YingXiu Town
(b) Landslide Interpretation
nearby DuWen Driveway

## Slide 13
Remote Sensing Image
Point Cloud Data
(colored by elevation)
Development of LiDAR Technology(III) -- High-Spatial resolution Image
Challenging to LiDAR Imaging
Image of sparse discrete point can not clearly display the details, such as nature tone and texture of surface features

## Slide 14
LiDAR Data
Optical Image
DEM
Orthographic Image
3D Image
Complicated process flow
With Same platform
Development of LiDAR Technology(III) -- High-Spatial resolution Image
Solution One: Sharing Same Plateform
Difficulty to match between LiDAR dot and image pixel
Hard to work in real time way
Image
Point Cloud Data
(colored by elevation)

## Slide 15
Key Point：
Adopt common-path push-broom approach
Precisely match two types of data at front-end device of signal acquisition for real-time 3D imaging
spectrum separation filter
laser detector
CCD detector
Development of LiDAR Technology(III) -- High-Spatial resolution Image
Solution Two(AOE Solution): Sharing Same Front Optical System

## Slide 16
Wula mountain of Bayannaoer
Bronze square of Ordos
Reservoir of Ordos
Equipment ground test
Equipment installation
（Y-12 aircraft ）
A prototype of flight was successfully developed since 2009. The experiments of the ground surface and flight were positively performed, and it was first time to real-time achieve 3D image in common-path way
Experiment Achievement -- AOE Opto-LiDAR Imaging System
Original CCD image
LiDAR point data
Experiment plot ：Ordos in Inner Mongolia
Flight time： December 2013
Flight hour：4 hours
Quantity of achievement data：210G
Flight elevation：2km
Resolution ratio of 3D image：0.05m
Accuracy degree of relative elevation：0.3m

## Slide 17
Breaking through the limitation of achievement real-time elevation information from traditional optical imaging detection, support the demand for rapid response of disaster Mitigation
HR optical two-dimension(2D) imaging
High-accuracy laser 3D measurement
16m
（410919.6,448092.2,1439.1）
86m
Real-time image technology of common aperture optical stereo
Experiment Achievement -- AOE Opto-LiDAR Imaging System
Notes: 17

## Slide 18
15.5m
3.6m
（414686.0,4404965.3,1392.2）
Water reservoir in Ordos
A prototype of Flight——Real-time 3D imaging
Point cloud of detection area
Experiment Achievement -- AOE Opto-LiDAR Imaging System
Notes: 18

## Slide 19
A prototype of Flight——Real-time 3D imaging
Water reservoir in Ordos
18.3m
20.8m
（415221.8,4405198.3,1405.2）
Experiment Achievement -- AOE Opto-LiDAR Imaging System
Notes: 19

## Slide 20
WuLa mountain in inner Mongolia
坡度30°
（371527.2,4532154.3,1493.8）
（337284.4,,4531989.1,1324.2）
A prototype of Flight——Real-time 3D imaging
Experiment Achievement -- AOE Opto-LiDAR Imaging System
Notes: 20

## Slide 21
Development of LiDAR Technology(IV) – AOE Mini LiDAR
  Emergency response, arrive on the scene immediately
  Flexibly and simply operate, low demand for field, and steadily worked
  Collect field data, rapidly process data and transfer data to command center for making decision and judgment
  Trace trend in development of disaster and assist command center to implement constant operation
  Participate in post-disaster reconstruction and provide relative geographic information
  Difficulty in Getting into Disaster Zone
  Real-time & Emergency Response
  Platform of mini UAV
+
LiDAR payload of miniaturization, light-weighting and low-power consumption
Requirement
Mini UAV

## Slide 22
Mini UAV LiDAR System
Development of LiDAR Technology(IV) -- AOE Mini LiDAR
Light-weight structure design;
high-accuracy mini LiDAR system integrated into light-small INS, GPS aerial, and mini memory cell;
system weight under 5KG;
Meet the demand for common mini UAV equipment
Wavelength ：905nm
Operating distance ：200m
Effective field angular ：110°
Range resolution ：4cm
Range accuracy ：0.1m
Number of echoes：3
Positioning accuracy: 1cm± 1ppm
Volume: 360mmX220mmX265mm

## Slide 23
Airborne data
Vehicle data
LiDAR Point Cloud
Three-dimensional model
Experiment Achievement -- AOE Mini LiDAR

## Slide 24
Landslide
Landslide
  Contour line
Development of LiDAR Technology(IV) -- AOE Mini LiDAR
Above-mentioned system loaded in mini UAV can be mobile, flexible, and high-speed to analyze landslide, dredge barrier lake, judge the situation, and formulate emergency plan
Point Cloud
  Contour line
DEM in disaster zone
Achieve DEM data in disaster zone
Build contour line
Analyze landslides
Analyze water level of barrier lake

## Slide 25
As aerospace infrastructures plays a key role in disaster emergency, “Aerospace Application Coordination System for Emergency Response and Data Sharing (ArcSer)” is established by support of Chinese National Science-Technology Support Plan Projects
Coordinate civil aerospace resources to acquire remote sensing data of disaster area
Distribute the data to disaster reduction application agencies as soon as possible
Do aerospace remote sensing data acquisition and collects the data together
Way Forward(Ⅰ) —— New Element to Arcser

## Slide 26
ArcSer Platform
Civil Aerospace Resources Coordination
Ministries
Local Government
Institutes & Organizations
Disaster assessment
Disaster relief on site
Technical support
Inter-Ministerial Coordination Mechanism
Way Forward(Ⅰ) —— New Element to Arcser
Data Sharing for Disaster Reduction
Once great natural catastrophe occurs in China, ArcSer starts working.
It has started three times:
  YuShu Earthquake(2010.4 )
  LuShan Earthquake(2013.4 )
  Ludian Earthquake(2014.8 )

## Slide 27
ArcSer Platform
Civil Aerospace Resources Coordination
Ministries
Local Government
Institutes & Organizations
Disaster assessment
Disaster relief on site
Technical support
Inter-Ministerial Coordination Mechanism
Data Sharing for Disaster Reduction
Common aperture LiDAR system
Mini LiDAR
Way Forward(Ⅰ) —— New Element to Arcser

## Slide 28
AOE is willing to offer its contribution to international society of disaster mitigation.
We have the ability to provide end - to - end reliable service to the user by using LiDAR technology.
Provide specific system solutions based on user requirement
Develop ready to use LIDAR remote sensing system on-demand
Undertake LiDAR data acquisition service and satisfy application need
Way Forward(Ⅱ) —— International Cooperation

## Slide 29
We believe that space-borne LiDAR system is assured of a place in global earth observation systems in the near future.
Way Forward(Ⅲ) —— Space-borne LiDAR
Technical Challenge:
  Power issue
  LiDAR technology
  Effect of atmosphere
  …..

## Slide 30
Thank you !