## Slide 1
RUSSIAN EARTH OBSERVATION SYSTEM

## Slide 2
The Russian Earth Observation Satellite Constellation
© JSC «Russian Space Systems»
2

## Slide 3
INFORMATION CAPABILITIES OF RUSSIAN Earth Observation SATELLITE CONSTELLATION
Satellite / Characteristics | Resurs-DK | Resurs-P |  |  |  | Kanopus-V |  | Meteor-M |  |  | Electro-L
Launch Date (dd-mm-yyyy) | 15.06.2006 (archive only) | 25.06.2013 (Resurs-P1) 26.12.2014 (Resurs-P2) 13.03.2016 (Resurs-P3) |  |  |  | 22.07.2012 |  | 17.09.2009 (Meteor-M1) 08.07.2014 (Meteor-M2) |  |  | 20.01.2011 (1) 11.12.2015 (2)
Active Lifetime (years) | 3 | 5 |  |  |  | 5…7 |  | 5 |  |  | 10
Instrument | Geoton | Geoton | GSA | ShMSA |  | PSS | MSS | KMSS* |  | MSU-MR* | MSU-GS*
 |  |  |  | VR | SR* |  |  | MSU-50* | MSU-100* |  | 
Swath Width (km) | 28 / 16** | 38 | 25 | 97 | 441 | 23 | 20 | 900 | 900 | 2800 | Entire disk of the Earth
Spatial Resolution (m): Panchromatic (PAN) Multispectral (MS) | 1 / 3** 2–3 / 3–5** | 1 3 | – 30 | 12 23.8 | 60 120 | 2.1 – | – 12 | – 60 | – 120 | – 1000 | VIS – 1000, IR – 4000
Spectral Bands | 4 | 6 | 96-255 | 6 | 6 | 1 | 4 | 3 | 3 | 6 | 10
Revisit Period (days) | 6–10 | 3–4 |  |  |  |  |  | 1–3 |  |  | 15–30 minutes
* Open access data; ** Before / after September 2011 |  |  |  |  |  |  |  |  |  |  | 
Satellite / Thematic Tasks | Cartography | Ecological Monitoring | Infrastructure Object Monitoring | Environmental Management | Natural Resources Monitoring | Monitoring of Man-Made and Natural Disasters
Resurs-DK | 1:10,000 and smaller | + | + | + | + | +
Resurs-P | 1:10,000 and smaller | + | + | + | + | +
Kanopus-V | 1:25,000 and smaller | + | + | + | + | +
Meteor-M | 1:500,000 and smaller | + | – | + | – | +
Electro-L | – | – | – | + | – | Large-scale +

## Slide 4
RESURS-DK
  Launch date – June 15, 2006
Mission Purpose
Near real-time acquiring of highly informative data in visible and near-IR spectral range for ecological monitoring, natural resources inventory, mineral exploration, and mapping
  Current Tasks
Inventory of natural resources, topographic and thematic mapping
Monitoring of the biosphere pollution sources;
Monitoring of emergencies
Research activities
Onboard Instrument
Highly Detailed-Resolution Optical Camera [Geoton]
  Resolution PAN (0.58-0.80µm) – 1m / 3m*
  Resolution MS (3 bands, 0.5-0.8µm) – 2-3m / 3-5m*
  Swath width – 28km / 16km*

## Slide 5
Resurs-DK
© JSC «Russian Space Systems»
5
Tehran

## Slide 6
RESURS-P
  Launch date – 25 June, 2013 (Resurs-P1)
  26 December, 2014 (Resurs-P2)
  13 March 2016 (Resurs-P3)
Mission Purpose
Near real-time acquiring of highly informative data in visible and near-IR spectral range for ecological monitoring, natural resources inventory, mineral exploration, and mapping
  Current Tasks
Maps creation and update (scale 1:10,000 and smaller)
Environmental ecological monitoring
Operational emergencies monitoring
Respond to agriculture and forestry challenges
Socio-economic infrastructure monitoring
Onboard Instruments
Highly Detailed-Resolution Optical Camera [Geoton]
  Resolution PAN (0.58-0.80µm) – 0.9m
  Resolution MS (5 bands, 0.45-0.90µm) – 3m
  Swath width – 38km
  2 Wide-Swath Optical Cameras [ShMSA]
High Resolution Camera [ShMSA-VR]
  Resolution PAN (0.58-0.80µm) – 12m
  Resolution MS (5 bands, 0.43-0.90µm) – 23.8m
  Swath width – 97km
Medium Resolution Camera [ShMSA-SR]
  Resolution PAN (0.58-0.80µm) – 60m
  Resolution MS (5 bands, 0.43-0.90µm) – 120m
  Swath width – 441km
  Hyperspectral Camera [GSA]
  Resolution (96-255 bands, 0.4-1.1µm) – 30m
  Swath width – 25km

## Slide 7
Resurs-P
© JSC «Russian Space Systems»
Dublin

## Slide 8
KANOPUS-V
  Launch date – July 22, 2012 (Kanopus-V1)
  Next launch – the end of 2015 (Kanopus-V-IK)
  Current Tasks
Maps creation and update (scale 1:25,000 and smaller)
Environmental ecological monitoring
Operational emergencies monitoring
Respond to agriculture and forestry challenges
Socio-economic infrastructure monitoring
Onboard Instruments
PAN Optical System [PSS]
  Resolution (0.54-0.86µm) – 2.1m
Swath width – 23km
MS Optical System [MSS]
  Resolution (4 bands, 0.46-0.84µm) – 12m
Swath width – 20km
Mission Purpose
Near real-time acquiring of highly informative data in visible and near-IR spectral range for ecological monitoring, natural resources inventory, mineral exploration, and topographic mapping

## Slide 9
Kanopus-V
© JSC «Russian Space Systems»
9
Tehran

## Slide 10
METEOR-M
  Launch date – 17 September, 2009 (Meteor-M1)
  Launch date – 8 July, 2014 (Meteor-M2)
  Next launch – the beginning of 2016 (Meteor-M2.1)
Mission Purpose
Operational acquiring of cloudiness and the Earth’s underlying surface data, hydrometeorological data acquisition, heliogeophysical measurements, Earth’s resources study, and ecological monitoring
  Current Tasks
Environmental monitoring
Ice conditions monitoring
Operational emergency monitoring
Monitoring of radiation and heliogeophysical conditions in near-Earth space
Onboard Instruments
  2 Medium-Resolution Optical Camera [KMSS]
Land-Using Camera [MSU-100]
  Resolution MS (3 bands, 0.53-0.90µm) – 60m
  Swath width – 900km
Marine-Using Camera [MSU-50]
  Resolution MS (3 bands, 0.37-0.69µm) – 120m
  Swath width – 900km
  Low-Resolution Optical Camera [MSU-MR]
  Resolution MS (6 bands, 0.5-12.5µm) – 1000m
  Swath width – 2800km

## Slide 11
Meteor-M
© JSC «Russian Space Systems»
11
Rasht

## Slide 12
ELECTRO-L
  Launch date – January 20, 2011 (Electro-L1)
  December 11, 2015 (Electro-L2)
Mission Purpose
Operational acquiring of cloudiness and the Earth’s underlying surface data, hydrometeorological data acquisition, heliogeophysical measurements
  Current Tasks
Operational imaging of the Earth’s underlying surface
The World Ocean state monitoring
Global monitoring of emergencies
Onboard Instrument
  Geostationary MS Optical Camera [MSU-GS]
  Coverage area – the entire disk of the Earth
  Resolution VIS (3 bands, 0.5-0.9µm) – 1000m
  Resolution IR (7 bands, 3.5-12.5µm) – 4000m
  Swath width – 900km
  Revisit period in 24h – 30min (as scheduled) /
  – 15min (on ground commands)

## Slide 13
Visible bands (RGB)
IR band (10,2-11,2µm)
13
ELECTRO-L
© JSC «Russian Space Systems»

## Slide 14
Space Communication Station
RC-7
RC-5
RC-3
RC-2
EO Data Receiving and Recording Complex
Russian and foreign Earth Observation Data receiving and recording FACILITIES
The antenna complexes provide data receiving at the rate between 5 and 320 Mbps of Х-band with left and right polarization, for 24 hours – up to 30 satellites

## Slide 15
RECEIVING COMPLEXES BEING DEVELOPED BY NTS OMZ OF JSC “RUSSIAN SPACE SYSTEMS”
Complex | PK 2.4 | PK 3.1 | PK 3.6
Antenna type | Axial-symmetric parabola с f/d=0,4 |  | 
Antenna size, m | 2.4 | 3.1 | 3.6
Rotary support | Double-elevation |  | 
Polarization | Right-hand (L­band), right- ad left-hand (Х­band) |  | 
Operating frequencies MHz | 1690­-1710; 7450­-7550; 8000­-8400 |  | 
Receive rate, Mbps | Up to 310Mbps in Х­band (155Mbps in each channel), up to 3.0 Mbps in L­band |  | 
Quality factor, dB/K | 20 | 22 | 24
Antenna complex/Rotary support weight no more than, kg | 60/260 | 80/350 | 110/350
Rotary support power consumption, no more than, W | 100 | 100 | 100
Reception area | Entire upper hemisphere including zenith area |  | 
Primary power supply | 220W, 50Hz |  | 
Antenna complex operating temperature range, C | ­40... +50 |  | 
Antenna complex deployment conditions | Under radar dome |  | 

## Slide 16
Double-elevation scheme of rotary support construction |  | Antenna complex feed is dual-band (X- and L-band) | 
New types of cycloidal speed reducers used in rotary support |  | Use of radio receiver | 
Receiving complex is automatic |  | Radio paths have the capabilities of controlling and adjusting: - Given receive frequencies Modulations - Data receive rate | 
BASIC ENGINEERING SOLUTIONS CHOSEN IN DEVELOPING RECEIVING COMPLEXES

## Slide 17
Data Storage
System
Standard Processing
Value-added Processing
External Users
Planning
Receiving and Registration
CATALOG
(Jobs / Data)
Customer Interaction
Technological scheme of RUSSIAN operator’s Cycle

## Slide 18
Earth Observation DATA APPLICATIONs

## Slide 19
MAPPING

## Slide 20
AGRICULTURE

## Slide 21
City Vegetation

## Slide 22
FORESTRY

## Slide 23
NATURAL RESOURCES

## Slide 24
River Floods

## Slide 25
Resurs-P data covering diagram
The area of the Russian territory coverage by Resurs-P1 and -P2 (PAN and MS data) is more than 30 million sq. km since 2013

## Slide 26
Kanopus-V data covering diagram
The area of the Russian territory coverage by Kanopus-V1 (PAN and MS data) is more than 50 million sq. km since 2013

## Slide 27
Hydrometeorology
Natural Resources
Electro-L2
Electro-L1
2006
Resurs-DK
Meteor-M1
Resurs-P1
Kanopus-V1
Resurs-P2
2009
2011
2012
2013
2014
2015
2016
2017
2018
2019
2020
Kanopus-V-IK
Meteor-M2.2
Arctica-M1
Meteor-M2
Kanopus-V3
Kanopus-V5
Kanopus-V6
Electro-L3
Meteor-M2.1
Resurs-P3
Resurs-PM1
Meteor-M2.4
Meteor-M2.3
Obzor-R1
Resurs-P4
Kondor-FKA1
Kondor-FKA2
Resurs-P5
Meteor-M3
THE RUSSIAN EARTH OBSERVATION SATELLITE CONSTELLATION 2006–2020
Arctica-M2
Kanopus-V4
Hydrometeorology
NATURAL RESOURCES
MS (visible and IR) data
SAR data
Electro-L4
Electro-L5

## Slide 28
Thank you for attention!