## Slide 1: Polar Image Mapping - Lessons Learned
Shinobu Kawahito
Remote Sensing Technology Center of Japan (RESTEC)
in support of Japan Aero-exploration Agency (JAXA)
WGISS-26 Boulder, Colorado

## Slide 2: Background
Polar regions are special regions.
  Polar region will be largely distorted if expressed in some projections. (e.g. popular “Geographic lat-long” projection)
  Polar images may be better understood in polar specific projections.
WGS84/Geographic lat-long
WGS84/Polar Stereographic
* WGS84 : Name of an ellipsoidal earth model (and its associated datum)

## Slide 3: Various Polar Specific Projections
Some CRS with Polar Projections
WGS 84 / North Pole Azimuthal Equidistant
WGS 84 / North Pole Lambert Azimuthal Equal Area
WGS 84 / North Pole Stereographic (*)
WGS 84 / South Pole Azimuthal Equidistant
WGS 84 / South Pole Lambert Azimuthal Equal Area
WGS 84 / South Pole Stereographic (*)
WGS 84 / UPS (Universal Polar Stereographic) North
WGS 84 / UPS (Universal Polar Stereographic) South
CRS (Coordinate Reference System) and Map Projection
  Data/Images are geographically referenced using CRS.
  CRS is determined by such elements as earth model, coordinate systems, and map projections.
  There are various map projections for polar regions.

## Slide 4: “ Polar Stereographic” Projection
Axes and coordinates in WGS84/Polar Stereographic Projection.
Source
(South Pole)
Projection Plane
Ｘ
Ｙ
< North Pole Stereographic>
(X, Y unit : meters)
North Pole
(minX, minY)
(maxX, maxY)
Notes: この軸設定がポーラステレオ図法のデフォルトと考えて良いか、投影図法ガイドを再度確認する。

## Slide 5: Explore Necessary Considerations
Perform a preliminary check
Preliminary check has been performed to find problems and/or considerations to provide data in polar specific projections in Web Map system.
  Explore considerations to make WMS server and client.
  Explore Free Open Source Software (MapServer) abilities to serve projected images in polar specific projections.
    (e.g. WGS84 “Polar Stereographic” projection, adopted in some JAXA products)

## Slide 6: For WMS access / What is the point?
The questions are;
  How can I figure out the EPSG code for a particular CRS?
  Does my software understand that code and process data appropriately?
A WMS server must support at least one CRS
In WMS v1.3, CRS is expected to be identified by;
  - Certain CRS code system (namely EPSG code)
  - Or, URL of the file containing a definition of the CRS that is compliant with ISO 19111.
Notes: CRS related parameters in WMS request;
  CRS : in a form of “identifier : code number”
  Bounding box : with min (x, y) and max (x, y) value using the axis units and axis order of the specified CRS.

## Slide 7: About the EPSG Code
… This requires certain knowledge of geography domain to manipulate the scripts.
EPSG Code
  - It is the code defined in “EPSG (European Petroleum Survey Group) geodetic dataset”.
  - This dataset adopts SQL scripts to create EPSG codes on-the-fly by setting geographical parameters.
  ( They don’t provide codes in a manner of possible entire list. )

## Slide 8: EPSG Code for CRS with Polar Projection
Ask comments/information to WGISS
  - What is the EPSG code for WGS84/Polar Stereographic Projection?
  - Does the EPSG code assure all the CRS covered?
Some CRS with Polar Projections | EPSG Code
WGS 84 / North Pole Azimuthal Equidistant | ?
WGS 84 / North Pole Lambert Azimuthal Equal Area | ?
WGS 84 / North Pole Stereographic (*) | ?
WGS 84 / South Pole Azimuthal Equidistant | ?
WGS 84 / South Pole Lambert Azimuthal Equal Area | ?
WGS 84 / South Pole Stereographic (*) | ?
WGS 84 / UPS (Universal Polar Stereographic) North | 32661
WGS 84 / UPS (Universal Polar Stereographic) South | 32761

## Slide 9: MapServer Ability regarding Polar Projection
- Basic method to process various projections has been checked.
Explore MapServer ability
i) The software seems to process popular polar projections, if adequate info is passed into its library (namely Proj4).
  set process-parameters manually
  or, use the predefined lists of code and parameters combinations ( however, no predetermined info of “Polar Stereographic” with EPSG code. )
ii) Containing critical spot (such as date-line-meridian) in a scene may cause mal-calculations to convert into/from polar projections.
- Some test cases are examined with MapServer 4.10.
Findings
Action
Notes:   - draw data in the specified projection
  - transformation ability from one projection to others
  (drawing, coordinate caliculation
  - No predetermined info for “Polar Stereographic” for EPSG code.

## Slide 10: MapServer problem on vector map drawing - Example
-> Some polygons disappeared.
Original : Geograhpic Lat-long
Export : Polar Stereographic
(on-the-fly transformation)
Original : Polar Stereographic
Export : Polar Stereographic
(non actual transformation)
Case : North Pole is center of the scene in the “polar stereographic” projection

## Slide 11: Polar Images in other projection from distributed WMS servers
NSIDC (National Snow and Ice Data Center) WMS
JAXA Test WMS
(EPSG:32661, “UPS North” projection)

## Slide 12: Lessons Learned / Considerations for Polar Image Mapping
EPSG Code
  EPSG code is widely adopted to identify CRS. Need advices on how to identify “WGS84/polar stereographic” in EPSG code, if corresponding code exists.
Map Projections
  Mutually agreeable CRS is necessary between data servers and clients. Common “Geographic lat-long” could be a possible answer to exchange images, however, image quality reduces after the client transforms to harmonize different projections.
  Any comment/recommendation is appreciated about in which projection to provide polar images via WMS service.
Notes: Mutually agreeable CRS is necessary between data servers and clients to interact with.
EPSG code may not be always apparent to everyone, especially for some particular projections.
So far, no see of WMS server which provides “polar stereographic” images yet.
which (polar) projection

## Slide 13: Lessons Learned (cont’)
Software limitations
  Map projections may have particular theoretical conditions such as ranges of value and extra parameters.
  Software, especially FOSS, might have limitations in understanding the identified projection, translating coordinates, transforming map projection, and so on.
  Preliminary check would be helpful as regards polar regions to avoid unexpected results and then to explore alternative ways.
Notes: transforming map projection from one to other,