## Slide 1: USGEO Strategic Assessment Group Presented to GEO User Interface Committee Sept 23, 2008
<number>

## Slide 2: USGEO
<number>
USGEO
U. S. Group on Earth Observations
Policy Group
Functional Groups
Architecture and Data
Management Group
Partnership, Outreach, and Communication Group
Strategic
Assessment
Group
Co-chairs: Phil DeCola (OSTP)
Jim Tucker (NASA)
Peter Wilczynski (NOAA)
Membership:
DOE OMB NOAA NASA EPA DOD USDA
DOI DOT USAID USGS Smithsonian DOS NSF
International
Working
Group
New

## Slide 3: Strategic Assessment Group
<number>
Deliver a U.S. Strategic Portfolio
High national priority Earth observation investment recommendations
Existing and future capabilities
Affecting Societal Benefit Areas
Inform decision-makers
  OSTP, OMB, Congress, and Agencies
Improve decisions regarding national investments in Earth observations
Charge

## Slide 4: Strategic Assessment Group
<number>
USGEO Functional Group
  Stood up Sept 07
Two time horizons
  Near term, Dec 2008 Deliverable
    National Earth Observation Portfolio: Strategic Assessment
    Leverage existing publications
      Focus on documented requirements and recommendations
  Longer term, 2009: Develop Process
    Create more analytical framework for evaluating gaps and solutions, determining recommended investment portfolio

## Slide 5: Strategic Assessment Group
<number>
Established SBA Teams in March 2008
  Subject matter experts
SBA Team Leads:
  Agriculture: USDA (Glenn Bethel)
  Climate: CCSP (Jim Tucker, Howard Diamond)
  Disaster: USGS (Bill Leith)
  Ecology: Smithsonian (Len Hirsch)
  Energy: DOE (Graham Pugh)
  Human Health: NIH (Ann Davis)
  Oceans: NOAA (Jessica Geubtner)
  Water: EPA (John Lyon)
  Weather: OFCM (Mike Babcock)

## Slide 6: SBA Team Tasks
<number>
Held SAG Workshop: April 2008
  Team Leads presented overview of each SBA
  Discussed framework and process
Draft SBA Assessments: May-June 2008
  Identified and reviewed relevant publications
  Synthesized existing documents
  Produced initial SBA assesments
Final SBA Assessments: Oct-Dec 2008

## Slide 7: USGEO SAG Tasks and Milestones
<number>
September
October
December
November
SAG Writing Team Completes Draft
Draft Circulated to USGEO
Comments Resolved
External Coordination
Comments Resolved
Publication Process
Draft Circulated to SAG
Comments Resolved
Assessment
Climate Assessment Document Completed (95%)
Other 8 SBAs revise initial drafts to conform to Climate Assessment format
Coordination of SBA Documents
Climate 2-Pager Drafted
2-Pagers for other SBAs Drafted
Coordination of 2-Pagers
Supporting Documents
Sep 25 SAG Meeting

## Slide 8
<number>
Agriculture
Energy
Eco/Biodiv
Climate
Disaster
Health
Ocean
Weather
Water
SBA 2 Pagers to Support Assessment
SBA Assessment
Documents (10-40 pages)
(TRD Updates)
Existing Reports & Studies
Crosscutting nature of all observational parameters
Assessment Document (10-20 pages)
Earth Observations Assessment
USGEO SAG Deliverables
Initial SBA Document Completed in May
Currently Working
Next Up – Climate 2-Pager

## Slide 9: Water SBA Scope
<number>
Fresh water availability
  Fluxes and storage of water in a watershed and its underlying aquifer system; precipitation, streamflow, lake and reservoir storage, evaporation and transpiration, soil moisture, ground water storage, ground water recharge and discharge, and withdrawals for various uses
Fresh water quality
  Concentrations and loads of various significant natural and anthropogenic contaminants, impact on water availability and aquatic habitats in freshwater, estuarine, and marine environments; suspended sediments
Water to support ecosystems
Drought monitoring
Land use and impervious area
Wetlands

## Slide 10: Key Requirements of Water Portfolio
<number>
Water Availability
  Precipitation
  Soil moisture
  Groundwater storage levels (aquifers)
  Surface water levels and extent (lakes, rivers, reservoirs)
  Snow and ice extent and thickness
  Streamflow
Water Quality
  Surface and ground water quality

## Slide 11: Key Requirements of Water Portfolio
<number>
Precipitation
  Importance to SBA: Central component of the global water cycle; primary source of fresh water
  Current status: Good national coverage with manual observing stations and radar networks; precipitation gauges, surface-based radars, LEO passive microwave, LEO & GEO visible and IR cloud observations
  Near term gaps and challenges: More real-time ground-based data for quantification and calibration. Information on the vertical distribution of precipitation. Passive microwave observations need higher spatial and spectral resolution. Gaps in precipitation measurement over complex terrain.
  New capabilities needed: Better algorithms that blend observations from all sources
  Future capabilities: Exploit capability of space-borne radar (currently only a demonstrated capability)
  Crosswalk with other SBAs: Climate, Agriculture, Weather, Disaster

## Slide 12: Key Requirements of Water Portfolio
<number>
Soil Moisture
  Importance to SBA: Regulates partitioning of incoming radiative energy into sensible and latent heat fluxes and partitioning rain water between infiltration and runoff (and subsequently evaporation). Component of water cycle.
  Current status: Generally inadequate. Some local monitoring, but no coordinated network of in situ measurements. Heavy reliance on model-generated estimates.
  Near term gaps and challenges: No standardized procedures for selection of sensor type, measurement sites, sensor depth, sensor calibration and intercomparison, etc.
  New capabilities needed: More work to exploit soil moisture measurements derived from space. Need a supersite program to provide the comprehensive data sets needed for sensor evaluation and calibration, and provide basis for developing soil moisture algorithms for satellite measurements.
  Future capabilities: L-Band radar, radiometer
  Crosswalk with other SBAs: Agriculture, Climate, Weather

## Slide 13: Key Requirements of Water Portfolio
<number>
Groundwater Storage Levels
  Importance to SBA: Major portion of world’s fresh water located underground. Key variable in water cycle, water availability, water quality.
  Current status: Data incomplete, unreliable or non-existent in many areas. Limited groundwater monitoring networks developed as pilot projects.
  Near term gaps and challenges: Data geographically limited. Interpretation of existing data is complex. Data not integrated. No reliable inventory exists.
  New capabilities needed: Most promising measurement concept is precise observation of time-dependent variations in the Earth gravity field using space-based gradiometer systems. Gravity field measurements are sensitive enough to detect minute gravitational changes in underground aquifers. (GRACE: Gravity Recovery And Climate Experiment). Need R&D to develop algorithms and error characteristics. Ground-truthing will be crucial.
  Future capabilities: Laser
  Crosswalk with other SBAs: Climate, Solid Earth

## Slide 14: Key Requirements of Water Portfolio
<number>
Surface water levels and extent (lakes, rivers, reservoirs)
  Importance to SBA: Critical to water cycle, and for engineering designs for dams, reservoirs, river navigation systems, flood protection, irrigation scheduling, international water allocation agreements, ecosystem management and water management plans. Key variable in hydrological models.
  Current status: Surface storage in lakes, wetlands and river channels currently estimated. There is no real capacity to inventory these stores on a regional basis or estimate interseasonal and interannual variability.
  Near term gaps and challenges: Aging infrastructure. Lack of coherent national plan for data collection.
  New capabilities needed: Exploit hydrologic altimetry to provide surface water distribution from existing satellite systems.
  Future capabilities: Radar altimeter, nadir SAR interferometer, microwave radiometer, GPS receiver
  Crosswalk with other SBAs: Climate, Ecosystems, Health, Weather

## Slide 15: Key Requirements of Water Portfolio
<number>
Snow and ice extent and thickness
  Importance to SBA: Fresh water storage variable in water cycle. Prediction of spring and summer water supplies and flood potential.
  Current status: Snow cover is estimated by satellite data (Landsat and AVHRR). Passive microwave can also provide estimates for snow pack in some areas. Snow depth often measured manually.
  Near term gaps and challenges: Derived measurement accuracy varies greatly with snow properties, terrain, and cloud cover. Algorithm assumptions not always valid. Snow drifting affects estimation.
  New capabilities needed: Microwave satellites can provide enhanced observational capabilities for snow water equivalent. Need to ensure research capabilities continued for operational uses. More research on algorithm development.
  Future capabilities: Further development of multispectral sensors that will be able to provide freeze/thaw patterns under different vegetation conditions.
  Crosswalk with other SBAs: Climate, Agriculture, Weather

## Slide 16: Key Requirements of Water Portfolio
<number>
Streamflow
  Importance to SBA: Critical to water cycle, and for engineering designs for dams, reservoirs, river navigation systems, flood protection, irrigation scheduling, international water allocation agreements, ecosystem management and water management plans. Key variable in hydrological models.
  Current status: In situ only cost-effective and reliable option. Current networks are declining on a worldwide basis.
  Near term gaps and challenges: Data archive and exchange limited and fragmented; much data lacks quality control
  New capabilities needed: Investment in national network to monitor streamflow. Satellite altimetry shows promise in estimating river levels. Need extensive research on sensor optimization and algorithm development to determine feasibility
  Future capabilities: Current procedures are labor-intensive. Explore use of radar to automate streamflow monitoring.
  Crosswalk with other SBAs: Climate, Ecosystems, Energy

## Slide 17: Key Requirements of Water Portfolio
<number>
Surface and Ground Water Quality
  Importance to SBA: Critical role in water management.
  Current status: In situ measurements carried out for several decades time-consuming and expensive. Many sampling programs have been scaled back due to budget constraints.
  Near term gaps and challenges: Fresh water contains a myriad of both dissolved and particulate matter that creates unique challenges for remote sensing. Episodic runoff events and algal blooms can occur in a short time period requiring frequent revisit periods. Remote sensing of water quality requires fine spatial resolution.
  New capabilities needed: Optimal freshwater satellite sensors will need high spectral, spatial, and temporal resolution capabilities. Precise, concurrent in situ measurements are a critical component to any remote sensing water quality investigation.
  Future capabilities: Hyperspectral imager, multispectral thermal sensor
  Crosswalk with other SBAs: Health, Agriculture, Ecosystems

## Slide 18: Water SBA Publications
<number>
  USGEO Technical Reference Document: Protect and Monitor Water Resources, Nov 8, 2004
    http://usgeo.gov/documents4b93.html?s=review
  A Strategy for Federal Science and Technology to Support Water Availability and Quality in the United States, CENR, SWAQ, Sept 2007
    http://www.ostp.gov/cs/nstc/documents_reports
  Science and Technology to Support Fresh Water Availability in the United States, CENR, SWAQ, Nov 2004
    http://www.ostp.gov/cs/nstc/documents_reports
  IGOS Cryosphere Theme Report, 2007
    http://www.igospartners.org/cryosphere.htm
  Contributions of Land Remote Sensing for Decisions about Food Security and Human Health, Workshop Report, NRC
    http://books.nap.edu/openbook.php?record_id=11759&page=R1
  Water for a Sustainable and Secure Future, National Council for Science and the Environment 2004
    http://www.ncseonline.org/2004conference/
  Assessing the TMDL Approach to Water Quality Management, NRC, 2001
    http://www.nap.edu/openbook.php?isbn=0309075793
  Estimating Water Use in the United States, NRC, 2002
    http://www.nap.edu/openbook.php?isbn=0309084830

## Slide 19: Water SBA Publications
<number>
  Earth Science Applications Plan, NASA, 2004
    http://science.hq.nasa.gov/strategy/research.html
  Integrating the Nation’s Environmental Monitoring and Research Networks and Programs, Mar 1997
    http://www.epa.gov/cludygxb/Pubs/framewrk.pdf
  Federal Ocean and Coastal Activities Report to the US congress, ICOSRMI
    http://ocean.ceq.gov/2007_Oceans_Report_final.pdf
  United States Detailed National Report on Systematic Observations for Climate, NOAA, 2001
    http://www.eis.noaa.gov/gcos/soc_long.pdf
  The Use of Remote Sensing for Drought Assessment and Monitoring in Southwest Asia, Thenkabail et all, IWMI, 2004
    http://www.iwmidsp.org/iwmi/info/research_docs/drought-paper-draft.rtf
  Canadian Environmental Sustainability Indicators, 2007
    http://www.environmentandresources.gc.ca/default.asp?lang=En&n=2102636F-1
  Water Quality Outlook, GEMS, UNEP, 2007
    http://www.gemswater.org/common/pdfs/water_quality_outlook.pdf
  Global Energy and Water Cycle Experiment, GEWEX, 2006?
    http://www.gewex.org/Feb2007.pdf

## Slide 20: Water SBA Publications
<number>
  Integrated Global Water Cycle Observations Theme, Integrated Global Observing Strategy (IGOS) for the Monitoring of our Environment from Space and from Earth, IGOS-P, 2004
    http://www.igospartners.org/docs/theme_reports/IGOS2.DOC
  Emerging Issues in Water and Infectious Disease, WHO, 2003
    http://www.who.int/water_sanitation_health/emerging/emerging.pdf
  Atlas of International Freshwater Agreements, UNEP, FAO, OSU, 2002
    http://na.unep.net/publications/treaties/1_Front_atlas.pdf
  Earth Observation Handbook, Committee on Earth Observation Satellites, CEOS, 2005
    http://www.eohandbook.com/index.html