## Slide 1: An Introduction to ISO 19130– Imagery Sensor Models for Geopositioning
Briefing to CEOS WGISS on September 24, 2008 in Boulder, Colorado
Liping Di
Center for Spatial Information Science and Systems (CSISS)
George Mason University
6301 Ivy Lane, Suite 620
Greenbelt, MD 20770
ldi@gmu.edu

## Slide 2: Contents
Briefing on ISO 19130 project
  The scope of ISO 19130
  Background and history
  Schedule
  Contents of the latest version of standard
A invitation for CEOS WGISS to contribute

## Slide 3: Introduction
Numerous sensors are collecting data.
  Geopositioning is a fundamental processing step before the data become useful.
Current situation: the diversity of sensor types and the lack of a common sensor model standard. Data from different producers
  contain different parametric information
  lack parameters required to describe the sensor that produces the data
  lack ancillary data necessary for geopositioning and analyzing the data.
The problem
  A separate software package often has to be developed to deal with data from each individual sensor or data producer.
  Unable to archive the plug-in-and-play capability sought by the constellation and sensor web concepts.
The solution: Standard sensor models and geolocation metadata
  Allow the development of generalized geopositioning software.
  Promote interoperability of data between sensors
  facilitate data exchange.

## Slide 4: What is ISO 19130
Identifies the information required to determine the relationship between the position of a remotely sensed pixel in image coordinates and its geoposition.
Defines the metadata to be distributed with the image to enable user determination of geographic position from the observations.
ISO 19130 specifies four ways in which geolocation information may be provided.
  A sensor description with the associated physical and geometric information necessary to rigorously construct a Physical Sensor Model.
    General sensor model components
    Detail models for frame, pushbroom, whiskbroom, and SAR sensors, constructed from those components as examples.
  A True Replacement Model, using functions whose coefficients are based on a Physical Sensor Model.
  A Correspondence Model that provides a functional fitting based on observed relationships between the geopositions of a set of ground control points and their image coordinates.
  A set of Ground Control Points that can be used to develop a Correspondence Model or to refine a Physical Sensor Model or True Replacement Model.

## Slide 5: History
Started in March 2001
  20 experts from 12 countries and 3 international organizations formed the project team
  Chaired by Liping Di of U.S.
Removed from ISO TC 211 program of work in March 2006 due to funding issue.
Reintroduced into ISO TC 211 program of work in February 2008 by U.S. with additional sensor types covered.
  After long preparation work by U.S. INCITS L1 sensor modeling group chaired by Liping Di of GMU and Bill Craig of NGA/SeiCorp
  Progress very rapidly since the reintroduction
Currently an ISO 19130 document is being voted by the members of ISO TC 211 members as ISO Draft Technical Specification (ISO DTS)

## Slide 6: ISO 19130 Project Schedule
1 Aug 08: ISO/TC 211 issues DTS inquiry for 3 month ballot.
31 Oct 08: Ballot closed.
01-03 Dec 08: 19130 Editing Committee Meeting to adjudicate comments (in conjunction with TC 211 Plenary) in Japan
January 2009: Edited DTS to ISO TC 211.
May 2009: DTS published as TS at ISO’s convenience.

## Slide 7: The 19130 DTS Draft Version
The current 19130 DTS draft includes:
  8 clauses
  3 normative annexes
  3 informative annexes
  An introduction clause
The draft currently has 164 pages
Notes: Normative annexes are mandatory and are considered be a part of the standard. One has to follow normative annexes to claim compliance with the standard. Informative annexes give you information. They are there as a service, for information only, but don’t carry any mandate for the user of the standard.

## Slide 8: Geopositioning, Geolocating, and Georeferencing
Geopositioning: determining the ground coordinates of an object from image coordinates.
Geolocating: geopositioning an object using a sensor model
Georeferencing: geopositioning an object using a correspondence model derived from a set of points for which both ground and image coordinates are known.

## Slide 9: The Table of Contents of 19130
Introduction
1 Scope
2 Conformance
3 Normative references
4 Terms and definitions
5 Symbols and abbreviated terms
6 Image geopositioning: overview and common elements
7 Physical Sensor Model
8 True replacement models and correspondence models
Annex A Conformance and testing (normative)
Annex B Geolocation information data dictionary (normative)
Annex C Coordinate systems (normative)
Annex D Frame sensor model metadata profile supporting precise geopositioning (informative)
Annex E Pushbroom / Whiskbroom sensor model metadata profile (informative)
Annex F Synthetic Apeture Radar sensor model metadata profile supporting precise geopositioning (informative)

## Slide 10: Top Level UML Model

## Slide 11: GCP Model

## Slide 12: Overview of Physical Sensor Model

## Slide 13: Position

## Slide 14: Dynamics

## Slide 15: Sensor Parameters

## Slide 16: Sensor System and Operation

## Slide 17: Fitting Function

## Slide 18: True Replacement Model

## Slide 19: Correspondence Model

## Slide 20: How Can CEOS Contribute to 19130
Review current draft DTS
  provide any comments in ISO format
  Nominate an expert to the 19130 Editing Committee as the WGISS representative.
  submit the comments and nomination to ISO TC 211 secretariat through WGISS liaison to ISO TC 211
Due date for the submission- Oct 31, 2008

## Slide 21: What is Next in ISO TC 211
ISO standard on Calibration and Validation of Remote Sensing Data
  We are looking for funding support to start this project.

## Slide 22: IGARSS 2009 DADTC Special Invited Sessions
Cape Town, South Africa July 13-17.
The Data Archiving and Distribution Technical Committee of IEEE GRSS is organizing three invited sessions
  Earth Observation Sensor Web
    Chair: Dr. Liping Di (ldi@gmu.edu, George Mason University)
    Co-Chair: Karen Moe (Karen.Moe@nasa.gov, NASA Goddard Space Flight Center)
  Advances in Data Systems to Support Future Earth Observation Missions
    Chair: Dr. Liping Di (ldi@gmu.edu, George Mason University, USA)
    Co-Chair: Ken McDonald (Kenneth.Mcdonald@noaa.gov, National Oceanic and Atmospheric Administration, USA )
  Progress in Use of Web Services to Enhance Earth Science Research in a Highly Distributed Environment
    Chair: Hampapuram K. Ramapriyan (Rama), NASA Goddard Space Flight Center, Greenbelt, MD, Rama.Ramapriyan@nasa.gov
    Co-Chair: Francis Lindsay, NASA Headquarters, Washington, DC, francis.lindsay-1@nasa.gov
Welcome WGISS members to contribute papers
  Please contact chair or co-chair of the sessions for your contributions.

## Slide 23: 17th International Conference on Geoinformatics
Annual Conference since 1992.
17th conference on August 12-14, 2009 in Fairfax, VA, organized by George Mason University (http://www.geoinformatics2009.org)
Themes include but not limited to
  Earth observation technology, data systems, and applications
  Geospatial Semantic Web, Sensor Web, Grid, and Web Portal
  Geospatial Web Services and service quality, and Workflow-oriented geospatial decision support system,
  Virtual Globes and their application to scientific research and daily life
  Geospatial Interoperability and standards
  Automated object extraction and database updates from imagery
  Integration of RS, GIS and GPS (3S)
  LIDAR technology for DEM generation and 3D modeling
  Geospatial education, such as virtual globes-based virtual education
  Acquisition and processing of Remotely Sensed Data
  Information Extraction from Remotely Sensed Data
  Theories and Algorithms in GIS
  Climate Changes and Global Environment
  Global Earth Observation System of Systems (GEOSS)
Abstract due: Jan. 30th, 2009. Papers will be published as IEEE proceedings and selected papers will be published in peer-reviewed journals
Welcome CEOS WGISS members to organize sessions and contribute papers.
Contact Liping Di (ldi@gmu.edu)