## Slide 1: CDCOL
Advances and lessons learned on Colombia Data Cube

## Slide 2
Colombia has a total area of 2.070.408 km²
55.14% of land area
44.85% of sea surface
  COLOMBIA

## Slide 3
Semestral
2015
Since 2013 Annual
Early warning
Identifying hot spots
Carbon monitoring
- Carbon stocks
- GHG Emissions
National quantification of deforestation
- Forest areas
- Forest change detection
Deforestation rate
Since 2016 Quarterly
C&A Deforestation and Degradation
- Caracterization
- Modelation
  FOREST AND CARBON MONITORING SYSTEM

## Slide 4
Increasing the use of satellite data

## Slide 5
Landsat Median Temporal Composite
2015
Forest area monitoring
Landsat 8 OLI Time series 2015

## Slide 6
COMPUESTO TEMPORAL 2013
COMPUESTO TEMPORAL 2014
COMPONENTES PRINCIPALES MULTITEMPORALES
CHANGE DETECTION - DEFORESTATION (FOREST LOST IN RED).

## Slide 7: CDCol Timeline

## Slide 8
Advances of Colombian Data Cube CDCol
15años
DATOS DE 2000-2015
30metros
RESOLUCIÓN DE PIXEL
27.070imágenes descargadas
LANDSAT 7, 5 Y 8
3sensores
LANDSAT 5/7/8
135.441tiles
LANDSAT 7 – CUBO DE DATOS
16.400 imágenes ingestadas
LANDSAT 7/8/5
3.8TB
DENTRO DEL CUBO - NETCDF
17.2TB
FUERA DEL CUBO
1.4x 1012
PIXELES
Downloading and ingestión of all country (Landsat 5-7-8)
Applicacions: temporal composed imagery, change detection PCA, WOFS, land cover classification
Workshops and capacity building
Interface WEB: user management, algorithms bank

## Slide 9: Results
15años
DATOS DE 2000-2015
30metros
RESOLUCIÓN DE PIXEL
342 escenas
LANDSAT 7/8
2h
PROCESAMIENTO

## Slide 10: Results
15años
DATOS DE 2000-2015
30metros
RESOLUCIÓN DE PIXEL
466 imágenes
LANDSAT 7/8
2min x año
PROCESAMIENTO
Bosque
Otras Coberturas

## Slide 11: Results
15años
DATOS DE 2000-2015
30metros
RESOLUCIÓN DE PIXEL
45 imágenes
LANDSAT 7
20min x periodo
PROCESAMIENTO

## Slide 12: CDCol Goals
Data ownership
Extensibility
Lineage
Replicability
Complexity abstraction
Ease of use
Parallelization
Standardization
Reusability

## Slide 13: Related Works

## Slide 14: Solution Strategy (on v2 July 2016)
Bank of algorithms and results
Web UI
Parallelization strategy
Training Workshop
Roles

## Slide 15: CDCol User Roles
System Administrator
Data Administrator
Developer
Analyst
Bank of algorithms and results
Web UI
Parallelization strategy
Bulk Ingestion
Training Workshop
Roles

## Slide 16: CDCol User Roles
Data administrator
Developer
Analyst
System administrator
Portal Web CDCOL
Bank of algorithms and results
Web UI
Parallelization strategy
Training Workshop
Roles

## Slide 17
Administrador de Datos
Desarrollador
Analista
Administrador
del Sistema
Portal Web CDCOL

## Slide 18: Arquitectura CDCol Despliegue

## Slide 19
ANALIST – ALGORITHMS EXECUTION

## Slide 20
DEVELOPER- ALGORITHMS PUBLISHING

## Slide 21
DATA ADMIN– COLEECTIONS MANAGEMENT

## Slide 22
SYSTEM ADMIN– USERS MANAGEMENT

## Slide 23: Algorithms Life Cycle
Bank of algorithms and results
Web UI
Parallelization strategy
Training Workshop
Roles

## Slide 24: Development
Complexity Abstraction
Independent of datacube-core
Automatic parallelization
Python well known libraries
Numpy
xArray
Bank of algorithms and results
Web UI
Parallelization strategy
Training Workshop
Roles

## Slide 25: Execution
Bank of algorithms and results
Web UI
Parallelization strategy
Training Workshop
Roles

## Slide 26: CDCol Web UI
Empowers users to work on a large set of satellite images from any device
Reduces learning curve
Authentication and roles management
Bank of algorithms and results
Web UI
Parallelization strategy
Training Workshop
Roles

## Slide 27: CDCol Demo
Bank of algorithms and results
Web UI
Parallelization strategy
Training Workshop
Roles

## Slide 28: Parallelization Strategy
Automatic
By Tile
Generic Task
Celery
Bank of algorithms and results
Web UI
Parallelization strategy
Training Workshop
Roles

## Slide 29: CDCol Components

## Slide 30: Lesson Learned and future work
Is important to define a governance for administration and operation of the Data Cube
Data is growing exponentially, how can our technological infrastructure can grow up?
Training and research should be a continuous activities
Horizontal Scaling
Algorithm dependent parallelization schemes
Workflows management
New sensors
New algorithms
Cloud enabled-CDCol

## Slide 31
Brian Killough from NASA
Alex Held and AGDC researchers team from CSIRO
Alfredo Delos Santos and Kayla Fox from AMA team
Environmental Ministry of Colombiafor financial support.
Acknowledgements

## Slide 32
Thanks for your attention…
Any question?
María Teresa Becerra mtbecerra@ideam.gov-co
Edersson Cabrera ecabreram@ideam.gov.co
Gustavo Galindo ggalindo@ideam.gov.co
Pilar Lozano-Rivera plozano@ideam.gov.co
Harold Castro hcastro@uniandes.edu.co