## Slide 1: CWIC Connectors to Data Providers in China CWIC Development Team 2018

## Slide 2: Two data providers in China
Two data providers
  ChinaGEOSS
  China NRSCC

## Slide 3: ChinaGEOSS – brief
ChinaGEOSS is a national satellite remote sensing data facility of National Remote Sensing Center of China (NRSCC), under the Ministry of Science and Technology, China
  Intend to provide discovery of and access to all satellite remote sensing data in the governmental data centers of China.
The ChinaGEOSS is broker, using system of system architecture
Four interfaces: data query, data, metadata, and data planning
Toolkit to connect to the data/metadata
More than 35 million of metadata/data records.
About100 high quality datasets: Data are harvested and stored at their central storage.
  Those data sets can be shared with international users immediately
  A mirror site of ChinaGEOSS is considered to be established at Chinese University of Hong Kong to facilitate the international access.
New satellite data are joining the network.
Its GeoPortal: metadata and data
Metadata are open access. Not all available to GeoPortal.
Standards: not sure (claim to support ISO metadata and OGC standards).

## Slide 4: ChinaGEO – Satellite/sensors (1/3)
FY3A (FY means wind and cloud. It is a meteorological satellite)
  MERSI
  VIRR
FY3B
  MERSI
  VIRR
FY3C
  MERSI
CBERS-01
  CCD
CBERS-02
  CCD

## Slide 5: ChinaGEO – Satellite/sensors (2/3)
CBERS-02B
  CCD
GF1 (GF means high resolution)
  WFV1
  WFV2
  WFV3
  WFV4
HJ1A (HJ means environment)
  CCD1
  CCD2

## Slide 6: ChinaGEO – Satellite/sensors (3/3)
HJ1B
  CCD1
  CCD2
GLASS
  LAI
  ABD
  LST
  FAPAR

## Slide 7: Snapshot of data status by the end of 2017
Granules at the end of 2017
[ 10 satellites 1127838 items]
FY3A(99305)
FY3B(133883)
FY3C(34572)
CBERS-01(10)
CBERS-02(2603)
CBERS-02B(69)
GF1(725)
HJ1A(421)
HJ1B(510)
GLASS(855740)

## Slide 8: CWIC ChinaGEO Connector Development Status(1)
Meeting with the chief engineer of NRSCC and her team at GEO Plenary gets initial agreement for ChinaGEOSS to participate in CWIC
Initiated first bi-lateral teleconference of technical teams on 11/14/2017
  Technical exchanges on CWIC connection have been going on since then
NRSCC has requested to sign a MOU between NRSCC and CEOS for ChinaGEOSS to join CWIC
  Draft MOU has been sent to NRSCC and discussion on MOU is going
  No problem with the MOU content but questioning who should sign the MOU on CEOS side – waiting for NRSCC’s official request.
Notes: There are three options for access their data (Option 1 is accessible with planned harvest, Option 2 is for human user, Option 3 is still in development and its stability needs to be tested when the service back after March 20.) Option 1.The global metadata harvesting mode：As we mentioned above, the web service interface is used for the metadata sharing mechanism with GEODAB. They can harvest global metadata in batch processing and republish the metadata catalog to the GEO portal. Option 2.The human-computer interaction mode: This mode is used on the China GEOSS portal (http://www.chinageoss.org/en/query.html). International users can select satellite, sensor and spatial-temporal range conditions to query the metadata result. Option 3.The API query interface mode. It consists of query, getalldescription and closequery three features. Firstly, the user should pass a query condition of an XML string and obtain the ID (QueryID) of the query result. If the query fails, the ID is null. Secondly, the user pass the QueryID and a maximum number (N) of returns to getalldescription. They can get the N query results expressed as an XML string in a sequential manner. Thirdly, the query is ended when the number of query results returned is less than N.

## Slide 9: CWIC ChinaGEO Connector Development Status(2)
Three access options
  Option 1.The global metadata harvesting mode
  Option 2.The human-computer interaction mode
    China GEOSS portal (http://www.chinageoss.org/en/query.html)
  Option 3.The API query interface mode
    CWIC will test this mode first
    If this one does not work, option 1 will be implemented

## Slide 10: CWIC ChinaGEO Connector Development Status (2)
Initial access to ChinaGEO dataset through protected interface (API)
  No dataset support
  No support on spatial/temporal constraints
  No total matches reported
  No support on retrieving metadata for specific granule
  Service stability needs to be tested and verified
    ChinaGEOSS intends to set up a mirror site at Chinese University of Hong Kong to improve the stability and accesibility

## Slide 11: CWIC ChinaGEO Connector Development Status (3)
ChinaGEO GeoPortal supports searches
  http://www.chinageoss.org/en/query.html
The API service by ChinaGEO would support similar capabilities for directly relayed search from CWIC Connector

## Slide 12: China NRSCC - brief
Global Change Data Processing and Analysis Center (est. 1/10/2011)
  Funded by China NRSCC to produce global annual land ecological products freely availabe to worldwide users
Multiple Data source, Multiple algorithms, long-term data product
Currently has 12 products (1981-2016)

## Slide 13: China NRSCC - products
12 products
Global products
Product since 1981

## Slide 14: China NRSCC – API and current snapshot
More than 30727 granules are registered in the NRSCC CSW catalog (last visited 3/18/2018)
Four datasets are registered
  DSR
  ET
  PAR
  FVC
API
  CSW interface
  Support both Dublin Core and ISO Profile
  ISO profile is complete with metadata

## Slide 15: CWIC China NRSCC Connector Development Status
CWIC Connector NRSCC implementation
  Completed in March 2018
  Deployed into DEV server of CWIC for integration testing
Six datasets registered in IDN
Issue
  Integration testing revealed that datasetId mismatching
short-name | concept-id
NRSCC_GLASS_ET | C1458427035-SCIOPS
NRSCC_GLASS_FVC | C1458427261-SCIOPS
NRSCC_GLASS_Albedo | C1451572871-SCIOPS
NRSCC_GLASS_DSR | C1458380697-SCIOPS
NRSCC_GLASS_LAI | C1458427894-SCIOPS
NRSCC_GLASS_PAR | C1458428050-SCIOPS

## Slide 16: Back
End of the main slide
After this – back slides

## Slide 17: Reference – FY-3
FY-3 (FengYun-3) 2nd Generation Polar Orbiting Meteorological Satellite Series
Spacecraft | Launch (projected launch) | LTDN (Local Time on Descending Node) | Mission Service Type
FY-3A | May 27, 2008 | 10:00 hours | R&D (Experimental)
FY-3B | Nov. 04, 2010 | 13:30 hours | R&D (Experimental)
FY-3C | Sept. 23, 2013 | 10:00 hours | Operational mission with MWHS-II (upgrade) and GNOS (new) instruments

## Slide 18: Reference – FY-3 - Instruments
Instruments
  MERCI (Medium Resolution Spectral Imager) (I, II)
  VIRR (Visible and Infrared Radiometer)
Instrument name | No of bands /channels | Spectral range | IFOV/line (pixels/scan line) | Spatial resolution at nadir (km) | Swath width (km)
VIRR (Visible and Infrared Radiometer) | 10 | 0.43-12.5 µm | 2048 | 1.1 | 2800
MERSI (Medium Resolution Spectral Imager) | 20 | 0.41-12.5 µm | 2048/8192 | 1.1/0.250 | 2800

## Slide 19: Reference – FY-3 - MERCI
18 Bands
Channel No | Center wavelength (µm) | Bandwidth (µm) | Spatial resolution (m) | Noise-equivalent reflectance (%), ΔT at 300 K | Dynamic range (max reflec., max T) | Primary use of data
3 | 0.650 | 0.05 | 250 | 0.4 | 100% | Land/cloud/ aerosols boundaries
4 | 0.865 | 0.05 | 250 | 0.45 | 100% | 
1 | 0.470 | 0.05 | 250 | 0.45 | 100% | Land/cloud/ aerosols properties
2 | 0.550 | 0.05 | 250 | 0.4 | 100% | 
5 | 11.50 | 2.50 | 250 | 0.54 K | 330 k | 
19 | 1.640 | 0.05 | 1000 | 0.08 | 90% | 
20 | 2.130 | 0.05 | 1000 | 0.07 | 90% | 
6 | 0.412 | 0.02 | 1000 | 0.1 | 80% | Ocean Color/ Phytoplankton/ Biogeochemistry
7 | 0.443 | 0.02 | 1000 | 0.1 | 80% | 
8 | 0.490 | 0.02 | 1000 | 0.05 | 80% | 
9 | 0.520 | 0.02 | 1000 | 0.05 | 80% | 
10 | 0.565 | 0.02 | 1000 | 0.05 | 80% | 
11 | 0.650 | 0.02 | 1000 | 0.05 | 80% | 
12 | 0.685 | 0.02 | 1000 | 0.05 | 80% | 
13 | 0.765 | 0.02 | 1000 | 0.05 | 80% | 
14 | 0.865 | 0.02 | 1000 | 0.05 | 80% | 
15 | 0.905 | 0.02 | 1000 | 0.10 | 90% | Atmospheric water vapor
16 | 0.940 | 0.02 | 1000 | 0.10 | 90% | 
17 | 0.980 | 0.02 | 1000 | 0.10 | 90% | 
18 | 1.030 | 0.02 | 1000 | 0.10 | 90% | 

## Slide 20: Reference – FY-3 - VIRR
10 Bands
Spatial resolution: 1.1 km on a swath of 2800 km (FOV=±55.4º)
Channel | Spectral range (µm) | Noise Equivalent Reflectance (%) or NEΔT (at 300 K) | Dynamic range (% or K)
1 | 0.58-0.68 | 0.1% | 0-100%
2 | 0.84-0.89 | 0.1% | 0-100%
3 | 3.55-3.95 | 0.3 K | 180-350 K
4 | 10.3-11.3 | 0.2 K | 180-330 K
5 | 11.5-12.5 | 0.2 K | 180-330 K
6 | 1.58-1.64 | 0.15% | 0-90%
7 | 0.43-0.48 | 0.05% | 0-50%
8 | 0.48-0.53 | 0.05% | 0-50%
9 | 0.53-0.58 | 0.05% | 0-50%
10 | 1.325-1.395 | 0.19% | 0-90%

## Slide 21: Reference - CBERS
CBERS-1 (China-Brazil Earth Resources Satellite) - 1st Generation Satellite Series
Spacecraft | Launch Date | Comment
CBERS-1 (ZY-1 FM1) | Oct. 14, 1999 | The spacecraft operated until Aug. 2003
CBERS-2 ZY-1 FM2) | Oct. 21, 2003 | The spacecraft was retired in late 2007 when imagery from CBERS-2B was available
CBERS-2B (ZY-1 FM2B) | Sept. 19, 2007 | The spacecraft is operational in 2010 — but was retired on May 10, 2010 due to a power failure.

## Slide 22: Reference – CBERS - CCD
HRCC (High Resolution CCD Camera)
Spatial resolution: 20 m
Parameter | Band | Wavelength | Radiance (W/m2 sr) |  | SNR (dB) | 
 |  |  | Maximum | Minimum | Maximum | Minimum
MS band | B1 B2 B3 B4 | 0.42-0.52 µm 0.52-0.59 µm 0.63-0.69 µm 0.77-0.89 µm | 28.7 30.1 25.9 35.6 | 4.6 3.7 2.4 2.7 | 48 50 48 52 | 32 31 26 29
PAN band | B5 | 0.51-0.73 µm | 55.6 | 9.0 | 53 | 37

## Slide 23: Reference – GF-1
GF-1 (Gaofen-1) High-resolution Imaging Satellite / CHEOS series of China
  Launch: The GF-1 spacecraft was launched on April 26, 2013 on a CZ-2D (Long March -2D) vehicle from the JSLC (Jiuquan Satellite Launch Center) in northwest China.
  Orbit: Sun-synchronous orbit, altitude 645 km, inclination = 98º, LTDN (Local Time on Descending Node) = 10:30 hours, revisit frequency of ≤4 days.

## Slide 24: Reference –GF-1 - WFV
Instruments
  WFI (Wide Field Imager)
Imager type | Pushbroom with TDI capability
Spectral bands | B1/blue: 0.45-0.52 µm B2/green: 0.52-0.59 µm B3/red: 0.63-0.69 µm B4/NIR: 0.77-0.89 µm
GSD (Ground Sample Distance) at nadir | 16 m
Swath width at nadir | 830 km
Detector type | CCD array

## Slide 25: Reference – HJ-1
HJ-1 (Huan Jing-1: Environmental Protection & Disaster Monitoring Constellation)
  Launch: A Long March-2C (CZ-2C) launch of two spacecraft, HJ-1A and HJ-1B, took place on Sept. 5, 2008 (UTC). The launch site was TSLC (Taiyuan Satellite Launch Center), located in the northwest part of the Shanxi Province, China.
  Orbit: Sun-synchronous circular orbit, altitude = 650 km, inclination = 97.95º, LTDN (Local Time of Descending Node) equator crossing at 10:45 hours.
  HJ-1A and HJ-1B are in a coplanar orbit with a phasing of 180º.

## Slide 26: Reference – HJ-1 - CCD
WVC (WIDE View CCD Cameras)
Satellite | Instrument | Bands | Spectral range | Resolution | Swath width | Repeat cycle
HJ-1A | WVC | 4 | 0.43-0.90 µm | 30 m | 700 km | 4 days
HJ-1B | WVC | 4 | 0.43-0.90 µm | 30 m | 720 km | 4 days
Instrument | CCD detector (pushbroom type)
Spectral bands (4), µm | B1=0.43-0.52, B2=0.52-0.60, B3=0.63-0.69, B4=0.76-0.90
Spatial resolution | 30 m
Swath width | 360 km x 2 = 720 km (double swath observation provided by parallel camera mounts)
Aspect angle | 31º
SNR (Signal-to-Noise Ratio) | ≥ 48 dB
Data quantization | 8 bit
Design life | ≥ 3 years
Notes: Each satellite has two WVC

## Slide 27: Reference - GLASS
Global LAnd Surface Satellite (GLASS) product
  Leaf Area Index (LAI),
  shortwave broadband albedo (ABD)
  Land Surface Temperature (LST)
  Fraction of Absorbed Photosynthetically Active Radiation(FAPAR).
References
  10.3390/rs5052436
  10.1080/17538947.2013.805262