## Slide 1: Ensuring ARD Interoperability
Medhavy Thankappan

## Slide 2: Project overview
Outcomes:
ARD correction parameter sensitivity: Determine the key set of common parameters between correction approaches to minimise artefacts in reflectance and downstream processes
Temporal stability: comparison of measurements from corrections through time (GA NBAR method vs LEDAPS/LaSRC )
Field validation: comparison with in situ measurements (historical and current)

## Slide 3: Project timeframe
Q3-Q4 2018
Outputs:
Summary report + peer reviewed article
Intercomparison tools for characterising multisource ARD

## Slide 4: Approach
Use NBAR / NBART / with WoFS as control
Quantify impact on reflectance
  Relative to control:
    per scene differencing
    target feature comparison (invariant within scene stack)
Quantify impact on downstream product
  Water (WoFS) classification results

## Slide 6: ARD correction parameters
Compare cross matrix of parameters, specifically look:
  MODIS BRDF
  Average BRDF
  Aerosol - actual, [ fixed values ]
  Water vapour - actual [ fixed values ]
  Nadir solar angle
Landsat Surface Reflectance processor as a surrogate for multiple sensors

## Slide 7: Test sites
Low vegetation cover areas (low BRDF): Lake Lefroy path/row 109/082 and adjacent paths 108/082 and 110/082
Medium vegetation cover: Wagga Wagga area, path/row 92/84 and adjacent path (91/84 and 93/84). The region has agricultural areas (MDB). Adjacent areas could be used to validate BRDF correction.
High BRDF areas: East coast forested area.Path/row 092/086) with adjacent path (091/086) and (093/086).
Supplemental area: North Queensland path/row 095/074 and its adjacent paths 094/074 and 096/074.
Notes: Tools will be developed to enable execution of

## Slide 8: Test sites

## Slide 9: Sensitivity analysis
Solar angle: BRDF normalized to 25, 45 (control) and 70 degree.
Aerosol change: aerosol optical depth 0.05, 0.15, 0.25. 0.05 (control is best observed)
Water vapour: 0.5, 2, 3.5 (control is NCEP global modelled/observed)
BRDF: temporal average (control is MCD43 modelled/observed)

## Slide 10: Temporal stability
GA NBAR/NBAR T and LEDAPS/LaSRC
Report including statistical summaries:
  Invariant targets within scene
  Points coincident with field spectra
  Polygonal statistics over homogenous targets
  Tools for expanded intercomparison studies eg. GA NBAR vs sen2cor

## Slide 11: Comparison tool - agricultural site

## Slide 12: Comparison tool - NE facing hill slope

## Slide 13: Comparison tool - grassland site

## Slide 14: Field validation

## Slide 15: Key elements of validation
Validation protocols (QA4EO, CEOS-LPV etc)
Field sites for product validation at national scale
Effective sampling design for validation across product classes
Nationally coordinated campaigns for field data collection
Supported by UAVs and automated field instrumentation
Field data collection management at national level
Automated systems to cross validate EO and field based data

## Slide 16: Ensuring ARD Interopability