## Slide 1
Federated Earth Observation (FedEO)
Yves Coene (Spacebel), Andrea Della Vecchia (Randstad),
Damiano Guerrucci (ESA), Mirko Albani (ESA)
CEOS WGISS#51
20 April 2021

## Slide 2: Outline
FedEO current metrics and DIF-10 export status
STAC interface evolution since WGISS-50
FedEO evolution activities
  EOVOC status update

## Slide 3: FedEO: Federated Earth Observation Gateway System
FedEO = Federated Earth Observation missions access
The FedEO system provides a unique entry point to a growing number of scientific catalogues and services.

## Slide 4: WGISS Connected Data Assets

## Slide 5: FedEO Metadata Mediator
Automatic Procedure – Available on FedEO reference environment, on Operational environment at ESA since Oct 2019
Partner Metadata repository
Metadata Import
IDN
repository
Metadata Export
DIF-10 Encoding
IDN
Complementary
Information gcmd keyword
DIF-10 Validator
(HERE)
DIF-10 Validation
Metadata Preparation
Metadata Preparation
IDN guideline for Information Content completeness and consistency (HERE)
Harvester tool
FedEO Collection Catalogue
FedEO Gateway
ISO to DIF-10
Metadata Mediator
ESA Thesauri Service

## Slide 6: DIF-10 Metadata Export
Many harvested collections have been ingested into IDN in past period, e.g.
ESA 136, DLR 53, VITO 45
See:
https://cmr.earthdata.nasa.gov/search/collections.umm_json?provider_id=ESA&data_center=DE/DLR&pretty=true
https://cmr.earthdata.nasa.gov/search/collections.umm_json?provider_id=ESA&data_center=VITO&pretty=true
https://cmr.earthdata.nasa.gov/search/collections.umm_json?provider_id=ESA&data_center=ESA/ESRIN&pretty=true
DIF-10 collections are ready for being ingested into IDN, from
https://fedeo.esa.int/asset/index.html
https://geo.spacebel.be/opensearch/asset/index.html
Notes: https://cmr.earthdata.nasa.gov/search/collections.umm_json?provider_id=ESA&data_center=DE/DLR&pretty=true
https://cmr.earthdata.nasa.gov/search/collections.umm_json?provider_id=ESA&data_center=VITO&pretty=true
https://cmr.earthdata.nasa.gov/search/collections.umm_json?provider_id=ESA&data_center=ESA/ESRIN&pretty=true
https://access.earthdata.nasa.gov/holdings

## Slide 7: Metrics evolution
FedEO: 73 million to 94 million granules (+28%) since WGISS-50 (Sept. 2020)
ESA: 147 to 162 collections (+10%), 16 to 23 million granules (+39%).

## Slide 8: Ongoing integration activities
ESA CCI integration in FedEO updated
  2.58 million granules available via two-step search
  DIF-10 generation and IDN insertion to be completed after ISO metadata update planned by CEDA/STFC to migrate from Gemini 2.1 to 2.3 and add platform/instrument information to metadata records currently missing this info (expected July 2021).

## Slide 9: Ongoing integration activities
JAXA G-Portal integration
  1110 additional collections with complete and valid DIF10 files.
  Next steps: integration of JAXA granule search in FedEO when ready at G-Portal side.

## Slide 10: STAC Interface evolution
Main improvements since September 2020 (WGISS-50)
  drill-down in STAC catalogues via instruments and earth topics (as per SKOS concept hierarchies) added to identify collections.
  drill-down per year/month/day with number of products indicated
  migration to STAC 1.0.0-rc.2

## Slide 11: STAC implementation improvements
Drill down according to SKOS concept hierarchy (e.g. instruments) to find collection
  Only includes branches leading to (STAC) collections…

## Slide 12: STAC implementation improvements
Drill-down per year/month/day with number of products indicated
  Only includes subcatalogs (year, month, day) leading to granules (for ESA collections only).

## Slide 13: STAC implementation improvements
Collection level assets now available
  Access to alternative collection metadata formats
  Access to external search client application, e.g. IDN or FedEO search client (future work)
Notes: https://stacindex.org/catalogs/fedeo-clearinghouse#/?t=catalogs

## Slide 14: STAC Progress since WGISS-50
Some issues identified previously are now resolved/ improved/completed.

## Slide 15: STAC implementation
Future work
  Check ongoing work on STAC-BROWSER related to “external paging” once available.

## Slide 16: Outline
FedEO current metrics and DIF-10 export status
STAC interface evolution since WGISS-50
FedEO evolution activities (EOVOC)

## Slide 17: FedEO Evolution – EOVOC Status Update
Status update of FedEO evolution project “EOVOC” presented at CEOS WGISS#50 (22 September 2020)

## Slide 18: Context
Extends previous CEOS WGISS work:
  CEOS OpenSearch Best Practice 1.2
    « search-friendly catalog » - Annex C (schema.org)...

## Slide 19: EOVOC Engineering Report (ER)
First EOVOC project review held February 2021
First version of proposed Data Model Engineering Report available for comments and feedback: heavily based on https://github.com/ESIPFed/science-on-schema.org

## Slide 20: EOVOC Engineering Report – Table of content
Covers 3 resource types:
  Collections
  Services/applications
  Granules
§4-6 assume schema.org as-is.
Similar TOC as OGC specs (derived from UMM TOC).
Traceability planned to OGC 17-084r1, OGC 19-020 and OGC 17-003r2.

## Slide 21: Engineering Report – Appendix E
Preliminary encoding examples (JSON-LD –> RDF)
  In appendix E of Engineering Report
  Loaded RDF/XML in SPARQL endpoint (Fuseki) and accessible at https://eovoc.spacebel.be/lodview (open-source Linked Data viewer)

## Slide 22: Example (served via SPARQL)

## Slide 23: Engineering Report – Appendix D
Addresses 3 ways to cover more granule metadata properties than currently available in schema.org.
Only method 3 requires extending the schema.org vocabulary with additional classes and properties.

## Slide 24: Granule metadata
Method 1: Exploits “additionalProperty” relation to include OGC17-003r2 properties.

## Slide 25: Granule metadata
Method 2: Use multiple types and mix properties.

## Slide 26: Granule metadata
Method 3:
  Extend (https://schema.org/docs/extension.html) schema.org when existing vocabulary is insufficient:
      Classes
      Properties
  Work done:
      Verify how to use the schema.org toolset and how to include “changes”.
      Syntax conversion of OGC OWL model to schema.org format.
      Deployment with schema.org toolset to validate approach.
Notes: The schema.org toolset can be reused to document extensions to schema.org (for EO) using the similar Web pages as the original schema.org web site.

## Slide 27: Granule metadata
Method 3: Try to fit OGC 17-003r2 classes with schema.org class hierarchy (very preliminary)

## Slide 28: Conclusion
Current EOVOC results:
  Draft Engineering Report (work in progress) to collect feedback, comments, and prototype implementation feedback.
  https://github.com/eovoc/eo-on-schema.org (private)
  https://eovoc.spacebel.be/lodview (public) hosting examples.
Next steps:
  Taking into account CEOS WGISS SLT partners’ feedback
  Completion and refinement of models
  Parallel implementation by adding RDF HTML and JSON-LD response types to FedEO catalogue interfaces.

## Slide 29: Conclusion
Proposed encodings to be used in a prototype implementation

## Slide 30: Conclusion
Proposed encodings to be used in a prototype implementation
Example clients:
  Linked Data: “LODView”
  SPARQL: Jupyter notebook, “LODView”