## Slide 1: WGISS-59
Matt Paget, CSIRO
Agenda Item 2.2
WGISS-59
24-28 March, 2025
Bangkok, Thailand
CSIRO agency report

## Slide 2: Overview
EASI 2.0 🡪 CSIRO cloud-hosted data analytics platform
SAR backscatter 🡪 ARD product workflow
Land and coastal mapping 🡪 Regional EO applications
AVHRR 🡪 CEOS historical data collection
Himawari 🡪 New product workflow
Hyperspectral and ODC 1.9 🡪 New product & analytics capability
EASI data catalogue services 🡪 CEOS interoperability

## Slide 3: EASI 2.0
AWS EKS Auto for much reduced maintenance overhead
  CEOS Analytics Lab can be updated in the next week or two
Karpenter for improved node/pod spin-up and scaling efficiency (> 2x)
  More GPU options
ARM64 image builds for ODC environment and custom processing
Anticipate reduction in AWS costs
Towards: multi-AWS-region processing

## Slide 4: SAR backscatter
Processing workflow built in EASI
  ASF source, SNAP-10, scalable
Intercomparison exercise with GA
Conversations with JPL NISAR & Opera teams
Used by the CEOS biodiversity / ecosystem extent study team
Applications in Aust and Asia
  Flooding, land mapping
Intercomparison of S1 backscatter for study sites in Australia. S1 backscatter produced with multiple methods: SNAP, pyroSAR, Gamma, Opera and EASI. Analysis and results to be published soon. Compliments of Geoscience Australia.

## Slide 5: NovaSAR for cyclone Alfred
NovaSAR-1 flood analysis for northern NSW, March 2024. HH NovaSAR image captured on 10 March 2025. "Dark" backscatter represents open water and specular (mirror-like) reflections. ”Bright" areas occur where water is present beneath vegetation - the signal has a strong double bounce off the water surface and the vertical trunks. This scattering mechanism would not occur in the Sentinel-1 data because it is VV/VH (no HH polarisation).

## Slide 6: Land and coastal mapping
Land Cover Classification System (LCCS) built in EASI
  Decision tree framework for separating classes
  Compatible with “Living Wales” and DEA Land Cover
  Training tools and notebooks
  Global datasets provide a baseline, then specialize per application / area
Land and coastal mapping projects in SE Asia (with in-country partners)
  PNG, Vietnam, Bangladesh, (more expected soon)
  Aquawatch – inland and offshore water quality
Aquawatch international pilot sites (Asia), Aust)
https://livingearthhub.org/

## Slide 7: Australian AVHRR
Archive uplift L0 🡪 L1C (WGISS-56)
  Collating and publishing information
  Scene footprints
Atmospheric correction (WGISS-57, 58)
  Re-implemented our original at.corr. method
  Trialing RTTOV
  Updated and consistent ancillary datasets
  Comparison of methods exercise?
Current online archive (Australian cut-outs), https://explorer.csiro.easi-eo.solutions/products/avhrr_toa
Living Planet Symposium 2025 🡪 ”Atmospheric Correction of the 30+ Year Australian AVHRR Archive using the RTTOV radiative transfer model”, Andrew Prata et al
Example AVHRR BRDF-corrected mosaic

## Slide 8: Himawari
Example Himawari image full-disk (1 Dec 2022), processed to LST
Geostationary over Pacific and east Asia (JMA, JAXA)
  Source: AWS opendata (NOAA)
Developing a TOA workflow
  Unpack (bz2) and combine (strips) using satpy
  Retain digital numbers to apply custom/future calibrations
  Write to COG / Zarr for efficient dense time-series data loading
Applications
  At.corr. workflows: volcanic ash transport
  Land surface: cloud masking with other sensors

## Slide 9: Hyperspectral and ODC 1.9
ODC 1.9 supports custom data loading and multiple dimensions
  Improved flexibility and efficiently for search and load
Hyperspectral sensors
  EnMAP, EMIT, Prisma, etc
Wavelength as a dimension
  Select and slice bands (like time/space)
  Convolve bands

## Slide 10: EASI data catalogue services
Work in progress: https://wps.dev.easi-eo.solutions/
Work in progress: https://catalogue.dev.easi-eo.solutions/
Rationale
  Improved integration, discovery and use of data for our researchers
  Align with CEOS interoperability
Expected features
  Data product workflows: user ordering, status transparency, BYO data
  Data product information
  STAC endpoint
  Web processing services

## Slide 11: Thank you
Matt Paget – matt.paget@csiro.au
Robert Woodcock - robert.woodcock@csiro.au Former CEOS WGISS Chair
… plus a cast of many ☺